UIT - Secteur de la normalisation des télécommunications

ITU - Telecommunication Standardization Sector

UIT - Sector de Normalización de las Telecomunicaciones

Study Period 2001-2004

9	  D.14

Geneva, 6-9 March 2001

E

Question: 	21/9

SOURCE*: 	Japan

TITLE:			Proposal of an objective picture quality measurement method with a reduced 				reference using invisible marker signals

___________________

# Summary

Automatic assessment of picture quality is an important issue. VQEG studies were conducted on picture quality assessment using reference pictures (FR). However, studies for highly accurate assessment of picture quality without reference pictures (RRNR) have not yet been conducted. This report proposes an invisible marker method. According to the experimental results, this method can estimate the PSNR of the received TV signal with the estimation error of about 1dB in the absence of the original, and it is useful even in a transmission chain which contains a tandem connection of codecs. This study is to be reflected in VQEG activities.

# 1. Introduction

In recent years, the development of technologies that provide support to operation and monitoring of television transmission systems and perform automatic monitoring in place of humans, has been an important issue. Especially awaited are technologies which automate picture quality assessment. Some of the methods proposed for this automatic assessment of picture quality utilize the original picture as a reference.

However, methods for absolute picture quality assessment without using the original picture, which are important in automatic monitoring of a transmission chain, have not yet been established.

In this report, therefore, the authors propose an absolute picture quality assessment method that does not require reference pictures, which is based on the insertion and the detection of invisible marker signals.

# 2. General configuration of the scheme

- On the transmission side, an invisible marker signal is embedded by the spread spectrum method into the picture to be transmitted.
The power of this signal is extremely small and it is spread over the whole picture, so that it is negligible compared to the degradation in picture quality due to subsequent transmission processing. (PSNR=50dB)

- Processing in a TV transmission chain. This includes elements such as:

  - Transmission using compression codecs.

  - Tandem connection of codecs.

  - Format conversion such as 1080I ((720P.

  - Up/down conversion between HDTV and SDTV.

  - Standard conversion that includes frame rate conversion.

Since the marker signal embedded at the entrance of the chain is extremely small as mentioned above,

it is negligible compared to the degradation in picture quality due to processing in the transmission chain.

- The marker signal is extracted from the received picture (i.e. the decoded picture when a codec is used).

- The degradation of the received picture compared to the original picture is estimated from the false detection rate of the marker signal.

Fig.1 shows an example of the configuration. This figure shows the case with tandem connection of codecs. At the entrance to the transmission chain, invisible marker signals are embedded. They are transmitted to the receiver point through the codec tandem connection stages. At each output of the decoders, a marker detector is connected, so that it is possible to evaluate the picture quality at the output of each stage.

Figure 1 : An example of configuration.

# 3. Features of the scheme

Picture quality assessment that does not require the original picture:

  - Can be realized simply by addition of preprocessing and postprocessing without changing existing equipment such as codecs.

  - Can automatically monitor the picture quality at each point in a TV transmission chain.

  - No need to process the transmitted signal itself at the relay points of the tandem connection. Only a marker detector is required.

  - No influence on picture quality due to the insertion of markers at the preprocessor.

  - Easy implementation.

# 4. Method for embedding and detecting marker signals

Fig.2,3,4 shows the configurations for embedding and detecting invisible marker signals by the spread spectrum method.

Figure 2: Embedding of marker signals by spread spectrum method.

Figure 3: Detection of marker signals.

Figure 4: Embedding and detection of signals by changing

Each picture is separated into rectangular blocks.  represents the input signal in each block. Next,  is multiplied by , a PN sequence, so that the spectrum is spread. Further, a Fourier transform is applied to this, and a spread spectrum signal  is obtained.

where  represents the Fourier transform.

Next, the amplitude of a frequency component  in ., is manipulated so as to embed binary information {0,1}. The detection of the binary information on the receiver side is performed by checking the parity of the level value that is obtained by quantizing  by a step size (Fig.4) where represents the embedded bit.

On the other hand, the embedding of {0,1} on the transmitter side is realized by changing the value of . When the quantized level of  is even, i.e.,  (m: integer), it is performed as follows.

- When

- When

If :

If :

Similarly, when the quantized level of is odd, i.e., , the signal is embedded by changing the value of . The above is repeatedly applied to all blocks to complete the signal embedding on the transmitter side. The bit pattern of the marker signal and the PN sequence is shared between the transmitter and the receiver sides.

On the receiver side, by the same procedure as that used on the transmitter side, after spectrum spreading is applied to each block in the received picture, the parity of the quantized level of the same frequency component as on the embedding side is checked so as to detect the embedded bit (Fig.3).

As the receiver side knows the sequence of embedded bits, it is possible to judge whether the detected bit is correct or not. By performing this judgment on all blocks, the rate of false detection of marker signals is obtained.

# 5. Experiments

In the proposed method, the false detection rate is calculated on the assumption that the relation between the false detection rate and objective picture quality are already known. Therefore, computer simulations are necessary to confirm that the relation can be obtained. It is necessary to have this relation prior to detecting the markers.

Table 1 shows the parameters for experiments.

Table 1: Parameters for experiments

## 5.1 Relationship between Marker detection rate and RSNR

Figure 5 shows the relation between the false detection rate and RSNR. In this figure, there is four different points for one kind of picture. Each point represents each result of four different bitrates, and the smaller the false detection rate that the point has, the higher the bitrate the picture is coded by. The vertical and horizontal axes represent the mean value of RSNR and false detection rate in 30 frames respectively.

RSNR represents degradation in the AC components in the decoded picture, and defined as following equation;

where represents the mean value of variances of each macroblock, and RSNR is used as a general picture quality measure because it can easily be converted to PSNR by using the value (which

can be substituted with the variance of macroblocks of the decoded picture if the degradation is moderate).

Figure 5 shows that there is a strong correlation between the false detection rate of the markers and the RSNR. From this result, a regression line can be drawn and its mean absolute error is 1.45dB. This regression line can be used independently of the bitrates and kind of pictures. Therefore, once this regression line is derived, the RSNR can be estimated only by the false detection rate.

Table 2 shows each picture’s degradation caused by marker embedding.  In each picture, the PSNR between the original and marker-embedded pictures is over 47dB, which is much smaller than the degradation caused by MPEG-2 coding and this degree of degradation is not perceivable by the human eye.

## 5.2 Application to tandem connection of codecs

In this section, application to tandem connections is discussed. If there is a correlation independent of connection stages and the kind of picture, then picture quality assessment just by using the false detection rate is possible in tandem connections.

Figure 6 shows the relation between false detection rate and the RSNR when applying the proposed method to tandem connection of codecs. As shown in Table 1, the number of stages in the tandem connection is 3.  This figure confirms that there is a correlation independent of the number of stages and picture titles, and the regression line shown in Figure 6 can also be obtained. Thus, the proposed method can be applied to tandem connection of codecs.

Table 2: Degradation of the original pictures by markers

Table 3:  MAE of RSNR estimation and degradations of the original pictures by the markers

## 5.3 Study on further accurate estimation

In this section, we discuss how to improve the estimation accuracy of the proposed method. In the above experiment, 1320 bits information were embedded as the marker into one frame, and the picture quality is measured by the detection rate. So, for a more accurate estimation, more information must be embedded into frames because the error variance (mean square error of estimation) is likely to decrease due to the increase in samples. In the proposed method, ways to increase the number of embedded bits in a frame are:

- To embed two or more bits in the macroblocks

- To embed a bit into a block smaller than the macroblock (16x16 square pixel block)

The difference in the above two items is that 1. does not change the size of data hiding block but increases the quantity of information embedded into the block and,  2. does not change the quantity of embedded information per block (1bit) but does change the pixel block units for data hiding. To confirm the effectiveness of these two approaches, the experiments were conducted under the following condition and the estimation accuracy and degradation cause by the markers were measured;

- Embed 2bit markers into macroblock (16x16 block, 2bits/block)

- Embed 1bit markers into 16x8 block (16x8 block, 1bit/block)

- Embed 1bit markers into 8x8 block (8x8 block, 1bit/block)

In Table 3, the mean absolute value of estimation error and degradation of the original pictures by the markers for each block size and the number of embedded bits are shown. The relationship between RSNR and the false detection rates of experiments ii.), iii.) and iv.) are shown in Figures 7 and 8 , respectively. These results prove that increasing the number of embedded bits in a block is not effective and only serves to increase the degradation in the original pictures. On the other hand, reducing the blocksize and embedding only one bit is proved to be effective in improving the estimation accuracy. This is because the correlation between each marker signal is so strong that they cannot decrease the error variance, while increasing the number of bits in a block. On the other hand, when reducing the block size, the correlations in marker signals in each block are not strong, so that they can decrease error variance and show high accuracy. As for the degradation due to the markers, all degradations in experiments i.)- iv.) caused by the markers were greater than degradation in the case of embedding 1bit for each macroblock; the estimation accuracy and degradation by the markers have a tradeoff relationship, so that block size for embedding the marker should be chosen carefully according to the required estimation accuracy and degradation.

# 6. Conclusion

As an automatic method for picture quality assessment, the authors proposed a scheme based on the insertion of invisible marker signals. It is effective even for tandem connection of codecs, and the estimation error is about 1dB.

This shows considerable potential for the realization of a picture quality assessment method that does not require reference pictures. Future work includes improvement of the estimation accuracy and the application of the method to transmission processing other than compression codecs by refining the method of embedding marker signals.

____________

# Text boxes

Figure 8: Relation between False detection rate and RSNR(8x8 pixel blocks, 1bit/block)

Figure 7: Relation between False detection rate and RSNR(16x8 pixel blocks, 1bit/block)

Figure 5: Relation between False detection rate and RSNR(One TM5 codec)

Figure 6: Relation between False detection rate and RSNR(Tandem Connection of codecs)