MM Group

TEST PLAN

Draft Version 1.0

Contact:	H. Myler	Tel: 	(407) 823-5098

Fax: 	(407) 823-5385

E-Mail: hrm@engr.ucf.edu

Editorial History

| Version | Date | Nature of the modification |
| --- | --- | --- |
| 1 | 28/01/04 | First draft, edited by David Hands |

Summary

List of Acronyms

1. Introduction	6

2. Subjective Evaluation Procedure	7

2.1.The <<XXX>> method	7

2.1.1.General description	7

2.1.2.Viewing conditions	7

2.1.3.Instructions to viewers for quality tests	7

2.1.4.Viewers	7

2.2.Data format	7

2.2.1.Results data format	7

2.2.2.Subject data format	7

2.2.3.Subjective Data analysis	7

3.Test Laboratories	7

3.1.ILG	7

3.2.Proponent Laboratories	7

4.Sequence processing and data formats	8

4.1.Sequence processing overview	8

4.2.Test materials	8

4.2.1.Selection of test material (SRC)	8

4.2.2.Hypothetical reference circuits (HRC)	8

4.2.3.Distribution of tests over facilities	8

4.2.4.Processing and editing sequences	8

4.2.5.Randomization	8

4.2.6.Presentation structure of test material	8

5.Objective Quality Models	8

5.1.Model type	8

5.2.Model input and output data format	8

5.3.Submission of executable model	8

5.4.Registration	9

5.5.Results analysis	9

6. Objective quality model evaluation criteria	10

6.1.Introduction to evaluation metrics	10

6.2.Evaluation Metrics	11

6.2.1.Metrics relating to Prediction Accuracy of a model	12

6.2.2.Metrics relating to Prediction Monotonicity of a model	12

6.2.3.Metrics relating to Prediction Consistency of a model	12

6.2.4.Metrics relating to agreement	13

6.3.Generalizability	13

6.4.Complexity	14

7.Calendar and actions 	14

8. Recommendation	14

9.Bibliography	15

10.Annex: Optimum mean square quantization method.	15

10.1.The Lloyd Iteration for codebook improvement	15

10.2.The Lloyd algorithm	16

List of Acronyms

ANOVA	ANalysis Of VAriance

ASCII	ANSI Standard Code for Information Interchange

CCIR	Comite Consultatif International des Radiocommunications

CODEC	Coder-Decoder

CRC	Communications Research Center (Canada)

DVB-C	Digital Video Broadcasting-Cable

FR	Full Reference

GOP	Group of Pictures

HRC	Hypothetical Reference Circuit

IRT	Institut Rundfunk Technische (Germany)

ITU	International Telecommunications Union

MM	multimedia

MOS	Mean Opinion Score

MOSp	Mean Opinion Score, predicted

MPEG	Motion Pictures Expert Group

NR	No (or Zero) Reference)

NTSC	Nat’l Television Standard Code (60 Hz TV)

PAL	(50 Hz TV)

PS	Program Segment

QAM	Quadrature Amplitude Modulation

QPSK	Quadrature Phase Shift Keying

RR	Reduced Reference

SMPTE	Society of Motion Picture and Television Engineers

SRC	Source Reference Channel or Circuit

SSCQE 	Single Stimulus Continuous Quality Evaluation

VQEG	Video Quality Experts Group

VTR	Video Tape Recorder

# Introduction

This document defines the procedure for evaluating the performance of objective video quality models submitted to the Video Quality Expert Group (VQEG) formed from experts of ITU-T Study Groups 9 and 12 and ITU-R Study Group 6. It is based on discussions from various meetings of the VQEG Multimedia experts group (MM), on 6-7 March in Hillsboro, Oregon at Intel and on 27-30 January 2004 in Boulder, Colorado at NTIA/ITS.

The goal of the MM group is to recommend a quality model suitable for application to digital video quality measurement in multimedia applications. Multimedia in this context is defined as being of or relating to an application that can combine text, graphics, full-motion video, and sound into an integrated package that is digitally transmitted over a communications channel. Common applications of multimedia that are appropriate to this study include video teleconferencing, video on demand and Internet streaming media. The measurement tools recommended by the MM group will be used to measure quality both in laboratory conditions using a FR method and in operational conditions using RRNR methods.

The performance of objective models will be based on the comparison of the MOS obtained from controlled subjective tests and the MOSp predicted by the submitted models. This testplan defines the test method or methods, selection of test material and conditions, evaluation metrics to examine the predictive performance of competing objective multimedia quality models.

to correlation metrics, the recommendation must consider technical constraints such as reference bit rate, in service and real time operation.

The overall preference is that for each form of model assessed by the group, to have one model for recommendation, but multiple models are possible depending on the outcome of the tests. In order to achieve this goal, the purpose of the MM Group is to produce a more discriminating test than was accomplished in the VQEG Phase I tests. Then, the quality range will address broadcast TV and real-time implementation issues will be evaluated through the complexity of the recommended model(s).

The objective models will be tested using a set of digital video sequences selected by the VQEG RRNR-TV group. The test sequences will be processed through a number of hypothetical reference circuits (HRC's). The quality predictions of the submitted models will be compared with subjective ratings from human viewers of the test sequences as defined by this Test Plan. The set of sequences will cover both 50 Hz and 60 Hz formats.

Several bit rates of reference channel are defined for the model, these being zero (No Reference), 10 Kb/s, 56 Kb/s and 256 Kb/s.

Model performance for each from of model will be compared separately with the results from each of the four bit rates, then compared between them, for a given efficiency.

A final report will be produced after the analysis of test results.

# Subjective Evaluation Procedure

## The <<XXX>> method

### General description

If two tests to be performed, one on TV (Test A: 384k and above) and one on simulated mobile (Test B: 384k and below), then desciption should cover requirements for each type of test.

Need to define video or audio-video.

### Viewing conditions

### Instructions to viewers for quality tests

### Viewers

## Data format

### Results data format

### Subject data format

### Subjective Data analysis

# Test Laboratories

## ILG

## Proponent Laboratories

# Sequence processing and data formats

## Sequence processing overview

## Test materials

### Selection of test material (SRC)

### Hypothetical reference circuits (HRC)

Bit-rates

Test A: 2 Mbit/s, 1.5 Mbit/s, 1 Mbit/s, 700 kbit/s, 512 kbit/s, 384 kbit/s

Test B: 384 kbit/s, 256 kbit/s, 128 kbit/s, 64 kbit/s, 32 kbit/s, 16 kbit/s

Packet Loss Rates

Test A and B: 0%, 0.5%, 1%, 5%, 8%, 10%

Frame Rates

Bit-rate dependent.

Proposal:

2 Mbit/s – 1 Mbit/s = 25 fps

700kbit/s – 256 kbit/s = 15 fps

128 kbit/s – 64 kbit/s = 10 fps

32 kbit/s – 16 kbit/s = 5 fps

Coding Schemes

Proposal:

WM9

h.264

RealNetworks

Apple Quicktime

Include matrix with test conditions set out for both types of test (i.e. TV and PDA/mobile)

### Distribution of tests over facilities

### Processing and editing sequences

### Randomization

### Presentation structure of test material

# Objective Quality Models

## Model type

## Model input and output data format

## Submission of executable model

## Registration

## Results analysis

# Objective quality model evaluation criteria

If DSCQS, need to include F-tests and consider aggregation issues.

## Introduction to evaluation metrics

A number of attributes characterize the performance of an objective video quality model as an estimator of video picture quality in a variety of applications. These attributes are listed in the following sections as:

- Prediction Accuracy

- Prediction Monotonicity

- Prediction Consistency

This section lists a set of metrics to measure these attributes. The metrics are derived from the objective model outputs and the results from viewer subjective rating of the test sequences. Both objective and subjective tests will provide a single number (figure of merit) for each half second of the processed sequence that correlates with the video quality MOS of the processed sequence. It is presumed that the subjective results include mean ratings and error estimates that take into account differences within the viewer population and differences between multiple subjective testing labs.

The objective quality model evaluation should be done in 5 steps, as described below. Two main evaluations are proposed, one common evaluation, and a post processed evaluation. The post processed evaluation allows an increase in the number of evaluation criteria in a meaningful way. The quantized evaluation is often more relevant than other comparisons.

| 1 | Data set verified by ILG. |
| --- | --- |
| 2 | Evaluation Metrics for the data set |
| 3 | Post processing : quantization |
| 4 | Evaluation Metrics for the quantized data set |
| 5 | Diagnostic |

- Objective quality model evaluation.

Evaluation metrics are described below and several metrics are computed to develop a set of comparison criteria. Furthermore, the data set should not be shared to keep information secure. Thus, if a proponent wanted to share the data set to distinguish several reduced reference bitrate categories, or other specific aspects, it will have to be discussed before the data analysis starts. The data set parts will have to be large enough to allow relevant statistical analysis (at least 600 MOS corresponding to one segment). Finally, all data parts will be size equivalent, and have the same standard deviation, to be compared each other.

Summary of evaluation criteria:

| Common criteria | Criteria for quantized data |
| --- | --- |
| Metric 1 | 95 % confidence interval | Metric 1 | 95 % confidence interval |
| Metric 2 | Root mean square error | Metric 2 | Root mean square error |
| Metric 3 | Pearson linear correlation | Metric 3 | Spearman Rank order correlation |
| Metric 4 | Outlier ratio | Metric 4 | Outlier ratio |
| Metric 5 | Kurtosis | Metric 5 | Kurtosis |
|  |  | Metric 6 | Kappa coefficient |

## Evaluation Metrics

This section lists the evaluation metrics to be calculated on the subjective and objective data. Once the nonlinear transformation of section  has been applied to subjective and objective data, the objective model prediction performance is then evaluated by computing various metrics on the actual sets of data.

The set of differences between measured and predicted MOS is defined as the quality-error set Qerror[]:

Qerror[i] = MOS[i] – MOSp[i]

Where the index i refers to a Time Code of the processed video sequence.

### Metrics relating to Prediction Accuracy of a model

Metric 1:	The 95% inverse-confidence interval-weighted root-mean-square error of the error set Qerror[].

with CONF[i] = 95% confidence interval for the ith point (of N points). The constant factor of 0,5 is added to stabilize the calculation for cases of very small confidence interval.

Metric 2:	The simple root-mean-square error of the error set Qerror[].

Note: The usual Pearson linear correlation coefficient between MOSp and MOS will not be used for quantized data due to the large amount of data where the Pearson correlation becomes inefficient. Instead, the Spearman rank order correlation will be used, which is well adapted for quantized data.

### Metrics relating to Prediction Monotonicity of a model

Metric 3:

For quantized data: Spearman rank order correlation coefficient between MOSp and MOS.

Therefore, results obtain with this metric must be interpreted carefully. Thus, there is a lot of data and only 5 possible values, so there is a very large amount of ex-æquo ???<<XXX>>. When the ex-æquo proportion is too large, the metric becomes less efficient; so the results can’t be considered alone. This metric has to be taken into account with regard of others metrics.

For classical data: Pearson linear correlation between MOS and MOSp.

### Metrics relating to Prediction Consistency of a model

Metric 4: 	Outlier Ratio of “outlier-points” to total points N.

Outlier Ratio = (total number of outliers)/N

where an outlier is a point for which: ABS[ Qerror[i] ] > 2*MOSStandardError[i].

Twice the MOS Standard Error is used as the threshold for defining an outlier point.

Metric 5:	The Kurtosis of the error distribution Qerror[]:

Where  is the standard deviation of the error set Qerror[]

The Kurtosis measures the relative spread of the model’s error distribution with respect to its standard deviation. The –3 term is classically introduced into the definition to compare the measured distribution to that of a normal distribution. A normal distribution has Kurtosis = 0, while a distribution with a shape broader than a normal distribution has a Kurtosis > 0.

### Metrics relating to agreement

Metric 6:	The Kappa coefficient.

=

Where ƒo is the observed number of agreement between MOS and MOSp for each of the 5 MOS class, and ƒE is the number of agreement due to coincidence (can be computed by the product of the number of MOS and MOSp for a given class, divided by N).

|  | MOS 1 | MOS 2 | MOS 3 | MOS 4 | MOS 5 | Total |
| --- | --- | --- | --- | --- | --- | --- |
| MOSp 1 | ƒo(1) |  |  |  |  | Tp 1 |
| MOSp 2 |  | ƒo(2) |  |  |  | Tp 2 |
| MOSp 3 |  |  | ƒo(3) |  |  | Tp 3 |
| MOSp 4 |  |  |  | ƒo(4) |  | Tp 4 |
| MOSp 5 |  |  |  |  | ƒo(5) | Tp 5 |
| Total | T 1 | T 2 | T 3 | T 4 | T 5 | N |

Where Ti = #MOSi and Tpi = #MOSpi.

and, ƒE(i)= (TiTpi)/N.

So, the Kappa is a metric of agreement, and is not influenced by coincidence. Thus, K values are between –1 and 1, but do not have to be interpreted as a correlation coefficient. K values are lower than correlation, and a value around 0.4 indicates that the method is efficient.

If these metrics will not allow model efficiency to be distinguished, it is possible to introduce a 7th metric as a false alarm rate. Indeed, it is possible to compute how many times the model gives a wrong estimation of the MOS class, and so on, to identify the most robust model.

## Generalizability

Generalizability is the ability of a model to perform reliably over a very broad range of video content. This is a critical selection factor given the very wide variety of content found in real applications. There is no specific metric that is specific to generalizability, so this objective testing procedure requires the selection of as broad a set of representative test sequences as is possible. The test sequences and specific HRC’s will be selected by the members of VQEG and should ensure broad coverage of typical content (spatial detail, motion complexity, color, etc.) and typical video processing conditions. The breadth of the test set will determine how well the generalizability of the models is tested. At least 20 different scenes are recommended as a minimum set of test sequences. It is suggested that some quantitative measures (e.g., criticality, spatial and temporal energy) should be used in the selection of the test sequences to verify the diversity of the test set.

## Complexity

The performance of a model as measured by the above Metrics #1-6 will be used as the primary basis for model recommendation. If several models are similar in performance, then the VQEG may choose to take model reference data bit rate into account in formulating their recommendations. For similar performance, the smaller reference data bit rate will be recommended. Thus, if reference data bitrates are not discriminating enough, a model comparison should be done within each module defined in ITU document 10-11Q/TEMP/28-R1.

# Calendar and actions

| Due date | Action | Who |
| --- | --- | --- |
|  | Test plan final version |  |
|  | Sequence processing |  |
|  | Subjective tests |  |
|  | Subjective data analysis |  |
|  | Submission of executable models |  |
|  | Objective data analysis Final report edition |  |
|  | Final report. |  |

# Recommendation

The VQEG will recommend methods of objective video quality assessment based on the primary evaluation metrics defined in section 4. The Study Groups involved (ITU-T SG 12, ITU-T SG 9, and ITU-R SG 6) will make the final decision(s) on ITU Recommendations.

# Bibliography

- VQEG Phase I final report.

- VQEG Phase I Objective Test Plan.

- VQEG Phase I Subjective Test Plan.

- VQEG FR-TV Phase II Test Plan.

- Vector quantization and signal compression, by A. Gersho and R. M. Gray. Kluwer Academic Publisher, SECS159, 0-7923-9181-0.

- Recommendation ITU-R BT.500-10.

- document 10-11Q/TEMP/28-R1.

- RR/NR-TV Test Plan

# Annex: Optimum mean square quantization method.

The principal goal of quantizer design is to select the reproduction levels and the partition regions or cells so as to provide the minimum possible average distorsion for a fixed number of levels N (here N = 5). Effective algorithms are available, like the Lloyd one, which is proposed below. More explicitly, for the average (mean square) distorsion measure, the goal, as usually stated, is to find the output points yi and partition cells Ri that minimize

D =

Where ƒX is the pdf (probability density function) of the random variable X.

Specifically, the Lloyd algorithm is applied to the design of a quantizer for the empirical distribution, that is the distribution of the set of observations. Here, the set of observations is the MOS data set.

The key to this iterative algorithm is a mapping that converts a given codebook into a new and improved codebook. The design algorithm begins with an initial codebook and repeats this mapping until a suitable stopping criterion is satisfied. The codebook improvement mapping is the basic iteration of the algorithm.

## The Lloyd Iteration for codebook improvement

- Given a codebook Cm = {yi }, find the optimal partition into quantization cells, that is, use the nearest neighbor condition to form the nearest neighbor cells:

Ri = {x : d(x,yi)  d(x,yj); all j  i }

- Using the centroid (or center of mass) condition, find Cm+1, the optimal reproduction alphabet (codebook) for the cells just found.

The basic form of the Lloyd iteration assumes that the input pdf is known in order to compute the centroids (a sample distribution based on empirical observations is used instead of pdf to generate the improved codebook). 10.1Illustrates the Lloyd iteration and indicates the dependence of the mapping on the specified pdf.

- Flow chart of the Lloyd iteration for codebook improvement

## The Lloyd algorithm

Step 1.	Begin with an initial codebook C1. Set m = 1.

Step 2.	Given the codebook, Cm, perform the Lloyd Iteration to generate the improved codebook Cm+1.

Step 3.	Compute the average distorsion for Cm+1. If it has changed by a small enough amount since the last iteration, stop. Otherwise set m+1  m and go to Step2.

The initial codebook may have the lattice pattern of a uniform quantizer or it may be a reasonable codebook that has N points roughly represent the range of values taken on by the input.

# Footnotes

VQEG Test Plan, Phase I Final Report, April 2000.

# Text boxes

Nearest Neighbor Partitioning

Centroid Computation

Cm

Cm+1

1

Data set

3

post processing

2

evaluation metrics

4

Evaluation Metrics

5

Analysis

Final Report

Editors Note: unresolved issues or missing data are annotated by the string <<XXX>>