Decision Reached (up until start of MM meeting, Rome 2004):

Agreement was reached to test mobile service and PC type HRCs only (i.e., not MM television HRCs). [Boulder Jan 2004]

Agreement was reached to use ACR method.  [MM audio call, May 04]

Agreement was reached to perform video only testing of FR, RR, and NR models; and audio-video testing of FR models. [Boulder Jan 2004]

Agreement was reached to push forward on video-only decisions; the door would not be closed to running an audio-video test in parallel, but general consensus that currently a number of issues with AV exist (especially access to test material and availability of a robust test methodology). [Boulder Jan 2004]

Agreement was reached to simulate a mobile display using an LCD screen. [Boulder Jan 2004]

Agreement reached to run all tests using LCD. [Audio call, May 2004]

Agreement was reached that, after proponents submit a model, they can run subjective testing.  This will ease ILG’s work. [Boulder Jan 2004]

[

- there are Independent Lab Group  (ILG) and proponent laboratories

- each proponent prepares some % of test conditions (SRC/HRC combinations)

- the proponent then sends all their prepared test conditions to the ILG

- the ILG is responsible for selecting some subset of test conditions from each of the proponent contributions

- proponents  will have no knowledge of what test conditions are selected by the ILG

- proponents will be responsible for ensuring the test conditions meet any registration requirements

- once proponent models have been submitted, the ILG distributes test material to proponents for subjective testing

][JRG March 2004)

Agreement was reached that the reference should be full frame-rate and not reduced to match the HRC. [Boulder Jan 2004]

Calibration/registration

Full Reference Models must include calibration.

Reduced reference Models must include temporal calibration if the models need it. Spatial offsets are expected to be very rare. Spatial registration will be assumed to be within (1) pixels. Gain, offset and spatial registration will be corrected if necessary, to satisfy the calibration requirement specified the test plan.

No reference Models should not need calibration.

[Boulder Jan 2004]

Discussion of viewing distance:

QCIF	nominally 6-10H, but viewers can choose a comfortable distance within this range

CIF	nominally 6-8H, but viewers can choose a comfortable distance within this range

601	6H

[Boulder Jan 2004]

Variable temporal offsets was considered to be allowable. Tentative agreement on +/- 1 second variable offset for all video formats. Need to have longer test sequences to accommodate variable temporal offsets – so if we use 8 seconds sequences we should have 9 seconds sequences for producing processed test sequences. [JRG March 2004]