HDTV Group

TEST PLAN

Draft Version 0.1

November 09, 2004

Contact:	Vivaik Balasubrawmanian	Tel: 	+1 (480) 554 1905

E-Mail: vivaik.balasubrawmanian@intel.com

Editorial History

| Version | Date | Nature of the modification |
| --- | --- | --- |
| 0.0 | November 1, 2004 | Initial Draft, edited by Vivaik Balasubrawmanian |
| 0.1 | November 9, 2004 | Incorporated the following changes from NTIA (Margaret Pinson): Added an editor’s note to highlight the unapproved status. Removed references to future test plans (AV & Interactive) Replaced ACR-HRR with DSIS subjective testing methodology Removed redundant sections Minimum bit rate for HRCs is now 2 Mbits/s. Replaced inconsistent section on Calibration/Registration with the latest text from RRNR test plan. Removed evaluation metrics in line with the agreements reached in the Seoul MM meeting. |

Summary

List of Acronyms

1. Introduction	6

2. Subjective Evaluation Procedure	7

2.1.The <<XXX>> method	7

2.1.1.General description	7

2.1.2.Viewing conditions	7

2.1.3.Instructions to viewers for quality tests	7

2.1.4.Viewers	7

2.2.Data format	7

2.2.1.Results data format	7

2.2.2.Subject data format	7

2.2.3.Subjective Data analysis	7

3.Test Laboratories	7

3.1.ILG	7

3.2.Proponent Laboratories	7

4.Sequence processing and data formats	8

4.1.Sequence processing overview	8

4.2.Test materials	8

4.2.1.Selection of test material (SRC)	8

4.2.2.Hypothetical reference circuits (HRC)	8

4.2.3.Distribution of tests over facilities	8

4.2.4.Processing and editing sequences	8

4.2.5.Randomization	8

4.2.6.Presentation structure of test material	8

5.Objective Quality Models	8

5.1.Model type	8

5.2.Model input and output data format	8

5.3.Submission of executable model	8

5.4.Registration	9

5.5.Results analysis	9

6. Objective quality model evaluation criteria	10

6.1.Introduction to evaluation metrics	10

6.2.Evaluation Metrics	11

6.2.1.Metrics relating to Prediction Accuracy of a model	12

6.2.2.Metrics relating to Prediction Monotonicity of a model	12

6.2.3.Metrics relating to Prediction Consistency of a model	12

6.2.4.Metrics relating to agreement	13

6.3.Generalizability	13

6.4.Complexity	14

7.Calendar and actions 	14

8. Recommendation	14

9.Bibliography	15

10.Annex: Optimum mean square quantization method.	15

10.1.The Lloyd Iteration for codebook improvement	15

10.2.The Lloyd algorithm	16

List of Acronyms

ACR-HRR	Absolute Category Rating with hidden reference removal

ANOVA	ANalysis Of VAriance

ASCII	ANSI Standard Code for Information Interchange

CCIR	Comite Consultatif International des Radiocommunications

CODEC	Coder-Decoder

CRC	Communications Research Center (Canada)

DVB-C	Digital Video Broadcasting-Cable

FR	Full Reference

GOP	Group of Pictures

HRC	Hypothetical Reference Circuit

IRT	Institut Rundfunk Technische (Germany)

ITU	International Telecommunications Union

MM	multimedia

MOS	Mean Opinion Score

MOSp	Mean Opinion Score, predicted

MPEG	Motion Pictures Expert Group

NR	No (or Zero) Reference)

NTSC	Nat’l Television Standard Code (60 Hz TV)

PAL	(50 Hz TV)

PS	Program Segment

QAM	Quadrature Amplitude Modulation

QPSK	Quadrature Phase Shift Keying

RR	Reduced Reference

SMPTE	Society of Motion Picture and Television Engineers

SRC	Source Reference Channel or Circuit

SSCQE 	Single Stimulus Continuous Quality Evaluation

VQEG	Video Quality Experts Group

VTR	Video Tape Recorder

# Introduction

This document defines the procedure for evaluating the performance of objective perceptual quality models submitted to the Video Quality Expert Group (VQEG) formed from experts of ITU-T Study Groups 9 and 12 and ITU-R Study Group 6. It is based on discussions from various meetings of the VQEG HDTV working group (HDTV).

The goal of the HDTV group is to recommend a quality model suitable for application to digital video quality measurement in HDTV applications. HDTV in this context is defined as being of or relating to an application that creates / consumes High Definition television broadcast that is digitally transmitted over a communication channel. Common applications of HDTV that are appropriate to this study include Television broadcasting, video on demand and satellite / cable transmissions. The measurement tools recommended by the HDTV group will be used to measure quality both in laboratory conditions using a FR method and in operational conditions using RR/NR methods.

In the first stage of testing, it is proposed that video only test conditions will be employed. It should be noted that presently there is a lack of HDTV test material for use in testing. The VQEG does desire to have copyright free (or at least free for research purposes) material for testing. The capability of the group to perform adequate audio-video and multimedia testing is dependent on access to a bank of potential test sequences.

The performance of objective models will be based on the comparison of the DMOS obtained from controlled subjective tests and the DMOSp predicted by the submitted models. This testplan defines the test method or methods, selection of test material and conditions, evaluation metrics to examine the predictive performance of competing objective multimedia quality models.

The goal of the testing is to examine the performance of proposed video quality metrics across representative transmission and display conditions. To this end, the tests will enable assessment of models for cable/satellite/terrestrial transmissions and broadband communications services. The Recommendation(s)  resulting from the VQEG MM testing will be deemed appropriate for services delivered on computer desktop monitors and high definition display television technologies.

It is expected that subjective tests will be performed separately for different display conditions (e.g. one specific test for LCD TVs; another test for desktop computer monitor). The performance of submitted models will be evaluated for each type of display condition. Therefore it may be possible for one model to be recommended for one display type (say, computer monitor) and another model for another display format (say, plasma television).

The objective models will be tested using a set of digital video sequences selected by the VQEG HDTV group. The test sequences will be processed through a number of hypothetical reference circuits (HRC's). The quality predictions of the submitted models will be compared with subjective ratings from human viewers of the test sequences as defined by this Test Plan.

A final report will be produced after the analysis of test results.

# Subjective Evaluation Procedure

## The DSIS method

This section describes the test method according to which the VQEG HDTV subjective tests will be performed.  We will use the DSIS [ITU-R Rec. BT.500-11].

### General description

The selected test methodology is the Double-Stimulus Impairment Scale (DSIS) method. This choice has been selected due to the fact that DSIS provides a reliable and standardized method (ITU-R Rec. 500-11, ITU-T P.910) that allows a large number of test conditions to be assessed in any single test session.

In the DSIS test method, each test condition is presented once only for subjective assessment. The test presentation order is randomized according to standard procedures (e.g. Latin or Graeco-Latin square). The test format is cyclic, in that the subject is first presented with the reference video sequence, then with the same video sequence impaired.  Following this, the subject is asked to vote on the second, keeping in mind the first.  Subjective ratings are reported on the five-grade impairment scale:

- imperceptible

- perceptible, but not annoying

- slightly annoying

- annoying

1	very annoying

### Application Across Different Video Formats and Displays

The proposed HDTV test will examine the performance of objective perceptual quality models for different video formats (720p, 1080i and 1080p). Section 2.1.3 defines format and display types in detail.  Video applications targeted in this test include internet video on demand, HDTV broadcasts, etc.

The instructions given to subjects will request subjects to maintain a specified viewing distance from the display device. The viewing distance has been agreed as:

- 720p: 	4H.

- 1080i:	4H.

- 1080p:	4H

H=Picture Heights (picture is defined as the size of the video window)

### Display Specification and Set-up

Given that the subjective tests will use different HD display technologies, it is necessary to ensure that each test laboratory selects appropriate display specification and common set-up techniques are employed. The following display technologies should be covered by the tests :

- Professional grade Computer Monitor (eg : Viewsonic Professional series P225f)

- Consumer grade LCD HD TV.

- Consumer grade Plasma HD Television.

- Consumer grade Rear Projection HD Television

- Consumer grade DLP HD Television.

- Consumer grade HD overhead projectors.

(XXX Note : Should we included EDTVs ?)

### Subjects

Each test will require at least 24 subjects. It is recommended that as many subjects as possible participate in each test in order to improve the statistical power of the resulting data. It is preferred that each subject be given a different ordering of video sequences where possible. Otherwise, the viewers will be assigned to sub-groups, which will see the test sessions in different orders. At least two different orderings of test sequences are required per subjective test.

Only non-expert viewers [Ed. Note: Definition of “non-expert viewer” is needed.  P. Corriveau agreed to provide this prior to the next VQEG meeting] will participate. The term non-expert is used in the sense that the viewers’ work does not involve video picture quality and they are not experienced assessors. They must not have participated in a subjective quality test over a period of six months. All viewers will be screened prior to participation for the following:

- normal (20/20) visual acuity with or without corrective glasses (per Snellen test or equivalent).

- normal colour vision (per Ishihara test or equivalent).

- familiarity with the language sufficient to comprehend instruction and to provide valid responses using semantic judgement terms expressed in that language.

Note; for any test involving audio, appropriate screening for normal hearing should be applied (following relevant audio test recommendations)[e.g., P.800, BS-1116].

### Viewing Conditions

Each test session will involve only one subject assessing the test material. Subjects will be seated directly in line with the centre of the video display at the appropriate viewing distance. The test cabinet will conform to ITU-T Rec. P.910 requirements.

### Test data collection

The collection and organization of the data files containing the votes will be under the direct responsibility of the ILG Chair.

## Data Format

### Results Data Format

### Subject Data Format

### Subjective Data Analysis

Each subject's results will be checked for completeness. An observer is discarded if the number of failed votes exceeds one in one of the sessions. Additionally, the observers will be screened after the test as specified in sec. 2.3.1 of Annex 2 “Screening for DSIS, DSCQS and alternative methods except SSCQE method” of recommendation ITU-R BT.500-10. The post-test screening will not be applied to these sub-groups but to the groups which participate in one test as a whole.

# Test Laboratories and Schedule

Given the scope of the HDTV testing, it is proposed that both independent test laboratories and proponent laboratories will be given subjective test responsibilities. The ILG will oversee the testing to ensure that all laboratories conform to the requirements set out in this testplan.

## ILG

The independent test group is composed of FUB (Italy), CRC (Canada) and Verizon (USA). A proposal from France Telecom has been received where FT would become an ILG. However, FT will only act as a member of the ILG if the MSCQS method is included in the subjective testing process. Currently, it has been provisionally agreed for FT to participate using the MSCQS method, but that the results from this method would only be valid if they mirror results from laboratories using the DSCQS approach. FT would receive a reduced fee for acting as an independent test laboratory.

## Proponent Laboratories

A number of proponents also have significant expertise in and facilities for subjective quality testing. Proponents indicating a willingness to participate as test laboratories are BT, Genista, NTIA, NTT, and Opticom and Yonsei. Precise details of how proponent laboratories would create test material and distribute results from their tests have yet to be specified. It is clearly important to ensure all test data is derived in accordance with this testplan. Critically, proponent testing must be free from charges of advantage to one their model or disadvantage to competing models.

## Test schedule

The ILG will verify that the submitted models (1) run on the ILG’s computers and (2) yield the correct output values when run on the test video sequences. Due to their limited resources, the ILG may encounter difficulties verifying executables submitted too close to the model submission deadline.  Therefore, proponents are strongly encouraged to submit a prototype model to the ILG prior to the verification deadline, to work out platform compatibility problems well ahead of the final verification date.  Proponents are also strongly encouraged to submit their final model executable 14 days prior to the verification deadline date, giving the ILG two weeks to resolve problems arising from the verification procedure.

The ILG requests that proponents kindly estimate the run-speed of their executables on a test video sequence and to provide this information to the ILG.

# Sequence Processing and Data Formats

Three subjective tests will be performed. The first test will assess the subjective quality of video material presented on a simulated viewing environment. This test will deploy a variety of display technologies and present video in 720p (1280 X 720p resolution). The second test will present 1080i (1920 X 1080i resolution) video. The third test will use 1080p (1920 X 1080p resolution) video.

Note that in all subjective tests 1 pixel of video will be displayed as 1 pixel native display. No upsampling or downsampling of the video is allowed.

Presently, VQEG has access to a set of video test sequences. For audio-video tests this database needs to be extended to include new source material containing both audio and video.

## Sequence processing overview

The test material will be selected from a common pool of video sequences.

## Test materials

The test material will be representative of a range of content and applications. The list below identifies the type of test material that form the basis for selection of sequences.

1)	movies, movie trailers

2)	sports,

3)	music video,

4)	advertisement,

5)	animation

6)	broadcasting news (business and current events)

7) 	home video

### Selection of test material (SRC)

Selection of test material will be done by the ILG. Proponents will be asked to provide source material as well as SRC/HRC combinations for consideration by the ILG when selecting test conditions for the subjective tests. The test should include some agreed percentage (e.g. 20%) of new SRC/HRC combinations that are unknown to proponents. The ILG will be responsible for selection of this unknown test material.

Further guidelines on selection of and access to test material are required if proponents are to be test laboratories.

## Hypothetical reference circuits (HRC)

The subjective tests will be performed to investigate a range of HRC error conditions. These error conditions may include, but will not be limited to, the following:

- Compression errors (such as those introduced by varying bit-rate, codec type, frame rate and so on)

- Transmission errors

- Post-processing effects

The overall selection of the HRCs will be done such that most, but not necessarily all, of the following conditions are represented:

### Video bit-rates:

- 720p: 	2 – 16 Mbps

- 1080i:	2 – 22 Mbps

- 1080p:	2 – 25 Mbps

### Transmission Errors

Error conditions produced using packet loss rates and bit errors:

- Level 1: 		None

- Level 2:		Low

- Level 3		Medium

- Level 4:		High

Proponents are asked to provide examples of error conditions that are relevant to the industry.  These examples will be viewed at the next meeting and/or examined after electronic distribution (only open source video is allowed for this).  Error conditions can be introduced using packet-loss and/or bit error conditions.

When producing test material, care must be taken to ensure that the codec has stabilized before the actual test sequence begins and after it has ended.

### Frame Freezing and Frame Skipping

A frame freeze is defined as any event where the video pauses for some period of time then restarts without losing any video information. The temporal delay through the system increases. Frame freezes will not be included in the current testing.

Frame skipping is defined as events where the video pauses then restarts with some loss of video information. In frame skipping, the temporal delay through the system is approximately unchanged. Anomalous frame skipping (*definition required*) is not allowed during the first 1s or the final 1s of a video sequence. Note that where skipping is included in a test then source material containing still sections should form part of the testing.

### Frame rates

For those codecs that only offer automatically set frame rate, this rate will be decided by the codec. Some codecs will have options to set the frame rate either automatically or manually. For those codecs that have options for manually setting the frame rate (and we choose to set it for the particular case), 25 fps will be considered the minimum frame rate.

Manually set frame rates (new-frame refresh rate) may include:

- 720p: 	50, 59.94, 60 fps

- 1080i:	24, 29.97, 30 fps

- 1080p:	50, 59.94, 60 fps

### Pre-Processing

The HRC processing  may include, typically prior to the encoding, one or more of the following:

- Filtering

- Colour space conversion (e.g. from 4:2:2 to 4:2:0)

- 3:2 Pull down.

This processing will be considered part of the HRC.

### Post-Processing

The following  post-processing effects may be used in the preparation of test material:

- Colour space conversion

- De-blocking

- Decoder jitter

### Coding Schemes

Coding Schemes that will be used may include, but are not limited to:

- Windows Media

- MPEG-2

- H.264 (MPEG-4 Part 10)

- MPEG 4

- DV

### Distribution of tests over facilities

### Processing and editing sequences

Test sequences will be captured from the decoded video in uncompressed format. Two capture methods may be employed. The two methods are as follows:

### Randomization

### Presentation structure of test material

# Objective Quality Models

## Model type

VQEG HDTV has agreed that Full Reference, Reduced Reference and No reference models may be submitted for evaluation. The side channel allowable for the RR models are:

- 720p: 	(XXX)

- 1080i:	(XXX)

- 1080p:	(XXX)

Proponents may submit one model of each type for all image size conditions. Thus, any single proponent may submit up to a total of 13 different models. Note that where multiple models are submitted, additional model submission fees may apply.

## Model input and output data format

## Submission of executable model

## Registration

The choice of HRCs and Processing by the ILG will verify that the following limits are not exceeded between Original Source and Processed sequences:

- maximum allowable deviation in Peak Video Level is +/- 10%

- maximum allowable deviation in Black Level is +/- 10%

- maximum allowable Horizontal Shift is +/- 1 pixels

- maximum allowable Vertical Shift is +/- 1 lines

- maximum allowable Horizontal Cropping is 30 pixels

- maximum allowable Vertical Cropping is 20 lines

- no Vertical or Horizontal Re-scaling is allowed

- Temporal Alignment between SRC and HRC sequences shall be maintained to within +/- 1 video frames

- Dropped or Repeated Frames are excluded from above temporal alignment limit

- no visible Chroma Differential Timing is allowed

- no visible Picture Jitter is allowed

ILG will verify adherence of all HRCs to these limits by using at least one, but preferably two softwares (NTIA software suggested) in addition to human checking. The ILG can use proponent software to fix calibration errors in selected video sequences.  Preferably, such software should be written in a language that can be easily understood (e.g., Matlab, C++ source code) and posted to the reflector.

VQEG acknowledges that the ILG can not guarantee perfect adherence to the calibration limitations in section 3.2.5, particularly for very degraded HRCs.  To prevent inclusion of too many HRC that are nonconforming, proponents will be allowed after objective data & models submitted but prior to running subjective tests, to analyze video sequences for calibration errors & suggest fixes. The proponents will be given three weeks to perform such verification. If the problem cannot be addressed satisfactorily before the subjective test has been performed, the offending sequence will be replaced.  If a sequence is found to not adhere to the calibration limitations after the subjective test has been performed, the offending sequence will not be discarded.

It is suggested that a follow-on study may be performed at a later time to test sensitivity of models against purposely inserted mis-calibrations (spatial shift, temporal shift, gain, offset).

## Results analysis

# Objective quality model evaluation criteria

Data Analysis

The same techniques that were used in the VQEG PhaseII test and reported in the final report will be used.

If DSCQS, need to include F-tests and consider aggregation issues.

## Introduction to evaluation metrics

A number of attributes characterize the performance of an objective video quality model as an estimator of video picture quality in a variety of applications. These attributes are:

- Prediction Accuracy

- Prediction Monotonicity

- Prediction Consistency

This section lists a set of metrics to measure these attributes. The metrics are derived from the objective model outputs and the results from viewer subjective rating of the test sequences. Both objective and subjective tests will provide a single number (figure of merit) for each half second of the processed sequence that correlates with the video quality DMOS of the processed sequence. It is presumed that the subjective results include mean ratings and error estimates that take into account differences within the viewer population and differences between multiple subjective testing labs.

The objective quality model evaluation should be done in 5 steps, as described below. Two main evaluations are proposed, one common evaluation, and a post processed evaluation. The post processed evaluation allows an increase in the number of evaluation criteria in a meaningful way. The quantized evaluation is often more relevant than other comparisons.

| 1 | Data set verified by ILG. |
| --- | --- |
| 2 | Evaluation Metrics for the data set |
| 3 | Post processing : quantization |
| 4 | Evaluation Metrics for the quantized data set |
| 5 | Diagnostic |

Objective quality model evaluation.

Evaluation metrics are described below and several metrics are computed to develop a set of comparison criteria. Furthermore, the data set should not be shared to keep information secure. Thus, if a proponent wanted to share the data set to distinguish several reduced reference bitrate categories, or other specific aspects, it will have to be discussed before the data analysis starts.

## Evaluation Metrics

This section lists the evaluation metrics to be calculated on the subjective and objective data. Once the nonlinear transformation (see Section X) section has been applied to subjective and objective data, the objective model prediction performance is then evaluated by computing various metrics on the actual sets of data.

The set of differences between measured and predicted DMOS is defined as the quality-error set Qerror[]:

Qerror[i] = DMOS[i] – DMOSp[i]

Where the index i refers to processed video sequence.

The following evaluation metrics along with their 95% confidence intervals and statistical significance tests (i.e.. F-Test) where applicable will to be used for models’ comparison and evaluation:

Metric 1:	The simple root-mean-square error of the error set Qerror[].

Metric 2:

Pearson linear correlation coefficient between DMOSp and DMOS.

Metric 3: 	Outlier Ratio of “outlier-points” to total points N.

Outlier Ratio = (total number of outliers)/N

where an outlier is a point for which: ABS[ Qerror[i] ] > 2*DMOSStandardError[i].

Twice the DMOS Standard Error is used as the threshold for defining an outlier point.

## Generalizability

Generalizability is the ability of a model to perform reliably over a very broad range of video content. This is a critical selection factor given the very wide variety of content found in real applications. There is no specific metric that is specific to generalizability, so this objective testing procedure requires the selection of as broad a set of representative test sequences as is possible. The test sequences and specific HRC’s will be selected by the members of VQEG and should ensure broad coverage of typical content (spatial detail, motion complexity, color, etc.) and typical video processing conditions. The breadth of the test set will determine how well the generalizability of the models is tested. At least 20 different scenes are recommended as a minimum set of test sequences. It is suggested that some quantitative measures (e.g., criticality, spatial and temporal energy) should be used in the selection of the test sequences to verify the diversity of the test set.

## Complexity

The performance of a model as measured by the above metrics will be used as the primary basis for model recommendation. If several models are similar in performance, then the VQEG may choose to take model reference data bit rate into account in formulating their recommendations. For similar performance, the smaller reference data bit rate will be recommended. Thus, if reference data bitrates are not discriminating enough, a model comparison should be done within each module defined in ITU document 10-11Q/TEMP/28-R1.

# Calendar and actions

| Due date | Action | Who |
| --- | --- | --- |
|  | Test plan final version |  |
|  | Sequence processing |  |
|  | Subjective tests |  |
|  | Subjective data analysis |  |
|  | Submission of executable models |  |
|  | Objective data analysis Final report edition |  |
|  | Final report. |  |

# Recommendation

The VQEG will recommend methods of objective video quality assessment based on the primary evaluation metrics defined in Section 6. The Study Groups involved (ITU-T SG 12, ITU-T SG 9, and ITU-R SG 6) will make the final decision(s) on ITU Recommendations.

# Bibliography

- VQEG Phase I final report.

- VQEG Phase I Objective Test Plan.

- VQEG Phase I Subjective Test Plan.

- VQEG FR-TV Phase II Test Plan.

- Recommendation ITU-R BT.500-11.

- document 10-11Q/TEMP/28-R1.

- RR/NR-TV Test Plan

- VQEG MM Test Plan

- “Overall quality assessment when targeting wide-XGA flat panel displays” by SVT Corporate Development Technology, Sweden.

Annex I
Instructions to the Subjects

“In this test, we ask you to evaluate the overall quality of the video material you see.  We are interested in your opinion of the video quality of each scene.  Please do not base your opinion on the content of the scene or the quality of the acting.  Take into account the different aspects of the video quality and form your opinion based upon your total impression of the video quality.

Possible problems in quality include:

- poor, or inconsistent, reproduction of detail;

- poor reproduction of colours, brightness, or depth;

- poor reproduction of motion;

- imperfections, such as false patterns, or “snow”.

# The test consists of a series of judgement trials

# Text boxes

1

Data set

3

post processing

2

evaluation metrics

4

Evaluation Metrics

5

Analysis

Final Report

Editors Note: unresolved issues or missing data are annotated by the string <<XXX>>

Editors Note:  This text has not been approved by VQEG and is not subject to the 2/3 majority change rule.

Phases of presentation:

T1 = 10sec Reference picture

T2 = 3sec Mid-grey

T3 = 10sec Test condition

T4 = Mid-grey / voting period

T4

T3

T2

T1