Draft Matrix Details

Arthur Webster, April, 2006

3 formats QCIF, CIF, VGA

Limit each format to 4 codecs

Limit each codec to 5 bit rates

Limit each bit rate to 4 frame rates

Gives 80 non-error HRC possibilities per format Limit to 5 error conditions per format

Gives 480 HRC possibilities per format

Subjective tests:

6-15 SRCs per test, test must be full matrix within test.

160 PVSs per test defined

Consider 10 SRC per test

Therefore 16 HRCs minus one for NULL HRC = 15 HRCs

480/15=32 tests per format to fully cover all of the assumed 480 conditions.

Propose we pick 1/3 of the conditions as being more typical than the others.

Gives about 11 subjective tests per format.

33 subjective tests at a minimum will be required.

This does not yet consider the redundancy requirement for clips across tests nor for complete test redundancy.

Still if Proponents do an average of 1 test/format then the ILG should be able to handle the rest.