| INTERNATIONAL TELECOMMUNICATION UNION | STUDY GROUP 12 |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2005-2008 | TD 203rev1 (GEN/12) |
|  | English only Original: English |
| Question(s): | 13/12 | Geneva, 16-25 January 2007 |
| TEMPORARY DOCUMENT |
| Source: | Co-Rapporteur for Question 13/12 |
| Title: | Latest draft of G.OMV |

Draft new Recommendation G.OMV

Opinion model for video-telephony applications

Summary

This Recommendation proposes an algorithm that estimates videophone quality to the QoE/QoS planners. This model can be used by QoE/QoS planners to help ensure that users will be satisfied with end-to-end service quality to avoid over-engineering the application, terminal, and network. The outputs from the model are overall multimedia quality considering the interactive quality.

The application scenario of this Recommendation is limited to QoE/QoS planning. Other application scenarios such as quality benchmarking and monitoring are outside the scope of this Recommendation.

Keywords

QoE, QoS, Subjective quality, Opinion model, Quality planning, Video telephony, Multimedia, MOS

1.	Scope	3

2.	References	3

3.	Definitions	5

4.	Abbreviations	6

5.	Conventions	6

6.	Application scenario	6

7.	Framework	8

8.	Model assumptions	10

8.1.	Speech-related assumptions	10

8.1.1.	Terminal factors	10

8.1.2.	Environmental factors	10

8.2.	Video-related assumptions	11

8.2.1.	Terminal factors	11

8.2.2.	Environmental factors	11

8.3.	Task-related assumptions	11

9.	Model inputs	11

9.1.	Speech quality parameters	12

9.1.1.	Speech delay (TS [ms])	12

9.1.2.	Speech coding distortion (IeS)	12

9.1.3.	Speech packet-loss robustness (BplS)	12

9.1.4.	Speech packet-loss rate (PplS [%])	12

9.1.5.	Talker echo loudness rating (TELR)	12

9.2.	Video quality parameters	12

9.2.1.	Video delay (TV [ms])	12

9.2.2.	Video codec specifications	12

9.2.3.	Video packet-loss rate (PplV [%])	13

9.2.4.	Video frame rate (FrV [fps])	13

9.2.5.	Video bit rate (BrV [kbps])	13

10.	Model outputs	13

11.	Model description	13

11.1.	Speech quality estimation function	13

11.2.	Video quality estimation function	14

11.2.1.	Calculation of video quality, Vq	14

11.2.2.	Basic video quality affected by coding distortion, Icoding	14

11.2.3.	Packet loss robustness factor, DPplV	15

11.3.	Multimedia quality integration function	15

11.3.1.	Calculation of the multimedia quality, MMq	15

11.3.2.	Audiovisual quality, MMSV	15

11.3.3.	Audiovisual delay impairment factor, MMT	16

12.	Accuracy of model	16

Annex A	Methodology for deriving coefficients in video quality estimation function with respect to coding and packet-loss degradations	19

A.1 Methodology for deriving coefficients v1, v2, ..., and v7	19

A.2 Methodology for deriving coefficients v8, v9, …, and v12	20

Appendix I - Coefficients in video quality estimation function with respect to coding and packet-loss degradations	22

Appendix II - Coefficients in multimedia quality integration function.	23

# Scope

This Recommendation describes a computational model for point-to-point interactive videophone applications over IP networks that is useful as a QoE/QoS planning tool for assessing the combined effects of variations in several video and speech parameters that affect the quality of experience (QoE). This model can be used by QoE/QoS planners to help ensure that users will be satisfied with end-to-end service quality to avoid over-engineering the applications, terminals, and networks. Network, application, and terminal quality parameters of high importance to QoE/QoS planners are incorporated into this model.

The model provided in this Recommendation needs to be a flexible tool capable of providing feedback on individual qualities as well as overall quality.

This Recommendation is very different from Recommendation J.148 in terms of input parameters. In this Recommendation, audiovisual quality is calculated by using network, application, and terminal equipment parameters, whereas in Recommendation J.148, the calculation is done by using speech and video signals.

This Recommendation assumes videophone applications using dedicated videophone terminals, desktop PCs, laptop PCs, PDAs, and mobile phones. The speech bandwidth is limited to the telephone band (300-3400 Hz).

The application scenario of this Recommendation is limited to QoE/QoS planning. Other application scenarios such as quality benchmarking and monitoring are outside the scope of this Recommendation.

# References

The following ITU-T Recommendations and other references contain provisions, which, through reference in this text, constitute provisions of this Recommendation. At the time of publication, the editions indicated were valid. All Recommendations and other references are subject to revision; users of this Recommendation are therefore encouraged to investigate the possibility of applying the most recent edition of the Recommendations and other references listed below. A list of the currently valid ITU-T Recommendations is regularly published.

The reference to a document within this Recommendation does not give it, as a stand-alone document, the status of a Recommendation.

ITU-T Recommendation P.800, “Methods for subjective determination of transmission quality,” Aug. 1996.

ITU-T Recommendation P.910, “Subjective video quality assessment methods for multimedia applications,” Sep. 1999.

ITU-T Recommendation P.911, “Subjective audiovisual quality assessment methods for multimedia applications,” Dec. 1998.

ITU-T Recommendation P.920, “Interactive test methods for audiovisual communications,” May 2000.

ITU-T Recommendation G.711, “Pulse code modulation (PCM) of voice frequencies,” Nov. 1988.

ITU-T Recommendation P.833, “Methodology for derivation of equipment impairment factors from subjective listening-only tests,” Feb. 2001.

ITU-T Recommendation P.834, “Methodology for derivation of equipment impairment factors from instrumental models,” July 2002.

ITU-T Recommendation P.862, “Perceptual evaluation of speech quality (PESQ): An objective method for end-to-end speech quality assessment of narrow-band telephone networks and speech codecs,” Feb. 2001.

ITU-T Recommendation P.862.1, “Mapping function for transforming P.862 raw result scores to MOS-LQO,” Nov. 2003.

ITU-T Recommendation P.862.2, “Wideband extension to Recommendation P.862 for the assessment of wideband telephone networks and speech codecs,” Nov. 2005.

ITU-T Recommendation P.561, “In-service, non-intrusive measurement device –voice service measurements,” July 2002.

ITU-T Recommendation P.562, “Analysis and interpretation of INMD voice service measurements,” May 2004.

ITU-T Recommendation P.563, “Single ended method for objective speech quality assessment in narrow-band telephony applications,” May 2004.

ITU-T Recommendation G.107, “The E-model, a computational model for use in transmission planning,” Mar. 2005.

ITU-R Recommendation BS.1387-1, “Method for objective measurements of perceived audio quality,” 1998.

ITU-T Recommendation J.144, “Objective perceptual video quality measurement techniques for digital cable television in the presence of a full reference,” Mar. 2004.

ITU-T Recommendation J.148, “Requirements for an objective perceptual multimedia quality model,” May 2003.

ITU-T Recommendation G.113, “Transmission impairments due to speech processing,” Jan. 2001.

ITU-T Recommendation G.122, “Influence of national systems on stability and talker echo in international connections,” March 1993.

# Definitions

This Recommendation defines the following terms as shown in Table 1/G.OMV:

Table 1/G.OMV - List of definitions

| Name | Description | Unit |
| --- | --- | --- |
| Sq | Objective measurement of speech quality | - |
| Q | Speech quality index | - |
| R | Transmission rating factor | - |
| Idd | Degradation caused by pure delay in Recommendation G.107 | - |
| Idte | Degradation caused by talker echo | - |
| Ie-eff | Degradation caused by speech coding and packet loss | - |
| IeS | Speech coding distortion | - |
| BplS | Speech packet-loss robustness | - |
| PplS | Speech packet-loss rate | % |
| TELR | Talker echo loudness rating | dB |
| Vq | Objective measurement of video quality | - |
| Vqs | Subjective video quality |  |
| Icoding | Objective measurement of basic video quality accounting for coding distortion | - |
| IOfr | Objective measurement of maximum video quality at each bit rate | - |
| Ofr | Optimal frame rate that maximizes video quality at each bit rate | - |
| DFrV | Degree of video quality robustness due to frame rate reduction | - |
| DPplV | Degree of video quality robustness against packet loss | - |
| FrV | Video frame rate | fps |
| BrV | Video bit rate | kbps |
| PplV | Video packet-loss rate | % |
| bn | Video bit rate (n = 1, 2, …, N) | kbps |
| fm | Frame rate (m = 1, 2, …, M) | fps |
| Vqs(bn, fm) | Subjective video quality under conditions of bn and fm | - |
| On | Optimal frame rate (n = 1, 2, …, N) | - |
| In | Object measurement of maximum video quality at each bit rate (n = 1, 2, …, N) | - |
| Dn | Degree of video quality robustness due to frame rate reduction (n = 1, 2, …, N) | - |
| Dbnfm | Degree of video quality robustness against packet loss (n = 1, 2, …, N, m = 1, 2, …, M) | - |
| MMq | Objective measurement of overall multimedia quality accounting for influence of speech and video quality | - |
| MMSV | Audiovisual quality | - |
| MMT | Audiovisual delay impairment factor | - |
| AD | Absolute audiovisual delay | - |
| MS | Audiovisual media synchronization | - |
| TS | Speech delay | ms |
| TV | Video delay | ms |
| Sq(Vq) | Objective measurement of speech quality accounting for influence of video quality | - |
| Vq(Sq) | Objective measurement of video quality accounting for influence of speech quality | - |

# Abbreviations

ACR:	Absolute Category Rating

AEC:	Acoustic Echo Canceller

ERL:	Echo Return Loss

MOS:	Mean Opinion Score

RLR:	Receiving Loudness Rating

SLR:	Sending Loudness Rating

VGA:	Video Graphics Array (640×480 pixels)

CIF:	Common Intermediate Format (352×288 pixels)

QVGA:	Quarter Video Graphics Array (320×240 pixels)

QCIF:	Quarter CIF (176×144 pixels)

QQVGA:	Quarter Quarter VGA (160×120 pixels)

CT:	Codec type

VF:	Video Format

KFI:	Key Frame Interval

VDS:	Video Display Size

# Conventions

In this Recommendation, “Subjective quality” refers to the MOS obtained in ACR tests as defined in Recommendations P.800, P.910, P.911, and P.920, depending on the media under evaluation and evaluation context such as one-way listening/viewing and two-way interactive communication.

# Application scenario

The application scenario of this Recommendation is limited to QoE/QoS planning. Other application scenarios such as quality benchmarking and monitoring are outside the scope of this Recommendation. Table 2/G.OMV gives an overview of various Recommendations related to objective quality assessment methodologies from the viewpoints of intended application scenarios, media, and the subjective quality aspects are taken into account.

Table 2/G.OMV - Relationship of G.OMV to other ITU Recommendations for objective quality assessment

| Media | Estimated subjective quality | Application Scenario |
| --- | --- | --- |
|  |  | Benchmarking/ Intrusive monitoring | Non intrusive monitoring | Network planning |
| Speech | One way (Listening quality) | P.862/P.862.1 (Telephone band) P.862.2 (Wideband) | P.563, P.564 (Telephone band) | G.107 (Telephone band) G.107 Appendix II (Wideband) |
|  | Two way (Conversational quality) | P.CQO (Telephone-band) |  |
|  |  |  | P.561, P.562 (Telephone band) |  |
| Audio | One way (Listening quality) | BS.1387-1 |  |  |
| Video | One way (Viewing quality) | J.144 (Cable TV) *.xxx (Multimedia) | *.yyy (Cable TV) *.zzz (Multimedia) |  |
| Speech/Audio and Video | One way | J.148 (Multimedia) | G.OMVS (Video streaming) |
|  | Two way |  | G.OMV (Videophone) |
| Data | One way | G.Chirp (Web browsing) |  | G.1030 Annex A (Web browsing) |

# Framework

The framework of the opinion model treated in this Recommendation is illustrated in Figure 1/G.OMV. Its input parameters are video and speech quality parameters that are considered important in QoE/QoS planning. The model consists of three functions: video quality estimation, speech quality estimation, and multimedia quality integration functions. The degradation caused by pure delay is considered only in the multimedia quality integration function.

This Recommendation provides basic formulas for the above functions. The outputs from the model are multimedia quality (MMq), video quality influenced by speech quality (Vq(Sq)), and speech quality influenced by video quality (Sq(Vq)).

The model assumes some specific evaluation conditions for terminals, environments, and evaluation contexts, and quality estimation under other evaluation conditions is currently under study. In that sense, these are the limitations of the current Recommendation.

It should be noted that the effects of a codec on subjective quality are heavily dependent on its implementation. In particular, the quality of a video codec cannot be estimated based simply on the information about the coding technology (e.g., MPEG4) used in the system under test, although specifying the implementation of a speech codec based on the standard (e.g., Recommendation G.711) employed in the system under test is relatively easily. For example, there are a number of different implementations for MPEG4 codecs due to variations in coding-parameter settings and decoder characteristics. Therefore, the coefficients of video and speech quality estimation functions in this Recommendation were determined by referring to tables prepared in advance for each video and speech codec. A coefficient database for video is illustrated in Figure 2/G.OMV. Such tables can be constructed by using the methodology provided in Annex A for video and by using Recommendations P.833 or P.834 for speech.

Figure 1/G.OMV - Framework of multimedia communication quality assessment model

Figure 2/G.OMV -Determination of coefficients that depend on codec implementation

# Model assumptions

This section describes conditions that the model assumes for terminals, environments, and evaluation contexts.

# Speech-related assumptions

# Terminal factors

For hands-free terminals, acoustic echo is assumed to be appropriately eliminated by applying AEC, and it does not cause any additional degradation of speech signals.

If a noise canceller and/or an automatic gain controller is applied, it is also assumed that the device works without causing any additional degradation of speech signals.

# Environmental factors

The assumed ambient noise is Hoth noise at 35 dB(A). Although other ambient noise conditions can be assumed to exist, especially in mobile applications, dealing with such conditions is for further study.

# Video-related assumptions

# Terminal factors

The model estimates video quality when that is evaluated by using a monitor whose specifications are listed in Table 3/G.OMV. Although this Recommendation treats video-telephony services using dedicated videophone terminals, desktop PCs, laptop PCs, PDAs, and mobile phones, the effects of terminal characteristics with specifications other than those shown in Table 3/G.OMV are still under study.

NOTE: Specifications of monitors used in most PDAs and mobile phones are less than those in Table 3/G.OMV. Thus, the model’s predictions are often more sensitive than the users’ opinions. From the viewpoint of QoE/QoS planning, which is the intended application of this Recommendation, the assumptions described in Table 3/G.OMV are reasonable because they ensures accurate planning.

Table 3/G.OMV - Assumptions about monitor characteristics

| Monitor specifications | Value |
| --- | --- |
| Diagonal length | 2-10 inches |
| Native resolution | Native resolution |
| Dot pitch | < 0.30 |
| Color temperature | 6500 K |
| Bit depth | 8 bits/color |
| Refresh rate | > 60 Hz |
| Brightness | 100-300 cd/m2 |

“Diagonal length” refers to the image size on the monitor screen.

# Environmental factors

The assumed ambient illuminance is 500 lux. The model assumes video content to be a so-called “bust shot” with grey background, but that does not consider moving backgrounds in mobile applications, nor camera shaking due to hand movement.

# Task-related assumptions

Conversational tasks in subjective quality evaluation affect the resultant conversational quality. In particular, the effects of delay have great impact on the interactivity in a conversation. Therefore, it is desirable that the model takes into account the kind of task assumed in the service scenario. However, the only task currently considered in the model is “free conversation.” Modelling of conversational tasks other than free conversation is for further study.

# Model inputs

This section describes the input parameters used in the model.

# Speech quality parameters

The parameters described in this section are similar to those in Recommendation G.107. Speech quality parameters not listed in this section are assumed to take their default values as defined in Recommendation G.107.

# Speech delay (TS [ms])

This refers to end-to-end, one-way delay in speech. Considering the delay in terminals, such as processing delay and jitter-buffer delay is extremely important. An input value of TS must be less than 1000 ms.

# Speech coding distortion (IeS)

Distortion due to speech coding needs to be quantified as IeS. The IeS values for ITU-T standard codecs are provided in ITU-T Recommendation G.113, Appendix I.

# Speech packet-loss robustness (BplS)

Packet-loss robustness of a speech codec should be quantified as BplS. The BplS values for ITU-T standard codecs are provided in ITU-T Recommendation G.113 Appendix I.

# Speech packet-loss rate (PplS [%])

This refers to the end-to-end packet-loss rate in speech. Considering the packet loss in a terminal-jitter buffer and the packet loss in networks is extremely important.

# Talker echo loudness rating (TELR)

This is the sum of SLR, RLR, and ERL in the talker-echo path. SLR and RLR are defined in Recommendation P.79, and ERL is defined in Recommendation G.122.

# Video quality parameters

# Video delay (TV [ms])

This refers to end-to-end one-way delay in video. Considering the delay in terminals, such as processing delay and jitter-buffer delay is extremely important. An input value of TV must be less than 1000 ms.

# Video codec specifications

The model’s coefficients for coding and packet-loss distortion are determined by looking up the coefficient database that has the following information (see Fig. 2/G.OMV).

# Codec type and implementation

This information is used to identify the specific implementation of a video codec under evaluation so that the model can consider the performance divergence due to differences in implementation of a video codec.

# Spatial resolution

This parameter refers not to the actual/effective spatial resolution reflecting the performance of a camera and/or a display but to the theoretical spatial resolution employed in a codec. It is better to measure the effective spatial resolution, if possible, and reflect it in the quality estimation. Reference [1] provides a methodology for measuring the effective spatial resolution. However, how to reflect such results in the quality estimation model is still under study.

The model handles video whose size is between QQVGA and VGA.

# Key-frame interval

This is the time interval in which video is coded solely from intra frame information. This affects the effectiveness of video coding (i.e., quality vs. video bit rate) and the robustness against packet-loss degradation.

# Video packet-loss rate (PplV [%])

This refers to end-to-end packet-loss rate in video. Considering the packet loss in a terminal-jitter buffer and the packet loss in networks is extremely important.

# Video frame rate (FrV [fps])

This refers to the frame rate used in an encoder and does not reflect frame repetition used at a decoder, for example, in the case of packet loss. This Recommendation assumes that the range of the frame rate is from 1 to 30 fps.

# Video bit rate (BrV [kbps])

This refers to the video bit rate at an encoder.

# Model outputs

The model outputs are the overall multimedia quality index (MMq), speech quality accounting for the influence of video quality (Sq(Vq)), and video quality accounting for the influence of speech quality (Vq(Sq)).

NOTE: The determination of Vq(Sq) and Sq(Vq) is for further study.

# Model description

### Speech quality estimation function

First, the speech quality parameters defined in Section ‎9.1 are mapped to a quality index Q as follows:

.	(1)

NOTE: The quality index Q is equivalent to the transmission rating factor R defined in Recommendation G.107, but the definition in this Recommendation is simplified due to the smaller number of input parameters.

NOTE: Quality evaluation characteristics in multimedia applications might be different from those expected in telephony applications. Therefore, the model described in this subsection is a provisional method. The applicability of Recommendation G.107 in such applications is still under study.

NOTE: The delay quality is considered separately in the multimedia quality integration function (see Fig. 1/G.OMV), so Eq. (1) excludes Idd, which represents the degradation caused by pure delay in Recommendation G.107.

Idte represents the degradation caused by talker echo and is defined as

,	(2)

where

and	(3)

.	(4)

Ie-eff represents the degradation caused by speech coding, and packet loss and is defined as

.	(5)

Speech quality Sq is defined as a function of the quality index Q.

For Q ( 0:	,

For 0 ( Q ( 100:	,	(6)

For Q ( 100:	.

### Video quality estimation function

### Calculation of video quality, Vq

Video quality Vq is calculated using the video quality parameters defined in Section 9.2. Vq is expressed as

,							(V-1)

where Icoding represents the basic video quality affected by the coding distortion under a combination of video bit rate (BrV [kbps]) and video frame rate (FrV [fps]), and the packet loss robustness factor DPplV expresses the degree of video quality robustness due to packet loss where PplV [%] represents the packet loss rate.

### Basic video quality affected by coding distortion, Icoding

The basic video quality affected by coding distortion Icoding is expressed as

.					(V-2)

The Ofr is an optimal frame rate that maximizes the video quality at each video bit rate (BrV) and is expressed as

, v1 and v2: const.				(V-3)

When FrV = Ofr, Icoding = IOfr, IOfr represents the maximum video quality at each video bit rate (BrV) and is expressed as

, v3, v4, and v5: const.		(V-4)

DFrV represents the degree of video quality robustness due to frame rate (FrV) and is expressed as

, v6 and v7: const.				(V-5)

Coefficients v1, v2, ..., and v7 are determined by codec type, video format, key frame interval, and video display size (See Appendix I to this Recommendation).

### Packet loss robustness factor, DPplV

The packet loss robustness factor DPplV represents the degree of video quality robustness against packet loss and is expressed as

,		(V-6)

where PplV represents the packet loss rate.

Coefficients v8, v9, ..., and v12 are determined by codec type, video format, key frame interval, and video display size (See Appendix I to this Recommendation).

### Multimedia quality integration function

### Calculation of the multimedia quality, MMq

The multimedia quality MMq is calculated using speech quality Sq, video quality Vq, speech delay TS, and video delay TV. MMq is expressed as

,			(MM-1)

where MMSV represents audiovisual quality, MMT represents the audiovisual delay impairment factor, and coefficients m1, m2, ..., and m4 are dependent on video display size and conversational task.

### Audiovisual quality, MMSV

The audiovisual quality MMSV is expressed as

.					(MM-2)

Coefficients m5, m6, ..., and m8 are dependent on video display size and conversational task.

### Audiovisual delay impairment factor, MMT

The MMT represents the degree of the audiovisual quality degradation due to audiovisual delay and synchronization and is expressed as

,							(MM-3)

,								(MM-4)

, and				(MM-5)

,				(MM-6)

where AD represents the absolute audiovisual delay and MS represents the audiovisual media synchronization.

Coefficients m9, m10, ..., and m14 are dependent on video display size and conversational task.

NOTE: Provisional values of mi that assumes VGA as a video format, 8.5 inches as video display size, free conversation as a conversational task are provided in Appendix II to this Recommendation.

NOTE: Currently, the derivation of Vq(Sq) and Sq(Vq), which are video quality affected by speech quality and vice verse, is under study.

# Accuracy of model

The correlation between subjective quality and estimated quality is used for estimating the accuracies of the functions that are the speech quality estimation function, video quality estimation function, and multimedia quality integration function. The correlation c should be calculated over all the test data sets as follows:

,

where V is the number of test data sets, and the mean values of the data sets are calculated as follows:

and

,

where 	xv represents the estimated quality of test data and

yv represents the subjective quality of test data.

The accuracy of the speech quality estimation function, which is presented in ITU-T Recommendation G.107, is described in [2].

The accuracy of the video quality estimation function was verified by the following manner:

  - The validity of the forms ((V-1) – (V-6)) was verified by using the subjective quality database employing H.264 and MPEG4 codecs (DB#1 – DB#4 in Table 12-1/G.OMV). Here, the coefficients v1, v2, ..., and v12 were optimized for each database. The cross-correlation is about 0.975 on average [3][4].

  - The validity of the optimized coefficients v1, v2, ..., and v12 was verified by applying them to unknown data. This was done by optimizing the coefficients by DB#5 and DB#7, and applying them to DB#6 and DB#8. The cross-correlation is about 0.955 on average [5].

Table 12-1/G.OMV - Verification of form of video quality estimation function for various terminals

|  | cV | CT | VF | KFI [s] | VDS [inches] |
| --- | --- | --- | --- | --- | --- |
| DB#1 | 0.967 [3] | H.264 | QVGA | 1 | 4.2 |
| DB#2 | 0.987 [3], [4] | MPEG4 | QVGA | 1 | 4.2 |
| DB#3 | 0.973 [4] | MPEG4 | QVGA | 1 | 8.5 |
| DB#4 | 0.972 [4] | MPEG4 | VGA | 1 | 8.5 |

Table 12-2/G.OMV - Accuracy of video quality estimation function

|  | cV | CT | VF | KFI [s] | VDS [inches] |
| --- | --- | --- | --- | --- | --- |
| DB#5 | 0.951 [5] | MPEG4 | QVGA | 1 | 4.2 |
| DB#6 | 0.961 [5] | MPEG4 | QVGA | 1 | 4.2 |
| DB#7 | 0.958 [5] | MPEG4 | QQVGA | 1 | 2.1 |
| DB#8 | 0.949 [5] | MPEG4 | QQVGA | 1 | 2.1 |

The accuracy of the multimedia integration function was verified as follows.

The video and speech quality (Vq and Sq) were estimated by the speech and video quality estimation functions described in Sections 11.1 and 11.2, respectively, in this Recommendation. Next, we fed these values and video and speech delay values (TV and TS) into the multimedia integration function given in 11.3. By comparing the estimated multimedia quality with multimedia quality obtained by a conversational subjective test, we evaluated the validity of the multimedia quality integration function.

We used a G.711 codec without a packet-loss concealment algorithm as a speech codec. The speech packet-loss rate varied from 0 to 10%. No echo was introduced in the evaluation system. The video codec was MPEG4, and the bit rate was 2 Mb/s and 1 Mb/s for QVGA and QQVGA, respectively. The video packet-loss rate varied from 0 to 5%. The video frame rate was between 2 to 30 f/s. One-way delay varied from 167 to 1000 ms, and was controlled for speech and video separately to evaluate the effects of lip synchronization.

The subjective testing method was 5-grade conversational ACR defined in Recommendation P.910. There were 32 subjects. The viewing distances were 50 and 80 cm for QQVGA and QVGA, respectively.

The estimation accuracy of the G.OMV model, including speech and video quality estimation functions, is demonstrated in Table 12-3.

NOTE: These databases were used for optimizing the coefficients of the multimedia quality integration function under each VDS condition. The coefficients are provided in Appendix II to this Recommendation.

Table 12-3/G.OMV - Accuracy of multimedia estimation model

|  | cMM | Speech codec | Video codec | VF | KFI [s] | VDS [inches] |
| --- | --- | --- | --- | --- | --- | --- |
| DB#10 | 0.87 | G.711 | MPEG4 @ 2Mb/s | QVGA | 1 | 4.2 |
| DB#11 | 0.90 | G.711 | MPEG4 @ 1Mb/s | QQVGA | 1 | 2.1 |

# Annex A	Methodology for deriving coefficients in video quality estimation function with respect to coding and packet-loss degradations

### A.1 Methodology for deriving coefficients v1, v2, ..., and v7

Using the subjective video quality MOS, which is called Vqs hereafter, for various video bit rate (BrV) and video frame rate (FrV) conditions, coefficients v1, v2, ..., and v7 are calculated in the following four steps.

### Step A.1.1: Calculation of values IOfr, Ofr, and Dfr

1) If we employ M different frame rates for each video bit rate condition bn, we obtain Table A.1.1/G.OMV.

Table A.1.1/G.OMV - Relationships among BrV, FrV, and Vq

| BrV | FrV | Vq |
| --- | --- | --- |
| bn | f1 | Vqs(bn,f1) |
| bn | f2 | Vqs(bn,f2) |
| ... | ... | ... |
| bn | fm | Vqs(bn,fm) |
| ... | ... | ... |
| bn | fM | Vqs(bn,fM) |

NOTE: M represents the number of frame rate conditions.

NOTE: Vqs(bn, fm) represents the MOS under the condition with a video bit rate of bn and a frame rate of fm.

2) By applying the data set in Table A.1.1/G.OMV to Eq. (V-1), Ofr, IOfr, and Dfr are approximated for each video bit rate bn based on the Least Square Approximation (LSA). As a result, we can obtain Table A.1.2/G.OMV.

Table A.1.2/G.OMV - Relationship between BrV, IOfr, Ofr, and Dfr

| BrV | Ofr | IOfr | Dfr |
| --- | --- | --- | --- |
| b1 | O1 | I1 | D1 |
| b2 | O2 | I2 | D2 |
| ... | ... | ... | ... |
| bn | On | In | Dn |
| ... | ... | ... | ... |
| bN | ON | IN | DN |

Note: N represents the number of video bit rate conditions.

### Step A.1.2: Calculation of coefficients v1 and v2

By applying bn and On for n = 1, 2, ..., N in Table A.1.2/G.OMV to Eq. (V-3), coefficients v1 and v2 are approximated based on the LSA.

### Step A.1.3: Calculation of coefficients v3, v4, and v5

By applying bn and In for n = 1, 2, ..., N in Table A.1.2/G.OMV to Eq. (V-4), coefficients v3, v4, and v5 are approximated based on the LSA.

### Step A.1.4: Calculation of coefficients v6 and v7

By applying bn and Dn for n = 1, 2, ..., N to Eq. (V-5), coefficients v6 and v7 are approximated based on the LSA.

### A.2 Methodology for deriving coefficients v8, v9, …, and v12

Using the subjective video quality (Vqs) related to video bit rate (BrV), video frame rate (FrV), and video packet loss rate (PplV), coefficients v8, v9, …, and v12 are calculated in the following four steps.

NOTE: The subjective quality characteristics of packet-loss degradation often depend on the duration of video sequences used in a subjective test, so one should use video sequences that have a reasonable length (e.g., 1 min.).

### Step A.2.1: Calculation of values DPplV

By applying Icoding, which is calculated by using the coefficients derived in A.1, and subjective video quality (Vqs) to Eq. (V-1), the packet loss robustness factor DPplV is approximated based on the LSA for each combination of BrV and FrV, as shown in Table A.2.

Table A.2/G.OMV - Relationships among video bit rate, video frame rate, and DPplv

| DPplV | FrV |
| --- | --- |
|  | f1 | f2 |  | fm |  | fM |
| BrV | b1 | Db1f1 | Db1f2 | ... | ... | ... | Db1fM |
|  | b2 | Db2f1 | Db2f2 | ... | ... | ... | Db2fM |
|  | ... | ... | ... | ... | ... | ... | ... |
|  | bn | Dbnf1 | Dbnf2 | ... | Dbnfm | ... | DbnfM |
|  | ... | ... | ... | ... | ... | ... | ... |
|  | bN | DbNf1 | DbNf2 | ... | ... | ... | DbNfM |

Note: N represents the number of video bit rate conditions.

Note: M represents the number of video frame rate conditions.

Note: Dbnfm indicates a temporary value of the packet loss robustness factor DPplV for a video bit rate of bn and a frame rate of fm.

### Step A.2.2: Calculation of coefficient v8

By applying fm and DPplV = Db1fm for m = 1, 2, ..., M to Eq. (A-1), coefficients a, b, and v8 are approximated based on the LSA.

(A-1)

### Step A.2.3: Calculation of coefficient v9

By applying bn and DPplV = Dbif1, for n = 1, 2, ..., N to Eq. (A-2), coefficients c, d, and v9 are approximated based on the LSA.

(A-2)

NOTE: Coefficients a, b, c, and d are temporary and never used in the following calculation.

### Step A.2.4: Calculation of coefficients v10, v11, and v12

By applying v8, v9, DPplV = Dbnfm, BrV = bn, and FrV = fm for n = 1, 2, ..., N and m = 1, 2, ..., M to Eq. (V-6), coefficients v10, v11, and v12 are approximated based on LSA.

# Appendix I - Coefficients in video quality estimation function with respect to coding and packet-loss degradations

This Appendix provides two examples of the coefficient table used for the video quality estimation function. Table I.1/G.OMV summarizes the conditions under which each coefficient table was constructed.

NOTE: The coefficient tables given in this Appendix cannot be applied to arbitrary MPEG4 codecs. That is dependent on the implementation and setting of codec, as noted in Section 7 of this Recommendation. Therefore, if one needs to construct a coefficient table for a specific codec, he/she needs to follow the procedure described in Annex A to this Recommendation.

Table I.1/G.OMV - Conditions for deriving coefficient tables

| Factors | # 1 | # 2 |
| --- | --- | --- |
| Codec type | MPEG4 | MPEG4 |
| Video format | QVGA | QQVGA |
| Key frame interval (s) | 1 | 1 |
| Video display size (inch) | 4.2 | 2.1 |

The resultant coefficient tables are provided in Table I.2/G.OMV.

NOTE: These coefficient tables were constructed based on subjective tests in which video sequences with a duration of 10 s were used. Therefore, the quality estimation based on these coefficients may result in optimistic evaluation in comparison with that of the video quality of longer video sequences in evaluating the effects of packet loss.

Table I.2/G.OMV - Coefficient table for video quality estimation model

| Coefficients | # 1 | # 2 |
| --- | --- | --- |
| v1 | 3.759 | 3.461 |
| v2 | 184.1 | 111.9 |
| v3 | 1.161 | 2.091 |
| v4 | 1.431 | 7.160 |
| v5 | 2.228 × 10–2 | 2.215 × 10–2 |
| v6 | 1.446 | 1.382 |
| v7 | 3.881 × 10–4 | 5.881 × 10–4 |
| v8 | 467.4 | 113.9 |
| v9 | 2.116 | 0.8401 |
| v10 | 2.736 | 6.047 |
| v11 | 4.170 | 10.87 |
| v12 | 15.28 | 46.87 |

# Appendix II - Coefficients in multimedia quality integration function.

This Appendix provides two coefficient tables used for the multimedia quality integration function. As stated in Section 11.2, the coefficients are dependent on the video display size and conversational task. The coefficient tables in this Appendix assume two different video display sizes, which are 4.2, and 2.1 [inch]. They were derived by using “free conversation” as a conversational task.

Table II.1/G.OMV - Coefficients of multimedia quality integration model

| Coefficients | 4.2 inch | 2.1 inch |
| --- | --- | --- |
| m1 | 1.907 | 2.902 |
| m2 | 4.785 × 10–1 | 1.129 |
| m3 | -3.038 × 10–1 | -5.416 × 10–1 |
| m4 | -1.350 | -4.005 |
| m5 | -1.444 × 10–1 | -1.764 × 10–1 |
| m6 | 1.858 × 10–1 | 3.063 × 10–1 |
| m7 | 1.540 × 10–1 | 1.478 × 10–1 |
| m8 | 1.173 | 5.960 × 10–1 |
| m9 | -3.235 × 10–4 | -1.251 × 10–4 |
| m10 | 3.915 | 3.763 |
| m11 | 1.377 × 10–3 | 1.040× 10–3 |
| m12 | 0.000 | 0.000 |
| m13 | 1.043 × 10–3 | 9.729 × 10–4 |
| m14 | 3.015 × 10–2 | 1.702 × 10–2 |

# Bibliography

- P. Bijl and J. M. Valeton, “Guidelines for accurate TOD measurement,” Proc. SPIE. 3701, pp.14-25, 1999.

S. Moeller, Assessment and Prediction of Speech Quality in Telecommunications. Boston, MA: Kluwer, 2000.

K. Yamagishi and T. Hayashi, “Verification of Video Quality Opinion Model for Videophone Services,” 2nd ISCA Tutorial & Research Workshop on Perceptual Quality of Systems, pp.143 - 148, Sep. 2006.

K. Yamagishi and T. Hayashi, “Opinion Model for Estimating Video Quality of Videophone Services,” IEEE GLOBECOM 2006, QRP08-1, Nov. 2006.

ITU-T Contribution C-34, “Verification Of Video Quality Estimation Model For Videophone Services (NTT),” Jan. 2007.

______________