Appendix VI.  Individual Test Designs

The compiler of these test designs (GWC) has tried to use the same scale for packet loss ratio (PLR) for all designs.  The scale used is a nominal random packet loss rate without error correction or concealment.

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| V01 | Psytechnics | 0 | None | 4096 nominal | 25 | 0 | reference |
| V01 | Psytechnics | 1 | MPEG4 | 2000 | 25 | 0 |  |
| V01 | Psytechnics | 2 | VC1 | 1000 | 25 | 0 |  |
| V01 | Psytechnics | 3 | MPEG4 | 1000 | 25 | 0 |  |
| V01 | Psytechnics | 4 | H264 | 1000 | 25 | 0 |  |
| V01 | Psytechnics | 5 | VC1 | 512 | 25 | 0 |  |
| V01 | Psytechnics | 6 | RV10 | 512 | 25 | 0 |  |
| V01 | Psytechnics | 7 | MPEG4 | 512 | 25 | 0 |  |
| V01 | Psytechnics | 8 | H264 | 512 | 25 | 0 |  |
| V01 | Psytechnics | 9 | VC1 | 320 | 12.5 | 0 |  |
| V01 | Psytechnics | 10 | RV10 | 320 | 12.5 | 0 |  |
| V01 | Psytechnics | 11 | MPEG4 | 320 | 12.5 | 0 |  |
| V01 | Psytechnics | 12 | VC1 | 128 | 5 | 0 |  |
| V01 | Psytechnics | 13 | RV10 | 128 | 5 | 0 |  |
| V01 | Psytechnics | 14 | MPEG4 | 2000 | 25 | 2 | random |
| V01 | Psytechnics | 15 | MPEG4 | 2000 | 25 | 2 | bursty |
| V01 | Psytechnics | 16 | MPEG4 | 2000 | 25 | 5 | bursty |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| V02 | NTT | 0 | None | 4096 nominal | 30 | 0 | reference |
| V02 | NTT | 1 | MPEG4 | 2000 | 30 | 0 |  |
| V02 | NTT | 2 | MPEG4 | 1000 | 30 | 0 |  |
| V02 | NTT | 3 | MPEG4 | 1000 | 15 | 0 |  |
| V02 | NTT | 4 | MPEG4 | 1000 | 15 | 0 |  |
| V02 | NTT | 5 | MPEG4 | 320 | 10 | 0 |  |
| V02 | NTT | 6 | MPEG4 | 128 | 15 | 0 |  |
| V02 | NTT | 7 | MPEG4 | 128 | 10 | 0 |  |
| V02 | NTT | 8 | MPEG4 | 128 | 5 | 0 |  |
| V02 | NTT | 9 | MPEG4 | 4096 | 30 | 1 |  |
| V02 | NTT | 10 | MPEG4 | 4096 | 30 | 2 |  |
| V02 | NTT | 11 | MPEG4 | 4096 | 30 | 3 |  |
| V02 | NTT | 12 | MPEG4 | 1024 | 30 | 1 |  |
| V02 | NTT | 13 | MPEG4 | 1024 | 30 | 2 |  |
| V02 | NTT | 14 | MPEG4 | 1024 | 30 | 4 |  |
| V02 | NTT | 15 | MPEG4 | 320 | 30 | 2 |  |
| V02 | NTT | 16 | MPEG4 | 320 | 30 | 4 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| V03 | NTT | 0 | None | 4096 nominal | 30 | 0 | reference |
| V03 | NTT | 1 | RV10 | 4096 | 30 | 0 |  |
| V03 | NTT | 2 | RV10 | 1024 | 30 | 0 |  |
| V03 | NTT | 3 | RV10 | 1024 | 15 | 0 |  |
| V03 | NTT | 4 | RV10 | 320 | 15 | 0 |  |
| V03 | NTT | 5 | RV10 | 320 | 10 | 0 |  |
| V03 | NTT | 6 | RV10 | 128 | 15 | 0 |  |
| V03 | NTT | 7 | RV10 | 128 | 10 | 0 |  |
| V03 | NTT | 8 | RV10 | 128 | 5 | 0 |  |
| V03 | NTT | 9 | RV10 | 4096 | 30 | 1 |  |
| V03 | NTT | 10 | RV10 | 4096 | 30 | 2 |  |
| V03 | NTT | 11 | RV10 | 4096 | 30 | 4 |  |
| V03 | NTT | 12 | RV10 | 1024 | 30 | 1 |  |
| V03 | NTT | 13 | RV10 | 1024 | 30 | 2 |  |
| V03 | NTT | 14 | RV10 | 1024 | 30 | 4 |  |
| V03 | NTT | 15 | RV10 | 320 | 15 | 2 |  |
| V03 | NTT | 16 | RV10 | 320 | 15 | 4 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| V04 | NTT | 0 | None | 4096 nominal | 30 | 0 | reference |
| V04 | NTT | 1 | H264 | 4096 | 30 | 0 |  |
| V04 | NTT | 2 | H264 | 1024 | 30 | 0 |  |
| V04 | NTT | 3 | H264 | 1024 | 15 | 0 |  |
| V04 | NTT | 4 | H264 | 320 | 15 | 0 |  |
| V04 | NTT | 5 | H264 | 320 | 10 | 0 |  |
| V04 | NTT | 6 | H264 | 128 | 15 | 0 |  |
| V04 | NTT | 7 | H264 | 128 | 10 | 0 |  |
| V04 | NTT | 8 | H264 | 128 | 5 | 0 |  |
| V04 | NTT | 9 | H264 | 4096 | 30 | 1 |  |
| V04 | NTT | 10 | H264 | 4096 | 30 | 2 |  |
| V04 | NTT | 11 | H264 | 4096 | 30 | 4 |  |
| V04 | NTT | 12 | H264 | 1024 | 30 | 1 |  |
| V04 | NTT | 13 | H264 | 1024 | 30 | 2 |  |
| V04 | NTT | 14 | H264 | 1024 | 30 | 4 |  |
| V04 | NTT | 15 | H264 | 1024 | 15 | 2 |  |
| V04 | NTT | 16 | H264 | 1024 | 15 | 4 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| V05 | Yonsei | 0 | None | 4096 nominal | 30 | 0 | reference |
| V05 | Yonsei | 1 | H264 | 128 | 15 | 0 | QuickTime 7.1 |
| V05 | Yonsei | 2 | H264 | 320 | 15 | 0 | QuickTime 7.1 |
| V05 | Yonsei | 3 | H264 | 704 | 30 | 0 | QuickTime 7.1 |
| V05 | Yonsei | 4 | H264 | 1500 | 30 | 0 | QuickTime 7.1 |
| V05 | Yonsei | 5 | H264 | 3000 | 30 | 0 | QuickTime 7.1 |
| V05 | Yonsei | 6 | MPEG4 | 128 | 15 | 0 | QuickTime 7.1 |
| V05 | Yonsei | 7 | MPEG4 | 320 | 15 | 0 | QuickTime 7.1 |
| V05 | Yonsei | 8 | MPEG4 | 704 | 30 | 0 | QuickTime 7.1 |
| V05 | Yonsei | 9 | MPEG4 | 1500 | 30 | 0 | QuickTime 7.1 |
| V05 | Yonsei | 10 | MPEG4 | 3000 | 30 | 0 | QuickTime 7.1 |
| V05 | Yonsei | 11 | RV10 | 128 | 15 | 0 | Real Producer 11 |
| V05 | Yonsei | 12 | RV10 | 704 | 30 | 0 | Real Producer 11 |
| V05 | Yonsei | 13 | RV10 | 3000 | 30 | 0 | Real Producer 11 |
| V05 | Yonsei | 14 | VC1 | 320 | 15 | 0 | Media Encoder 9 |
| V05 | Yonsei | 15 | VC1 | 704 | 30 | 0 | Media Encoder 9 |
| V05 | Yonsei | 16 | VC1 | 1500 | 30 | 0 | Media Encoder 9 |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| V06 | Yonsei | 0 | None | 4096 nominal | 30 | 0 | reference |
| V06 | Yonsei | 1 | MPEG4 | 128 | 15 | 5 | QuickTime 7.1 |
| V06 | Yonsei | 2 | MPEG4 | 320 | 15 | 2 | QuickTime 7.1 |
| V06 | Yonsei | 3 | MPEG4 | 704 | 30 | 0 | QuickTime 7.1 |
| V06 | Yonsei | 4 | MPEG4 | 1500 | 30 | 0 | QuickTime 7.1 |
| V06 | Yonsei | 5 | MPEG4 | 3000 | 30 | 1 | QuickTime 7.1 |
| V06 | Yonsei | 6 | H264 | 128 | 15 | 0 | QuickTime 7.1 |
| V06 | Yonsei | 7 | H264 | 320 | 15 | 0 | QuickTime 7.1 |
| V06 | Yonsei | 8 | H264 | 1500 | 30 | 0 | QuickTime 7.1 |
| V06 | Yonsei | 9 | H264 | 3000 | 30 | 0 | QuickTime 7.1 |
| V06 | Yonsei | 10 | H264 | 704 | 30 | 7 | QuickTime 7.1 |
| V06 | Yonsei | 11 | RV10 | 128 | 15 | 0 | Real Producer 11 |
| V06 | Yonsei | 12 | RV10 | 704 | 30 | 0 | Real Producer 11 |
| V06 | Yonsei | 13 | RV10 | 3000 | 30 | 0 | Real Producer 11 |
| V06 | Yonsei | 14 | VC1 | 320 | 15 | 0 | Media Encoder 9 |
| V06 | Yonsei | 15 | VC1 | 704 | 30 | 0 | Media Encoder 9 |
| V06 | Yonsei | 16 | VC1 | 1500 | 30 | 0 | Media Encoder 9 |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| V07 | Opticom | 0 | None | 4096 nominal | 25 | 0 | reference |
| V07 | Opticom | 1 | H264 | 1024 | 25 | 0 |  |
| V07 | Opticom | 2 | H264 | 512 | 25 | 0 |  |
| V07 | Opticom | 3 | H264 | 512 | 12.5 | 0 |  |
| V07 | Opticom | 4 | H264 | 256 | 12.5 | 0 |  |
| V07 | Opticom | 5 | H264 | 256 | 8.33 | 0 |  |
| V07 | Opticom | 6 | MPEG4 | 1024 | 25 | 0 |  |
| V07 | Opticom | 7 | MPEG4 | 1024 | 12.5 | 0 |  |
| V07 | Opticom | 8 | MPEG4 | 512 | 12.5 | 0 |  |
| V07 | Opticom | 9 | MPEG4 | 512 | 8.33 | 0 |  |
| V07 | Opticom | 10 | MPEG4 | 256 | 8.33 | 0 |  |
| V07 | Opticom | 11 | JPEG2000 | 1024 | 25 | 0 |  |
| V07 | Opticom | 12 | JPEG2000 | 1024 | 12.5 | 0 |  |
| V07 | Opticom | 13 | MPEG4 | 1024 | 12.5 | 1 |  |
| V07 | Opticom | 14 | MPEG4 | 1024 | 12.5 | 3 |  |
| V07 | Opticom | 15 | MPEG4 | 1024 | 12.5 | 1 |  |
| V07 | Opticom | 16 | MPEG4 | 1024 | 12.5 | 0.5 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| V08 | SwissQual | 0 | None | 4096 nominal | 25 | 0 | reference |
| V08 | SwissQual | 1 | H264 | 2048 | 25 | 0 |  |
| V08 | SwissQual | 2 | H264 | 512 | 25 | 0 |  |
| V08 | SwissQual | 3 | H264 | 256 | 25 | 0 |  |
| V08 | SwissQual | 4 | H264 | 512 | 12.5 | 0 |  |
| V08 | SwissQual | 5 | H264 | 512 | 8.3 | 0 |  |
| V08 | SwissQual | 6 | H264 | 256 | 12.5 | 0 |  |
| V08 | SwissQual | 7 | H264 | 512 | 25 | 0.5 | 5% freeze |
| V08 | SwissQual | 8 | H264 | 512 | 25 | 1 | 10% freeze |
| V08 | SwissQual | 9 | H264 | 512 | 25 | 2.5 | 25% freeze |
| V08 | SwissQual | 10 | H264 | 512 | 25 | 0.125 |  |
| V08 | SwissQual | 11 | H264 | 512 | 25 | 0.5 |  |
| V08 | SwissQual | 12 | MPEG4 | 2048 | 25 | 0 |  |
| V08 | SwissQual | 13 | MPEG4 | 512 | 25 | 0 |  |
| V08 | SwissQual | 14 | MPEG4 | 256 | 25 | 0 |  |
| V08 | SwissQual | 15 | MPEG4 | 512 | 8.3 | 0 |  |
| V08 | SwissQual | 16 | H264 | 512 | 25 | 0 | 5 key frames/sec |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| V09 | NTIA | 0 | H.264 | 4096 nominal | 29.9 | 0 | Reference |
| V09 | NTIA | 1 | H.264 | 512 | 7.1 | 0 |  |
| V09 | NTIA | 2 | H.264 | 768 | 7.5 | 0.3 | 3% random packet loss, error concealment |
| V09 | NTIA | 3 | H.264 | 256 | 18.3 | 0.5 | 5% random packet loss, error concealment |
| V09 | NTIA | 4 | H.264 | 384 | 18.1 | 0 |  |
| V09 | NTIA | 5 | mpeg4 | VBR (3800) | 14.1 | 0.2 | up to 4 mbits/s including FEC bandwidth, burst packet loss, CIF |
| V09 | NTIA | 6 | H.261 | VBR (1800) | 14.5 | 0.2 | up to 2 mbits/s including FEC bandwidth, burst error |
| V09 | NTIA | 7 | H.264 | VBR (1800) | 26.9 | 0 | up to 2 mbits/s including FEC bandwidth |
| V09 | NTIA | 8 | H.264 | 1536 | 29.7 | 0.1 | 1/2 clips have 0.2% randomly distributed packet loss |
| V09 | NTIA | 9 | H.264 | 704 | 29.3 | 0.1 | 1/2 clips have 0.2% randomly distributed packet loss |
| V09 | NTIA | 10 | H.264 | 448 | 27 | 0 | on one clip, decoder cannot keep up with frame rate & displays bars briefly |
| V09 | NTIA | 11 | MPEG-2 | 1000 | 28.6 | 0.25 | 1/2 clips have 0.5% randomly distributed packet loss |
| V09 | NTIA | 12 | MPEG-2 | 512 | 20.1 | 0 |  |
| V09 | NTIA | 13 | H.261 | 2000 | 20 | 0 |  |
| V09 | NTIA | 14 | H.261 | 384 | 7.1 | 2 | burst errors, CIF resolution |
| V09 | NTIA | 15 | H.263 | 256 | 22.5 | 0 | QCIF resolution |
| V09 | NTIA | 16 | H.264 | 256 | 6.3 | 0 | CIF resolution |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| V10 | T&W FUB | 0 | None | 4096 nominal | 25 | 0 | Reference |
| V10 | T&W FUB | 1 | H264 | 256 | 5 | 0 | Deblocking =yes |
| V10 | T&W FUB | 2 | H264 | 256 | 12.5 | 0 | Deblocking = yes |
| V10 | T&W FUB | 3 | H264 | 384 | 5 | 0 | Deblocking = yes |
| V10 | T&W FUB | 4 | H264 | 384 | 12.5 | 0 | Deblocking = yes |
| V10 | T&W FUB | 5 | H264 | 384 | 25 | 0 | Deblocking = yes |
| V10 | T&W FUB | 6 | H264 | 512 | 5 | 0 | Deblocking = yes |
| V10 | T&W FUB | 7 | H264 | 512 | 5 | 0 | Deblocking =no |
| V10 | T&W FUB | 8 | H264 | 512 | 12.5 | 0 | Deblocking = yes |
| V10 | T&W FUB | 9 | H264 | 512 | 12.5 | 0 | Deblocking =no |
| V10 | T&W FUB | 10 | H264 | 512 | 25 | 0 | Deblocking = yes |
| V10 | T&W FUB | 11 | H264 | 512 | 25 | 0 | Deblocking = no |
| V10 | T&W FUB | 12 | H264 | 750 | 12.5 | 0 | Deblocking = yes |
| V10 | T&W FUB | 13 | H264 | 750 | 25 | 0 | Deblocking = yes |
| V10 | T&W FUB | 14 | H264 | 750 | 25 | 0 | Deblocking = no |
| V10 | T&W FUB | 15 | H264 | 1024 | 25 | 0 | Deblocking = yes |
| V10 | T&W FUB | 16 | H264 | 128 | 5 | 0 | Deblocking = yes |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| V11 | IRCCyN | 0 | None | 4096 nominal | 25 | 0 | Reference |
| V11 | IRCCyN | 1 | x264 | 128 | 5 | 0 | Pre- & post-processing |
| V11 | IRCCyN | 2 | x264 | 128 | 10 | 0 | Pre- & post-processing |
| V11 | IRCCyN | 3 | x264 | 256 | 12.5 | 0 | Pre- & post-processing |
| V11 | IRCCyN | 4 | x264 | 256 | 10 | 0 | Pre- & post-processing |
| V11 | IRCCyN | 5 | x264 | 512 | 12.5 | 0 | Pre- & post-processing |
| V11 | IRCCyN | 6 | x264 | 512 | 25 | 0 | Pre- & post-processing |
| V11 | IRCCyN | 7 | H264 | 256 | 25 | 0 | Pre- & post-processing |
| V11 | IRCCyN | 8 | H264 | 512 | 12.5 | 0 | Pre- & post-processing |
| V11 | IRCCyN | 9 | H264 | 512 | 25 | 0 | Pre- & post-processing |
| V11 | IRCCyN | 10 | H264 | 704 | 25 | 0 |  |
| V11 | IRCCyN | 11 | H264 | 1000 | 25 | 0 |  |
| V11 | IRCCyN | 12 | SVC | 256 | 12.5 | 0 | Pre- & post-processing |
| V11 | IRCCyN | 13 | SVC | 256 | 25 | 0 | Pre- & post-processing |
| V11 | IRCCyN | 14 | SVC | 704 | 25 | 0 | Pre- & post-processing |
| V11 | IRCCyN | 15 | SVC | 704 | 25 | 0 | Pre- & post-processing |
| V11 | IRCCyN | 16 | SVC | 1000 | 25 | 0 | Pre- & post-processing |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| V12 | NTIA | 0 | None | 4096 nominal | 27.9 | 0 | Reference |
| V12 | NTIA | 1 | MPEG2 | 512 | 4.6 | 0 |  |
| V12 | NTIA | 2 | H.264 | 256 | 6 | 0 |  |
| V12 | NTIA | 3 | MPEG2 | ≈448 | 28.6 | 0 | QCIF resolution |
| V12 | NTIA | 4 | MPEG2 | ≈1000 | 27.6 | 0 |  |
| V12 | NTIA | 5 | MPEG2 | 3000 | 19.7 | 0 |  |
| V12 | NTIA | 6 | H.264 | 256 | 9.9 | 0 |  |
| V12 | NTIA | 7 | Cinepak | 2500 | 28.1 | 0 | RGB colorspace conversion |
| V12 | NTIA | 8 | WM9 | 2000 | 9.9 | 0 |  |
| V12 | NTIA | 9 | DivX | 704 | 9.9 | 0 | noise filter |
| V12 | NTIA | 10 | DivX | ≈320 | 20.1 | 0 | VBR |
| V12 | NTIA | 11 | MPEG4 | 128 | 20.1 | 0 | SIF resolution |
| V12 | NTIA | 12 | Sorenson | 320 | 4.6 | 0 | RGB colorspace conversion |
| V12 | NTIA | 13 | Chain of codecs | * (128) | 11.2 | 0 | Multiple transformations |
| V12 | NTIA | 14 | H.263 | 128 to 448 | 4.8 | 0 | VBR |
| V12 | NTIA | 15 | H.264 | 256 | 15 | 0 | 240x180 resolution |
| V12 | NTIA | 16 | Theora | 643 to 2014 | 27.9 | 0 | VBR |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| V13 | T&W FUB | 0 | None | 4096 nominal | 30 | 0 | Reference |
| V13 | T&W FUB | 1 | H264 | 384 | 15 | 0 | Deblocking = yes |
| V13 | T&W FUB | 2 | H264 | 512 | 5 | 0 | Deblocking = yes |
| V13 | T&W FUB | 3 | H264 | 512 | 15 | 0 | Deblocking = no |
| V13 | T&W FUB | 4 | H264 | 512 | 15 | 0 | Deblocking = yes |
| V13 | T&W FUB | 5 | H264 | 512 | 30 | 0 | Deblocking = no |
| V13 | T&W FUB | 6 | H264 | 512 | 30 | 0 | Deblocking = yes |
| V13 | T&W FUB | 7 | H264 | 750 | 15 | 0 | Deblocking = yes |
| V13 | T&W FUB | 8 | H264 | 750 | 30 | 0 | Deblocking = no |
| V13 | T&W FUB | 9 | H264 | 750 | 30 | 0 | Deblocking = yes |
| V13 | T&W FUB | 10 | H264 | 1024 | 15 | 0 | Deblocking = yes |
| V13 | T&W FUB | 11 | H264 | 1024 | 30 | 0 | Deblocking = yes |
| V13 | T&W FUB | 12 | H264 | 1024 | 30 | 0 | Deblocking = no |
| V13 | T&W FUB | 13 | H264 | 2048 | 30 | 0 | Deblocking = yes |
| V13 | T&W FUB | 14 | H264 | 2048 | 30 | 0 | Deblocking = no |
| V13 | T&W FUB | 15 | H264 | 4096 | 30 | 0 | Deblocking = yes |
| V13 | T&W FUB | 16 | H264 | 6000 | 30 | 0 | Deblocking = yes |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| C01 | Psytechnics | 0 | none | 1536 nominal | 25 | 0 | reference |
| C01 | Psytechnics | 1 | MPEG4 | 2000 | 25 | 0 |  |
| C01 | Psytechnics | 2 | VC1 | 1000 | 25 | 0 |  |
| C01 | Psytechnics | 3 | MPEG4 | 1000 | 25 | 0 |  |
| C01 | Psytechnics | 4 | H264 | 1000 | 25 | 0 |  |
| C01 | Psytechnics | 5 | VC1 | 512 | 25 | 0 |  |
| C01 | Psytechnics | 6 | RV10 | 512 | 25 | 0 |  |
| C01 | Psytechnics | 7 | MPEG4 | 512 | 25 | 0 |  |
| C01 | Psytechnics | 8 | H264 | 512 | 25 | 0 |  |
| C01 | Psytechnics | 9 | VC1 | 320 | 12.5 | 0 |  |
| C01 | Psytechnics | 10 | RV10 | 320 | 12.5 | 0 |  |
| C01 | Psytechnics | 11 | MPEG4 | 320 | 12.5 | 0 |  |
| C01 | Psytechnics | 12 | VC1 | 128 | 5 | 0 |  |
| C01 | Psytechnics | 13 | RV10 | 128 | 5 | 0 |  |
| C01 | Psytechnics | 14 | MPEG4 | 2000 | 25 | 2 | random |
| C01 | Psytechnics | 15 | MPEG4 | 2000 | 25 | 2 | bursty |
| C01 | Psytechnics | 16 | MPEG4 | 2000 | 25 | 5 | bursty |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| C02 | NTT | 0 | none | 1536 nominal | 30 | 0 | reference |
| C02 | NTT | 1 | MPEG4 | 704 | 30 | 0 |  |
| C02 | NTT | 2 | MPEG4 | 320 | 30 | 0 |  |
| C02 | NTT | 3 | MPEG4 | 320 | 15 | 0 |  |
| C02 | NTT | 4 | MPEG4 | 128 | 15 | 0 |  |
| C02 | NTT | 5 | MPEG4 | 128 | 10 | 0 |  |
| C02 | NTT | 6 | MPEG4 | 64 | 15 | 0 |  |
| C02 | NTT | 7 | MPEG4 | 64 | 10 | 0 |  |
| C02 | NTT | 8 | MPEG4 | 64 | 5 | 0 |  |
| C02 | NTT | 9 | MPEG4 | 704 | 30 | 1 |  |
| C02 | NTT | 10 | MPEG4 | 704 | 30 | 2 |  |
| C02 | NTT | 11 | MPEG4 | 704 | 30 | 4 |  |
| C02 | NTT | 12 | MPEG4 | 320 | 30 | 1 |  |
| C02 | NTT | 13 | MPEG4 | 320 | 30 | 2 |  |
| C02 | NTT | 14 | MPEG4 | 320 | 30 | 4 |  |
| C02 | NTT | 15 | MPEG4 | 128 | 30 | 2 |  |
| C02 | NTT | 16 | MPEG4 | 128 | 30 | 4 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| C03 | NTT | 0 | none | 1536 nominal | 30 | 0 | reference |
| C03 | NTT | 1 | RV10 | 704 | 30 | 0 |  |
| C03 | NTT | 2 | RV10 | 320 | 30 | 0 |  |
| C03 | NTT | 3 | RV10 | 320 | 15 | 0 |  |
| C03 | NTT | 4 | RV10 | 128 | 15 | 0 |  |
| C03 | NTT | 5 | RV10 | 128 | 10 | 0 |  |
| C03 | NTT | 6 | RV10 | 64 | 15 | 0 |  |
| C03 | NTT | 7 | RV10 | 64 | 10 | 0 |  |
| C03 | NTT | 8 | RV10 | 64 | 5 | 0 |  |
| C03 | NTT | 9 | RV10 | 704 | 30 | 1 |  |
| C03 | NTT | 10 | RV10 | 704 | 30 | 2 |  |
| C03 | NTT | 11 | RV10 | 704 | 30 | 4 |  |
| C03 | NTT | 12 | RV10 | 320 | 30 | 1 |  |
| C03 | NTT | 13 | RV10 | 320 | 30 | 2 |  |
| C03 | NTT | 14 | RV10 | 320 | 30 | 4 |  |
| C03 | NTT | 15 | RV10 | 320 | 15 | 2 |  |
| C03 | NTT | 16 | RV10 | 320 | 15 | 4 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| C04 | NTT | 0 | none | 1536 nominal | 30 | 0 | reference |
| C04 | NTT | 1 | H264 | 704 | 30 | 0 |  |
| C04 | NTT | 2 | H264 | 320 | 30 | 0 |  |
| C04 | NTT | 3 | H264 | 320 | 15 | 0 |  |
| C04 | NTT | 4 | H264 | 128 | 15 | 0 |  |
| C04 | NTT | 5 | H264 | 128 | 10 | 0 |  |
| C04 | NTT | 6 | H264 | 64 | 15 | 0 |  |
| C04 | NTT | 7 | H264 | 64 | 10 | 0 |  |
| C04 | NTT | 8 | H264 | 64 | 5 | 0 |  |
| C04 | NTT | 9 | H264 | 704 | 30 | 1 |  |
| C04 | NTT | 10 | H264 | 704 | 30 | 2 |  |
| C04 | NTT | 11 | H264 | 704 | 30 | 4 |  |
| C04 | NTT | 12 | H264 | 320 | 30 | 1 |  |
| C04 | NTT | 13 | H264 | 320 | 30 | 2 |  |
| C04 | NTT | 14 | H264 | 320 | 30 | 4 |  |
| C04 | NTT | 15 | H264 | 320 | 15 | 2 |  |
| C04 | NTT | 16 | H264 | 320 | 15 | 4 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| C05 | Yonsei | 0 | none | 1536 nominal | 30 | 0 | reference |
| C05 | Yonsei | 1 | H264 | 64 | 10 | 0 |  |
| C05 | Yonsei | 2 | H264 | 128 | 15 | 0 |  |
| C05 | Yonsei | 3 | H264 | 320 | 15 | 0 |  |
| C05 | Yonsei | 4 | H264 | 320 | 30 | 0 |  |
| C05 | Yonsei | 5 | H264 | 704 | 30 | 0 |  |
| C05 | Yonsei | 6 | MPEG4 | 64 | 10 | 0 |  |
| C05 | Yonsei | 7 | MPEG4 | 128 | 15 | 0 |  |
| C05 | Yonsei | 8 | MPEG4 | 320 | 15 | 0 |  |
| C05 | Yonsei | 9 | MPEG4 | 320 | 30 | 0 |  |
| C05 | Yonsei | 10 | MPEG4 | 704 | 30 | 0 |  |
| C05 | Yonsei | 11 | RV10 | 128 | 15 | 0 |  |
| C05 | Yonsei | 12 | RV10 | 320 | 30 | 0 |  |
| C05 | Yonsei | 13 | RV10 | 704 | 30 | 0 |  |
| C05 | Yonsei | 14 | RV10 | 64 | 10 | 0 |  |
| C05 | Yonsei | 15 | RV10 | 320 | 15 | 0 |  |
| C05 | Yonsei | 16 | RV10 | 704 | 30 | 0 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| C06 | Yonsei | 0 | none | 1536 nominal | 30 | 0 | reference |
| C06 | Yonsei | 1 | MPEG4 | 64 | 10 | 0 |  |
| C06 | Yonsei | 2 | MPEG4 | 128 | 15 | 5 |  |
| C06 | Yonsei | 3 | MPEG4 | 320 | 15 | 2 |  |
| C06 | Yonsei | 4 | MPEG4 | 320 | 30 | 1 |  |
| C06 | Yonsei | 5 | MPEG4 | 704 | 30 | 0 |  |
| C06 | Yonsei | 6 | H264 | 64 | 10 | 0 |  |
| C06 | Yonsei | 7 | H264 | 128 | 15 | 0 |  |
| C06 | Yonsei | 8 | H264 | 320 | 15 | 0 |  |
| C06 | Yonsei | 9 | H264 | 320 | 30 | 7 |  |
| C06 | Yonsei | 10 | H264 | 704 | 30 | 0 |  |
| C06 | Yonsei | 11 | RV10 | 64 | 10 | 0 |  |
| C06 | Yonsei | 12 | RV10 | 320 | 15 | 0 |  |
| C06 | Yonsei | 13 | RV10 | 704 | 30 | 0 |  |
| C06 | Yonsei | 14 | VC1 | 64 | 10 | 0 |  |
| C06 | Yonsei | 15 | VC1 | 128 | 15 | 0 |  |
| C06 | Yonsei | 16 | VC1 | 704 | 30 | 0 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| C07 | KDDI | 0 | none | 1536 nominal | 30 | 0 | reference |
| C07 | KDDI | 1 | H264 | 64 | 3 | 0 |  |
| C07 | KDDI | 2 | H264 | 64 | 5 | 0 |  |
| C07 | KDDI | 3 | H264 | 128 | 5 | 0 |  |
| C07 | KDDI | 4 | H264 | 256 | 5 | 0 |  |
| C07 | KDDI | 5 | H264 | 256 | 10 | 0 |  |
| C07 | KDDI | 6 | H264 | 384 | 10 | 0 |  |
| C07 | KDDI | 7 | H264 | 384 | 15 | 0 |  |
| C07 | KDDI | 8 | MPG4 | 128 | 5 | 0 |  |
| C07 | KDDI | 9 | MPG4 | 256 | 5 | 0 |  |
| C07 | KDDI | 10 | MPG4 | 512 | 10 | 0 |  |
| C07 | KDDI | 11 | MPG4 | 768 | 10 | 0 |  |
| C07 | KDDI | 12 | MPG4 | 768 | 15 | 0 |  |
| C07 | KDDI | 13 | H264 | 256 | 10 | 1 |  |
| C07 | KDDI | 14 | H264 | 256 | 10 | 2 |  |
| C07 | KDDI | 15 | MPG4 | 512 | 10 | 1 |  |
| C07 | KDDI | 16 | MPG4 | 512 | 10 | 2 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| C08 | KDDI | 0 | none | 1536 nominal | 30 | 0 | reference |
| C08 | KDDI | 1 | H264 | 64 | 3 | 0 |  |
| C08 | KDDI | 2 | H264 | 64 | 5 | 0 |  |
| C08 | KDDI | 3 | H264 | 128 | 5 | 0 |  |
| C08 | KDDI | 4 | H264 | 256 | 5 | 0 |  |
| C08 | KDDI | 5 | H264 | 256 | 10 | 0 |  |
| C08 | KDDI | 6 | H264 | 384 | 10 | 0 |  |
| C08 | KDDI | 7 | H264 | 384 | 15 | 0 |  |
| C08 | KDDI | 8 | MPG4 | 128 | 5 | 0 |  |
| C08 | KDDI | 9 | MPG4 | 256 | 5 | 0 |  |
| C08 | KDDI | 10 | MPG4 | 512 | 10 | 0 |  |
| C08 | KDDI | 11 | MPG4 | 768 | 10 | 0 |  |
| C08 | KDDI | 12 | MPG4 | 768 | 15 | 0 |  |
| C08 | KDDI | 13 | H264 | 256 | 10 | 1 |  |
| C08 | KDDI | 14 | H264 | 256 | 10 | 2 |  |
| C08 | KDDI | 15 | MPG4 | 512 | 10 | 1 |  |
| C08 | KDDI | 16 | MPG4 | 512 | 10 | 2 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| C09 | KDDI | 0 | none | 1536 nominal | 30 | 0 | reference |
| C09 | KDDI | 1 | H264 | 64 | 3 | 0 |  |
| C09 | KDDI | 2 | H264 | 64 | 5 | 0 |  |
| C09 | KDDI | 3 | H264 | 128 | 5 | 0 |  |
| C09 | KDDI | 4 | H264 | 256 | 5 | 0 |  |
| C09 | KDDI | 5 | H264 | 256 | 10 | 0 |  |
| C09 | KDDI | 6 | H264 | 384 | 10 | 0 |  |
| C09 | KDDI | 7 | H264 | 384 | 15 | 0 |  |
| C09 | KDDI | 8 | MPG4 | 128 | 5 | 0 |  |
| C09 | KDDI | 9 | MPG4 | 256 | 5 | 0 |  |
| C09 | KDDI | 10 | MPG4 | 512 | 10 | 0 |  |
| C09 | KDDI | 11 | MPG4 | 768 | 10 | 0 |  |
| C09 | KDDI | 12 | MPG4 | 768 | 15 | 0 |  |
| C09 | KDDI | 13 | H264 | 256 | 10 | 1 |  |
| C09 | KDDI | 14 | H264 | 256 | 10 | 2 |  |
| C09 | KDDI | 15 | MPG4 | 512 | 10 | 1 |  |
| C09 | KDDI | 16 | MPG4 | 512 | 10 | 2 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| C10 | Symmetricom | 0 | none | 1536 nominal | 25 | 0 | reference |
| C10 | Symmetricom | 1 | H264 | 64 | 12.5 | 0 |  |
| C10 | Symmetricom | 2 | H264 | 128 | 12.5 | 0 |  |
| C10 | Symmetricom | 3 | H264 | 256 | 12.5 | 0 |  |
| C10 | Symmetricom | 4 | H264 | 256 | 25 | 0 |  |
| C10 | Symmetricom | 5 | H264 | 512 | 25 | 0 |  |
| C10 | Symmetricom | 6 | WM9 | 64 | 12.5 | 0 |  |
| C10 | Symmetricom | 7 | WM9 | 128 | 12.5 | 0 |  |
| C10 | Symmetricom | 8 | WM9 | 256 | 12.5 | 0 |  |
| C10 | Symmetricom | 9 | WM9 | 256 | 25 | 0 |  |
| C10 | Symmetricom | 10 | WM9 | 512 | 25 | 0 |  |
| C10 | Symmetricom | 11 | MPG4 | 256 | 25 | 0 |  |
| C10 | Symmetricom | 12 | MPG4 | 512 | 25 | 0 |  |
| C10 | Symmetricom | 13 | JP2000 | 256 | 8.33 | 0 |  |
| C10 | Symmetricom | 14 | JP2000 | 256 | 12.5 | 0 |  |
| C10 | Symmetricam | 15 | JP2000 | 512 | 12.5 | 0 |  |
| C10 | Symmetricom | 16 | JP2000 | 768 | 25 | 0 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| C11 | NTIA | 0 | none | 1536 nominal | 29.7 | 0 | reference |
| C11 | NTIA | 1 | H.264 | 704 | 29.7 | 0 |  |
| C11 | NTIA | 2 | MPEG-1 | 320 | 29.7 | 0 |  |
| C11 | NTIA | 3 | MPEG-1 | 448 | 29.7 | 0 |  |
| C11 | NTIA | 4 | DivX | 448 | 29.7 | 0 |  |
| C11 | NTIA | 5 | DivX | 192 | 29.7 | 0 |  |
| C11 | NTIA | 6 | Cinepak | 320 | 29.7 | 0 | RGB Colorspace conversion |
| C11 | NTIA | 7 | Sorenson 3 | 64 | 29.7 | 0 | RGB Colorspace conversion |
| C11 | NTIA | 8 | MPEG4-ISO | 128 | 29.7 | 0 |  |
| C11 | NTIA | 9 | H.264 | 384 | automatic (24.4) | 1 | error concealment |
| C11 | NTIA | 10 | H.264 | 128 | automatic (9.5) | 0 |  |
| C11 | NTIA | 11 | H.263 | 256 | automatic (5.9) | 0 |  |
| C11 | NTIA | 12 | H.264 | 256 | automatic (13.4) | 0.2 | burst error with FEC |
| C11 | NTIA | 13 | H.263 | 128 | automatic (8.0) | 0 |  |
| C11 | NTIA | 14 | H.263 | 384 | automatic (14.5) | 0 |  |
| C11 | NTIA | 15 | H.264 | 704 | automatic (29.4) | 0.25 | 1/2 clips 0.5% packet loss |
| C11 | NTIA | 16 | H.261 | 384 | automatic (21.4) | 0 | QCIF resolution |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| C12 | CRC | 0 | none | 1536 nominal | 30 | 0 | reference |
| C12 | CRC | 1 | H.264 | 768 | 30 | 0 |  |
| C12 | CRC | 2 | H.264 | 768 | 20 | 0 |  |
| C12 | CRC | 3 | H.264 | 256 | 20 | 0 |  |
| C12 | CRC | 4 | H.264 | 256 | 15 | 0 |  |
| C12 | CRC | 5 | H.264 | 128 | 20 | 0 |  |
| C12 | CRC | 6 | H.264 | 128 | 15 | 0 |  |
| C12 | CRC | 7 | H.264 | 768 | 30 | 0.5 |  |
| C12 | CRC | 8 | H.264 | 768 | 30 | 1 |  |
| C12 | CRC | 9 | H.264 | 768 | 30 | 2 |  |
| C12 | CRC | 10 | H.264 | 768 | 30 | 4 |  |
| C12 | CRC | 11 | H.264 | 768 | 30 | 8 |  |
| C12 | CRC | 12 | H.264 | 256 | 20 | 0.5 |  |
| C12 | CRC | 13 | H.264 | 256 | 20 | 1 |  |
| C12 | CRC | 14 | H.264 | 256 | 20 | 2 |  |
| C12 | CRC | 15 | H.264 | 256 | 20 | 4 |  |
| C12 | CRC | 16 | H.264 | 256 | 20 | 8 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Deblocking |
| --- | --- | --- | --- | --- | --- | --- | --- |
| C13 | T&W FUB | 0 | none | 1536 nominal | 30 | 0 | reference |
| C13 | T&W FUB | 1 | H264 | 64 | 5 | 0 | yes |
| C13 | T&W FUB | 2 | H264 | 96 | 5 | 0 | yes |
| C13 | T&W FUB | 3 | H264 | 128 | 5 | 0 | yes |
| C13 | T&W FUB | 4 | H264 | 192 | 5 | 0 | yes |
| C13 | T&W FUB | 5 | H264 | 256 | 5 | 0 | yes |
| C13 | T&W FUB | 6 | H264 | 128 | 25 | 0 | yes |
| C13 | T&W FUB | 7 | H264 | 192 | 25 | 0 | yes |
| C13 | T&W FUB | 8 | H264 | 256 | 25 | 0 | yes |
| C13 | T&W FUB | 9 | H264 | 384 | 25 | 0 | yes |
| C13 | T&W FUB | 10 | H264 | 128 | 5 | 0 | no |
| C13 | T&W FUB | 11 | H264 | 192 | 5 | 0 | no |
| C13 | T&W FUB | 12 | H264 | 256 | 5 | 0 | no |
| C13 | T&W FUB | 13 | H264 | 384 | 5 | 0 | no |
| C13 | T&W FUB | 14 | H264 | 128 | 25 | 0 | no |
| C13 | T&W FUB | 15 | H264 | 192 | 25 | 0 | no |
| C13 | T&W FUB | 16 | H264 | 256 | 25 | 0 | no |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| C14 | Acreo | 0 | none | 1536 nominal | 25 | 0 | reference |
| C14 | Acreo | 1 | MPEG4 | 300 | 25 | 0 |  |
| C14 | Acreo | 2 | MPEG4 | 300 | 25 | 2 |  |
| C14 | Acreo | 3 | MPEG4 | 200 | 12.5 | 0 |  |
| C14 | Acreo | 4 | MPEG4 | 200 | 12.5 | 2 |  |
| C14 | Acreo | 5 | MPEG4 | 200 | 12.5 | 6 |  |
| C14 | Acreo | 6 | MPEG4 | 90 | 8.33 | 2 |  |
| C14 | Acreo | 7 | MPEG4 | 90 | 8.33 | 6 |  |
| C14 | Acreo | 8 | MPEG4 | 90 | 8.33 | 12 |  |
| C14 | Acreo | 9 | H.264 | 300 | 25 | 0 |  |
| C14 | Acreo | 10 | H.264 | 300 | 25 | 2 |  |
| C14 | Acreo | 11 | H.264 | 200 | 12.5 | 0 |  |
| C14 | Acreo | 12 | H.264 | 200 | 12.5 | 2 |  |
| C14 | Acreo | 13 | H.264 | 200 | 12.5 | 6 |  |
| C14 | Acreo | 14 | H.264 | 90 | 8.33 | 2 |  |
| C14 | Acreo | 15 | H.264 | 90 | 8.33 | 6 |  |
| C14 | Acreo | 16 | H.264 | 90 | 8.33 | 12 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Q01 | Psytechnics | 0 | none | 512 nominal | 25 | 0 | reference |
| Q01 | Psytechnics | 1 | H264 | 320 | 25 | 0 |  |
| Q01 | Psytechnics | 2 | MPEG4 | 320 | 25 | 0 |  |
| Q01 | Psytechnics | 3 | MPEG4 | 320 | 12.5 | 0 |  |
| Q01 | Psytechnics | 4 | H263 | 320 | 12.5 | 0 |  |
| Q01 | Psytechnics | 5 | H264 | 128 | 12.5 | 0 |  |
| Q01 | Psytechnics | 6 | MPEG4 | 128 | 12.5 | 0 |  |
| Q01 | Psytechnics | 7 | H263 | 128 | 12.5 | 0 |  |
| Q01 | Psytechnics | 8 | H264 | 64 | 12.5 | 0 |  |
| Q01 | Psytechnics | 9 | MPEG4 | 64 | 12.5 | 0 |  |
| Q01 | Psytechnics | 10 | H263 | 64 | 12.5 | 0 |  |
| Q01 | Psytechnics | 11 | H264 | 32 | 5 | 0 |  |
| Q01 | Psytechnics | 12 | MPEG4 | 32 | 5 | 0 |  |
| Q01 | Psytechnics | 13 | H263 | 32 | 5 | 0 |  |
| Q01 | Psytechnics | 14 | MPEG4 | 320 | 12.5 | 2 | periodic PL |
| Q01 | Psytechnics | 15 | MPEG4 | 320 | 12.5 | 5 | bursty PL |
| Q01 | Psytechnics | 16 | MPEG4 | 320 | 12.5 | 1 | periodic PL |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Q02 | NTT | 0 | none | 512 nominal | 30 | 0 | reference |
| Q02 | NTT | 1 | MPEG4 | 320 | 30 | 0 |  |
| Q02 | NTT | 2 | MPEG4 | 128 | 30 | 0 |  |
| Q02 | NTT | 3 | MPEG4 | 128 | 10 | 0 |  |
| Q02 | NTT | 4 | MPEG4 | 64 | 10 | 0 |  |
| Q02 | NTT | 5 | MPEG4 | 64 | 2.5 | 0 |  |
| Q02 | NTT | 6 | MPEG4 | 32 | 10 | 0 |  |
| Q02 | NTT | 7 | MPEG4 | 32 | 2.5 | 0 |  |
| Q02 | NTT | 8 | MPEG4 | 16 | 2.5 | 0 |  |
| Q02 | NTT | 9 | MPEG4 | 128 | 30 | 1 |  |
| Q02 | NTT | 10 | MPEG4 | 128 | 30 | 2 |  |
| Q02 | NTT | 11 | MPEG4 | 128 | 30 | 4 |  |
| Q02 | NTT | 12 | MPEG4 | 64 | 30 | 1 |  |
| Q02 | NTT | 13 | MPEG4 | 64 | 30 | 2 |  |
| Q02 | NTT | 14 | MPEG4 | 64 | 30 | 4 |  |
| Q02 | NTT | 15 | MPEG4 | 32 | 30 | 2 |  |
| Q02 | NTT | 16 | MPEG4 | 32 | 30 | 4 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Q03 | NTT | 0 | none | 512 nominal | 30 | 0 | reference |
| Q03 | NTT | 1 | RV10 | 320 | 30 | 0 |  |
| Q03 | NTT | 2 | RV10 | 128 | 30 | 0 |  |
| Q03 | NTT | 3 | RV10 | 128 | 10 | 0 |  |
| Q03 | NTT | 4 | RV10 | 64 | 10 | 0 |  |
| Q03 | NTT | 5 | RV10 | 64 | 2.5 | 0 |  |
| Q03 | NTT | 6 | RV10 | 32 | 10 | 0 |  |
| Q03 | NTT | 7 | RV10 | 32 | 2.5 | 0 |  |
| Q03 | NTT | 8 | RV10 | 16 | 2.5 | 0 |  |
| Q03 | NTT | 9 | RV10 | 128 | 30 | 1 |  |
| Q03 | NTT | 10 | RV10 | 128 | 30 | 2 |  |
| Q03 | NTT | 11 | RV10 | 128 | 30 | 4 |  |
| Q03 | NTT | 12 | RV10 | 64 | 30 | 1 |  |
| Q03 | NTT | 13 | RV10 | 64 | 30 | 2 |  |
| Q03 | NTT | 14 | RV10 | 64 | 30 | 4 |  |
| Q03 | NTT | 15 | RV10 | 64 | 10 | 2 |  |
| Q03 | NTT | 16 | RV10 | 64 | 10 | 4 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Q04 | NTT | 0 | none | 512 nominal | 30 | 0 | reference |
| Q04 | NTT | 1 | H264 | 320 | 30 | 0 |  |
| Q04 | NTT | 2 | H264 | 128 | 30 | 0 |  |
| Q04 | NTT | 3 | H264 | 128 | 10 | 0 |  |
| Q04 | NTT | 4 | H264 | 64 | 10 | 0 |  |
| Q04 | NTT | 5 | H264 | 64 | 2.5 | 0 |  |
| Q04 | NTT | 6 | H264 | 32 | 10 | 0 |  |
| Q04 | NTT | 7 | H264 | 32 | 2.5 | 0 |  |
| Q04 | NTT | 8 | H264 | 16 | 2.5 | 0 |  |
| Q04 | NTT | 9 | H264 | 128 | 30 | 1 |  |
| Q04 | NTT | 10 | H264 | 128 | 30 | 2 |  |
| Q04 | NTT | 11 | H264 | 128 | 30 | 4 |  |
| Q04 | NTT | 12 | H264 | 64 | 30 | 1 |  |
| Q04 | NTT | 13 | H264 | 64 | 30 | 2 |  |
| Q04 | NTT | 14 | H264 | 64 | 30 | 4 |  |
| Q04 | NTT | 15 | H264 | 64 | 10 | 2 |  |
| Q04 | NTT | 16 | H264 | 64 | 10 | 4 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Q05 | Yonsei | 0 | none | 512 nominal | 30 | 0 | reference |
| Q05 | Yonsei | 1 | MPEG4 | 32 | 5 | 5 |  |
| Q05 | Yonsei | 2 | MPEG4 | 32 | 10 | 0 |  |
| Q05 | Yonsei | 3 | MPEG4 | 64 | 10 | 2 |  |
| Q05 | Yonsei | 4 | MPEG4 | 128 | 15 | 0 |  |
| Q05 | Yonsei | 5 | MPEG4 | 320 | 30 | 1 |  |
| Q05 | Yonsei | 6 | H264 | 32 | 5 | 0 |  |
| Q05 | Yonsei | 7 | H264 | 32 | 10 | 0 |  |
| Q05 | Yonsei | 8 | H264 | 64 | 10 | 0 |  |
| Q05 | Yonsei | 9 | H264 | 128 | 15 | 7 | Darwin streaming server capture |
| Q05 | Yonsei | 10 | H264 | 320 | 30 | 0 |  |
| Q05 | Yonsei | 11 | RV10 | 16 | 5 | 0 |  |
| Q05 | Yonsei | 12 | RV10 | 64 | 10 | 0 |  |
| Q05 | Yonsei | 13 | RV10 | 320 | 30 | 0 |  |
| Q05 | Yonsei | 14 | VC1 | 32 | 10 | 0 |  |
| Q05 | Yonsei | 15 | VC1 | 128 | 15 | 0 |  |
| Q05 | Yonsei | 16 | VC1 | 320 | 30 | 0 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Q06 | Yonsei | 0 | none | 512 nominal | 30 | 0 | reference |
| Q06 | Yonsei | 1 | H264 | 32 | 5 | 0 |  |
| Q06 | Yonsei | 2 | H264 | 32 | 10 | 0 |  |
| Q06 | Yonsei | 3 | H264 | 64 | 10 | 0 |  |
| Q06 | Yonsei | 4 | H264 | 128 | 15 | 0 |  |
| Q06 | Yonsei | 5 | H264 | 320 | 30 | 0 |  |
| Q06 | Yonsei | 6 | MPEG4 | 32 | 5 | 0 |  |
| Q06 | Yonsei | 7 | MPEG4 | 32 | 10 | 0 |  |
| Q06 | Yonsei | 8 | MPEG4 | 64 | 10 | 0 |  |
| Q06 | Yonsei | 9 | MPEG4 | 128 | 15 | 0 |  |
| Q06 | Yonsei | 10 | MPEG4 | 320 | 30 | 0 |  |
| Q06 | Yonsei | 11 | RV10 | 16 | 5 | 0 |  |
| Q06 | Yonsei | 12 | RV10 | 32 | 10 | 0 |  |
| Q06 | Yonsei | 13 | RV10 | 320 | 30 | 0 |  |
| Q06 | Yonsei | 14 | VC1 | 32 | 5 | 0 |  |
| Q06 | Yonsei | 15 | VC1 | 64 | 10 | 0 |  |
| Q06 | Yonsei | 16 | VC1 | 320 | 30 | 0 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Q07 | KDDI | 0 | none | 512 nominal | 30 | 0 | reference |
| Q07 | KDDI | 1 | H264 | 16 | 3 | 0 |  |
| Q07 | KDDI | 2 | H264 | 16 | 5 | 0 |  |
| Q07 | KDDI | 3 | H264 | 32 | 5 | 0 |  |
| Q07 | KDDI | 4 | H264 | 64 | 5 | 0 |  |
| Q07 | KDDI | 5 | H264 | 64 | 10 | 0 |  |
| Q07 | KDDI | 6 | H264 | 128 | 10 | 0 |  |
| Q07 | KDDI | 7 | H264 | 128 | 15 | 0 |  |
| Q07 | KDDI | 8 | MPEG4 | 32 | 5 | 0 |  |
| Q07 | KDDI | 9 | MPEG4 | 64 | 5 | 0 |  |
| Q07 | KDDI | 10 | MPEG4 | 128 | 10 | 0 |  |
| Q07 | KDDI | 11 | MPEG4 | 256 | 10 | 0 |  |
| Q07 | KDDI | 12 | MPEG4 | 256 | 15 | 0 |  |
| Q07 | KDDI | 13 | H264 | 128 | 10 | 1 |  |
| Q07 | KDDI | 14 | H264 | 128 | 10 | 2 |  |
| Q07 | KDDI | 15 | MPEG4 | 128 | 10 | 1 |  |
| Q07 | KDDI | 16 | MPEG4 | 128 | 10 | 2 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Q08 | KDDI | 0 | none | 512 nominal | 30 | 0 | reference |
| Q08 | KDDI | 1 | H264 | 16 | 3 | 0 |  |
| Q08 | KDDI | 2 | H264 | 16 | 5 | 0 |  |
| Q08 | KDDI | 3 | H264 | 32 | 5 | 0 |  |
| Q08 | KDDI | 4 | H264 | 64 | 5 | 0 |  |
| Q08 | KDDI | 5 | H264 | 64 | 10 | 0 |  |
| Q08 | KDDI | 6 | H264 | 128 | 10 | 0 |  |
| Q08 | KDDI | 7 | H264 | 128 | 15 | 0 |  |
| Q08 | KDDI | 8 | MPEG4 | 32 | 5 | 0 |  |
| Q08 | KDDI | 9 | MPEG4 | 64 | 5 | 0 |  |
| Q08 | KDDI | 10 | MPEG4 | 128 | 10 | 0 |  |
| Q08 | KDDI | 11 | MPEG4 | 256 | 10 | 0 |  |
| Q08 | KDDI | 12 | MPEG4 | 256 | 15 | 0 |  |
| Q08 | KDDI | 13 | H264 | 128 | 10 | 1 |  |
| Q08 | KDDI | 14 | H264 | 128 | 10 | 2 |  |
| Q08 | KDDI | 15 | MPEG4 | 128 | 10 | 1 |  |
| Q08 | KDDI | 16 | MPEG4 | 128 | 10 | 2 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Q09 | KDDI | 0 | none | 512 nominal | 30 | 0 | reference |
| Q09 | KDDI | 1 | H264 | 16 | 3 | 0 |  |
| Q09 | KDDI | 2 | H264 | 16 | 5 | 0 |  |
| Q09 | KDDI | 3 | H264 | 32 | 5 | 0 |  |
| Q09 | KDDI | 4 | H264 | 64 | 5 | 0 |  |
| Q09 | KDDI | 5 | H264 | 64 | 10 | 0 |  |
| Q09 | KDDI | 6 | H264 | 128 | 10 | 0 |  |
| Q09 | KDDI | 7 | H264 | 128 | 15 | 0 |  |
| Q09 | KDDI | 8 | MPEG4 | 32 | 5 | 0 |  |
| Q09 | KDDI | 9 | MPEG4 | 64 | 5 | 0 |  |
| Q09 | KDDI | 10 | MPEG4 | 128 | 10 | 0 |  |
| Q09 | KDDI | 11 | MPEG4 | 256 | 10 | 0 |  |
| Q09 | KDDI | 12 | MPEG4 | 256 | 15 | 0 |  |
| Q09 | KDDI | 13 | H264 | 128 | 10 | 1 |  |
| Q09 | KDDI | 14 | H264 | 128 | 10 | 2 |  |
| Q09 | KDDI | 15 | MPEG4 | 128 | 10 | 1 |  |
| Q09 | KDDI | 16 | MPEG4 | 128 | 10 | 2 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Q10 | FT | 0 | none | 512 nominal | 30 | 0 | reference |
| Q10 | FT | 1 |  |  |  |  |  |
| Q10 | FT | 2 |  |  |  |  |  |
| Q10 | FT | 3 |  |  |  |  |  |
| Q10 | FT | 4 |  |  |  |  |  |
| Q10 | FT | 5 |  |  |  |  |  |
| Q10 | FT | 6 |  |  |  |  |  |
| Q10 | FT | 7 |  |  |  |  |  |
| Q10 | FT | 8 |  |  |  |  |  |
| Q10 | FT | 9 |  |  |  |  |  |
| Q10 | FT | 10 |  |  |  |  |  |
| Q10 | FT | 11 |  |  |  |  |  |
| Q10 | FT | 12 |  |  |  |  |  |
| Q10 | FT | 13 |  |  |  |  |  |
| Q10 | FT | 14 |  |  |  |  |  |
| Q10 | FT | 15 |  |  |  |  |  |
| Q10 | FT | 16 |  |  |  |  |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Q11 | CRC | 0 | none | 512 nominal | 30 | 0 | reference |
| Q11 | CRC | 1 | MPEG4 | 256 | 20 | 0 |  |
| Q11 | CRC | 2 | MPEG4 | 256 | 15 | 0 |  |
| Q11 | CRC | 3 | MPEG4 | 128 | 15 | 0 |  |
| Q11 | CRC | 4 | MPEG4 | 128 | 10 | 0 |  |
| Q11 | CRC | 5 | MPEG4 | 64 | 10 | 0 |  |
| Q11 | CRC | 6 | MPEG4 | 64 | 7.5 | 0 |  |
| Q11 | CRC | 7 | MPEG4 | 256 | 20 | 0.5 |  |
| Q11 | CRC | 8 | MPEG4 | 256 | 20 | 1 |  |
| Q11 | CRC | 9 | MPEG4 | 256 | 20 | 2 |  |
| Q11 | CRC | 10 | MPEG4 | 256 | 20 | 4 |  |
| Q11 | CRC | 11 | MPEG4 | 256 | 20 | 8 |  |
| Q11 | CRC | 12 | MPEG4 | 128 | 15 | 0.5 |  |
| Q11 | CRC | 13 | MPEG4 | 128 | 15 | 1 |  |
| Q11 | CRC | 14 | MPEG4 | 128 | 15 | 2 |  |
| Q11 | CRC | 15 | MPEG4 | 128 | 15 | 4 |  |
| Q11 | CRC | 16 | MPEG4 | 128 | 15 | 8 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Q12 | Acreo | 0 | none | 512 nominal | 25 | 0 | reference |
| Q12 | Acreo | 1 | MPEG4 | 200 | 25 | 0 |  |
| Q12 | Acreo | 2 | MPEG4 | 200 | 25 | 2 |  |
| Q12 | Acreo | 3 | MPEG4 | 90 | 12.5 | 0 |  |
| Q12 | Acreo | 4 | MPEG4 | 90 | 12.5 | 2 |  |
| Q12 | Acreo | 5 | MPEG4 | 90 | 12.5 | 6 |  |
| Q12 | Acreo | 6 | MPEG4 | 40 | 8.33 | 2 |  |
| Q12 | Acreo | 7 | MPEG4 | 40 | 8.33 | 6 |  |
| Q12 | Acreo | 8 | MPEG4 | 40 | 8.33 | 12 |  |
| Q12 | Acreo | 9 | H264 | 200 | 25 | 0 |  |
| Q12 | Acreo | 10 | H264 | 200 | 25 | 2 |  |
| Q12 | Acreo | 11 | H264 | 90 | 12.5 | 0 |  |
| Q12 | Acreo | 12 | H264 | 90 | 12.5 | 2 |  |
| Q12 | Acreo | 13 | H264 | 90 | 12.5 | 6 |  |
| Q12 | Acreo | 14 | H264 | 40 | 8.33 | 2 |  |
| Q12 | Acreo | 15 | H264 | 40 | 8.33 | 6 |  |
| Q12 | Acreo | 16 | H264 | 40 | 8.33 | 12 |  |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Q13 | NTIA | 0 | none | 512 nominal | 25 | 0 | reference |
| Q13 | NTIA | 1 | H.264 | 32 | 12 | 0 |  |
| Q13 | NTIA | 2 | mpeg4 AVC | 16 | 12 | 0 | noise reduction, color correct |
| Q13 | NTIA | 3 | MPEG-1 | 320 | 25 | 0 | conturing & de-noising |
| Q13 | NTIA | 4 | MPEG-1 | 192 | 25 | 0 |  |
| Q13 | NTIA | 5 | DivX | 128 | 8 | 0 | noise reduction |
| Q13 | NTIA | 6 | DivX | 32 | 5 | 0 |  |
| Q13 | NTIA | 7 | Cinepak | 128 | 8 | 0 |  |
| Q13 | NTIA | 8 | Sorenson 3 | 16 | 8 | 0 | RGB conversion required |
| Q13 | NTIA | 9 | MPEG4-ISO | 64 | 12 | 0 |  |
| Q13 | NTIA | 10 | H.264 | 256 | automatic(10) | 0.5 | error concealment |
| Q13 | NTIA | 11 | H.264 | 320 | automatic(12) | 0.5 | error concealment |
| Q13 | NTIA | 12 | H.264 | 128 | automatic(8) | 0 |  |
| Q13 | NTIA | 13 | H.263 | 128 | automatc(8) | 0 |  |
| Q13 | NTIA | 14 | H.264 | 320 | automatic(12) | 0 |  |
| Q13 | NTIA | 15 | H.261 | 256 | automatic(12) | 2 | 1/2 clips have burst errors |
| Q13 | NTIA | 16 | H.261 | 64 | automatic(10) | 2 | 1/2 clips have burst errors |

| Test | Lab | HRC # | Codec | Bit Rate | Frame Rate | PLR | Other |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Q14 | FT | 0 | none | 512 nominal | 25 | 0 | reference |
| Q14 | FT | 1 |  |  |  |  |  |
| Q14 | FT | 2 |  |  |  |  |  |
| Q14 | FT | 3 |  |  |  |  |  |
| Q14 | FT | 4 |  |  |  |  |  |
| Q14 | FT | 5 |  |  |  |  |  |
| Q14 | FT | 6 |  |  |  |  |  |
| Q14 | FT | 7 |  |  |  |  |  |
| Q14 | FT | 8 |  |  |  |  |  |
| Q14 | FT | 9 |  |  |  |  |  |
| Q14 | FT | 10 |  |  |  |  |  |
| Q14 | FT | 11 |  |  |  |  |  |
| Q14 | FT | 12 |  |  |  |  |  |
| Q14 | FT | 13 |  |  |  |  |  |
| Q14 | FT | 14 |  |  |  |  |  |
| Q14 | FT | 15 |  |  |  |  |  |
| Q14 | FT | 16 |  |  |  |  |  |