VQEG HDTV Group

Test Plan for Evaluation of Video Quality Models for Use with High Definition TV Content

Draft Version 2.1

March, 2008

Contact:	Greg Cermak	Tel:  +1 781-466-4132	Email:  greg.cermak@verizon.com

Leigh Thorpe	Tel:  +1 613 763-4382	Email:  thorpe@nortel.com

Editorial History

| Version | Date | Nature of the modification |
| --- | --- | --- |
| 0.0 | November 1, 2004 | Initial Draft, edited by Vivaik Balasubrawmanian |
| 0.1 | November 9, 2004 | Incorporated the following changes from NTIA (Margaret Pinson): Added an editor’s note to highlight the unapproved status. Removed references to future test plans (AV & Interactive) Replaced ACR-HRR with DSIS subjective testing methodology Removed redundant sections Minimum bit rate for HRCs is now 2 Mbits/s. Replaced inconsistent section on Calibration/Registration with the latest text from RRNR test plan. Removed evaluation metrics in line with the agreements reached in the Seoul MM meeting. |
| 0.5 | September 28, 2005 | Incorporated agreements in the April ’05 VQEG meeting in Scottsdale, AZ. |
| 1.0 | September 30, 2005 | Incorporated agreements in the September ’05 VQEG meeting in Stockholm, Sweden. |
| 1.1 | September 21, 2006 | Incorporate changes from audio conferences to date; and accept all previous change marks. |
| 1.2, 1.3 | September 28, 2006 | Changes agreed to at Tokyo VQEG Meeting |
| 1.4 | September 6 2007 | Changes agreed to at Paris VQEG meeting. Re-ordering of sections to be more or less chronological; re-group subsections into relevant sections. |
| 2.0 | Febrary, 2008 | Changes agreed to at Ottawa VQEG meeting. Proposals inserted for empty sections and marked as not having been approved. |

Table of Contents

1.	Introduction	8

2.	Division of Labor and Schedule	10

2.1.	ILG	10

2.2.	Proponent Laboratories	10

2.3.	Test Schedule	10

3.	Objective Quality Models	12

3.1.	Model Type	12

3.2.	Full Reference Model Input & Output Data Format	12

3.3.	Reduced Reference Model Input & Output Data Format	12

3.4.	No Reference Model Input & Output Data Format	13

3.3	Submission of Executable Model	13

4.	Subjective Rating Tests	14

4.1.	Subjective Dataset Submission	14

4.2.	Number of Datasets to Validate Models	14

4.3.	Test Design	14

4.4.	Subjective Test Conditions	15

4.4.1.	Application Across Different Video Formats and Displays	15

4.4.2.	Viewing Conditions	15

4.4.3.	Display Specification and Set-up	15

4.5.	Subjective Test Method:  ACR-HRR	15

4.6.	Length of Sessions	16

4.7.	Subjects	16

4.8.	Instructions for Subjects and Failure to Follow Instructions	16

4.9.	Randomization	17

4.10.	Subjective Data File Format	18

5.	Source Video Sequences	19

5.1.	Selection of Source Sequences (SRC)	19

5.2.	Purchased Source Sequences	19

5.3.	Requirements for Camera, Lens and SRC Coding	19

5.4.	Content	19

5.5.	Scene Cuts	19

5.6.	Scene Duration	19

5.7.	Source Scene Selection Criteria	19

6.	Video Format and Naming Conventions	21

6.1.	Storage of Video Material	21

6.2.	Video File Format	21

6.3.	Naming Conventions	21

7.	HRC Constraints and Sequence Processing	22

7.1.	Sequence Processing Overview	22

7.1.1.	Format Conversions	22

7.1.2.	PVS Duration	22

7.2.	Constraints on Hypothetical Reference Circuits (HRCs)	22

7.2.1.	Coding Schemes	22

7.2.2.	Video Bit-Rates:	23

7.2.3.	Video Encoding Modes	23

7.2.4.	Frame Freezing and Frame Skipping	23

7.2.5.	Rewinding	23

7.2.6.	Frame rates	23

7.2.7.	Transmission Errors	23

7.3.	Processing and Editing of Sequences	24

7.3.1.	Pre-Processing	24

7.3.2.	Post-Processing	24

8.	Calibration	25

8.1.	HRC Calibration Constraints	25

8.2.	HRC Calibration Problems	25

9.	Objective Quality Model Evaluation Criteria	26

9.1.	Evaluation Criteria	26

9.2.	Evaluation Procedure	26

9.3.	Post Subissions Elimination of PVSs	26

10.	Recommendation	28

11.	References	29

List of Acronyms

ACR-HRR	Absolute Category Rating with Hidden Reference Removal

ANOVA	ANalysis Of VAriance

ASCII	ANSI Standard Code for Information Interchange

CCIR	Comite Consultatif International des Radiocommunications

CODEC	Coder-Decoder

CRC	Communications Research Center (Canada)

DMOS	Difference Mean Opinion Score (as defined by ITU-R)

DVB-C	Digital Video Broadcasting-Cable

FR	Full Reference

GOP	Group of Pictures

HD	High Definition (television)

HRC	Hypothetical Reference Circuit

ILG	Independent Lab Group

IRT	Institut Rundfunk Technische (Germany)

ITU	International Telecommunications Union

ITU-R	ITU Radiocommunications Standardization Sector

ITU-T	ITU Telecommunications Standardization Sector

MM	Multimedia

MOS	Mean Opinion Score

MOSp	Mean Opinion Score, predicted

MPEG	Motion Pictures Expert Group

NR	No (or Zero) Reference

NTSC	National Television Standard Committee (60-Hz TV, used mainly in US and Canada)

PAL	Phase Alternating Line (50-Hz TV, used in Europe and elsewhere)

PS	Program Segment

PVS	Processed Video Sequence

RR	Reduced Reference

SMPTE	Society of Motion Picture and Television Engineers

SRC	Source Reference Channel or Circuit

SSCQE 	Single Stimulus Continuous Quality Evaluation

VQEG	Video Quality Experts Group

List of Definitions

Intended frame rate is defined as the number of video frames per second physically stored for some representation of a video sequence.  The intended frame rate may be constant or may change with time.  Two examples of constant intended frame rates are a BetacamSP tape containing 25 fps and a VQEG FR-TV Phase I compliant 625-line YUV file containing 25 fps; these both have an absolute frame rate of 25 fps.  One example of a variable absolute frame rate is a computer file containing only new frames; in this case the intended frame rate exactly matches the effective frame rate.  The content of video frames is not considered when determining intended frame rate.

Anomalous frame repetition is defined as an event where the HRC outputs a single frame repeatedly in response to an unusual or out of the ordinary event.  Anomalous frame repetition includes but is not limited to the following types of events: an error in the transmission channel, a change in the delay through the transmission channel, limited computer resources impacting the decoder’s performance, and limited computer resources impacting the display of the video signal.

Constant frame skipping is defined as an event where the HRC outputs frames with updated content at an effective frame rate that is fixed and less than the source frame rate.

Effective frame rate is defined as the number of unique frames (i.e., total frames – repeated frames) per second.

Frame rate is the number of (progressive) frames displayed per second (fps).

Live Network Conditions are defined as errors imposed upon the digital video bit stream as a result of live network conditions.  Examples of error sources include packet loss due to heavy network traffic, increased delay due to transmission route changes, multi-path on a broadcast signal, and fingerprints on a DVD.  Live network conditions tend to be unpredictable and unrepeatable.

Pausing with skipping (formerly frame skipping) is defined as events where the video pauses for some period of time and then restarts with some loss of video information. In pausing with skipping, the temporal delay through the system will vary about an average system delay, sometimes increasing and sometimes decreasing.  One example of pausing with skipping is a pair of IP Videophones, where heavy network traffic causes the IP Videophone display to freeze briefly; when the IP Videophone display continues, some content has been lost.  Another example is a videoconferencing system that performs constant frame skipping or variable frame skipping.  Constant frame skipping and variable frame skipping are subset of pausing with skipping. A processed video sequence containing pausing with skipping will be approximately the same duration as the associated original video sequence.

Pausing without skipping (formerly frame freeze) is defined as any event where the video pauses for some period of time and then restarts without losing any video information.  Hence, the temporal delay through the system must increase.  One example of pausing without skipping is a computer simultaneously downloading and playing an AVI file, where heavy network traffic causes the player to pause briefly and then continue playing.  A processed video sequence containing pausing without skipping events will always be longer in duration than the associated original video sequence.

Refresh rate is defined as the rate at which the computer monitor is updated.

Rewinding is defined as an event where the HRC playback jumps backwards in time.  Rewinding can occur immediately after a pause.  Given the reference sequence (A B C D E F G H I), two example processed sequence containing rewinding are (A B C D B C D E F) and (A B C C C C A B C).  Rewinding can occur as a response to transmission error; for example, a video player encounters a transmission error, pauses while it conceals the error internally, and then resumes by playing video prior to the frame displayed when the transmission distortion was encountered. Rewinding is different from variable frame skipping because the subjects see the same content again and the motion is much more jumpy.

Simulated transmission errors are defined as errors imposed upon the digital video bit stream in a highly controlled environment.  Examples include simulated packet loss rates and simulated bit errors.  Parameters used to control simulated transmission errors are well defined.

Source frame rate (SFR) is the intended frame rate of the original source video sequences.  The source frame rate is constant.

Transmission errors are defined as any error resulting from sending the video data over a transmission channel.  Examples of transmission errors are corrupted data (bit errors) and lost packets / lost frames.  Such errors may be generated in live network conditions or through simulation.

Variable frame skipping is defined as an event where the HRC outputs frames with updated content at an effective frame rate that changes with time.  The temporal delay through the system will increase and decrease with time, varying about an average system delay.  A processed video sequence containing variable frame skipping will be approximately the same duration as the associated original video sequence.

# Introduction

This document defines evaluation tests of the performance of objective perceptual quality models conducted by the Video Quality Experts Group (VQEG).  It describes the roles and responsibilities of the model proponents participating in this evaluation, as well as the benefits associated with participation.  The role of the Independent Lab Group (ILG) is also defined.  The text is based on discussions and decisions from meetings of the VQEG HDTV working group (HDTV) at the periodic face-to-face meetings as well as on conference calls and in email discussion.

The goal of the HDTV project is to recommend a quality model suitable for application to digital video quality measurement in HDTV applications.  A secondary goal of the HDTV project is to develop HDTV subjective datasets that may be used to improve HDTV objective models.  The performance of objective models with HD signals will be determined from a comparison of viewer ratings of a range of video sample quality obtained in controlled subjective tests and the quality predictions from the submitted models.  In accordance with decisions made at the Ottawa meeting, the test plan has been simplified to reduce the work load for the ILG.  The authors of the models (“proponents”) will do most of the work laid out in this Test Plan: selecting and preparing video source sequences (SRCs), preparing video test sequences (PVSs), gathering subjective quality ratings for the test sequences, ,carrying out the objective measurement of those same sequences with their particular model(s), and for much of the analysis comparing the subjective and objective results.  An ILG within the HDTV group will coordinate tests and help assure their compliance with the conditions of this Test Plan.

For the purposes of this document, HDTV is defined as being of or relating to an application that creates or consumes High Definition television video format that is digitally transmitted over a communication channel.  Common applications of HDTV that are appropriate to this study include television broadcasting, video-on-demand and satellite and cable transmissions.  The measurement tools recommended by the HDTV group will be used to measure quality both in laboratory conditions using a full reference (FR) method and in operational conditions using reduced reference (RR) or no-reference (NR) methods.

To fully characterize the performance of the models, it is important to examine a full range of representative transmission and display conditions. To this end, the test cases (hypothetical reference circuits or HRCs) should simulate the range of potential behavior of cable, satellite, and terrestrial transmission networks and broadband communications services. Both digital and analog impairments will be considered.  The recommendation(s) resulting from this work will be deemed appropriate for services delivered on high definition displays computer desktop monitors, and high definition display television technologies.

In Phase I of the HDTV testing, video-only test conditions will be employed. Currently, HDTV source material appropriate for creating test samples is in short supply.  VQEG would like to obtain material copyright-free or with a royalty-free license for research purposes for these and future tests.  Our ability to perform adequate audio-video and multimedia testing will depend on access to a bank of appropriate source material.

Display formats that will be addressed in these tests are:  1080i at 50 and 60 Hz; and 1080p at 25 and 30 fps Note that 720p is part of this test plan as included as HRCs.  Because currently 720p is commonly up-scaled as part of the display, it was felt that 720p HRCs would more appropriately address this format.  Currently, the following are of particular interest:

- 1080i 60 Hz (30 fps) Japan, US

- 1080p (25 fps) Europe

- 1080i 50 Hz (25 fps) Europe

- 1080p (30 fps) Japan, US

where objective models should be able to handle all of the above formats.  VQEG recognizes that 1080p 50fps and 1080p 60fps are going to become more commonly used and expects to address these formats when SRC content becomes more widely available.  Ratings of hypothetical reference circuits (HRCs) for each display format used will be gathered in separate subjective tests.  The performance of submitted models will be evaluated separately by display format. The method selected for the subjective testing is Absolute Category Rating with Hidden Reference Removal. The quality predictions of the submitted models will be compared with subjective ratings from human viewers from other proponents’ submitted subjective tests.

It is also proposed that a test of currently standardized standard definition models be tested for their extensibility to High Definition TV.

The final report will summarize the results and conclusions of the analysis along with recommendations for the use of objective perceptual quality models for each HDTV format.

# Division of Labor and Schedule

The HD group wishes to proceed with the HD project before the MM and RRNR-TV projects are completed.  This test plan has been defined taking into account the limited ILG resources available, since few ILG resources are available. A number of pragmatic compromises were made to enable implementation of a test plan using minimal ILG resources while continuing to have acceptable checks on the fairness of the process.  Otherwise, the project would be required to waiting an undesirable period of time, in order to proceed with a plan that reflects ideal fairness checks.  These decisions were:

- Assign ILG only those tasks that are necessary to ensure independent validation.

- Have proponents design and implement subjective tests.

- Have proponents submit subjective test results simultaneously with models.

## ILG

The independent test group will be taking the role of independent arbitrator for the HDTV test.  The ILG role will be primarily to helping proponents decide whether their testing abides by the HDTV test plan restrictions, between the date when the HDTV test plan is finalized, and the date when models and subjective tests are submitted.  Other proponents cannot participate in these clarification decisions, since all proponent tests are supposed to be secret from other proponents.

ILG will check that proponent test designs conform to this test plan.

In addition, the ILG can optionally provide HDTV subjective testing free of charge, and submit those datasets at the model/test submission date. If too few proponents participate in the HDTV test, then one or more ILG labs will be hired to perform subjective testing, so that the restrictions concerning the minimal number of subjective datasets for the evaluation (Section 4.1) are met.

## Proponent Laboratories

Each proponent will provide one (and only one) subjective test dataset.  The subjective datasets must meet all of the test plan's constraints (e.g., identical number of video sequences and number of test subjects). If the proponent does not have the facilities to perform subjective testing, then the proponent may hire an ILG facility to perform the testing.  Proponents will submit their test designs to the ILG for checking, and if the test design changes then the proponent will submit the modified test design to the ILG for a re-check.

VQEG recognizes that a proponent’s model may have been trained on the subjective data submitted.

## Test Schedule

| 1 | Approval of test plan. |  |
| --- | --- | --- |
| 2 | Date to declare intent to participate, the number of models that will be submitted, the format of subjective test to be performed (1080i or 1080p, 25fps or 30fps), and whether 720p HRCs will be included. It is desired that all 4 types of tests are performed, and that a significant number of 720p HRCs are examined (e.g., 50% of testing). All proponents will participate in the HDTV test must specify their intent by this date. |  |
| 3 | Fee payment (if applicable) if additional ILG subjective test are required. |  |
| 4 | Donated source video sequences are collected and redistributed among labs. |  |
| 5 | Proponents wanting to use purchased SRC obtain agreement from ILG and other Proponents (see section 5). |  |
| 6 | Proponents submit source video sequences to ILG for quality approval. |  |
| 7 | Proponents submit their models to ILG and (optionally) to other proponents. | Approximately February 28, 2009 |
| 8 | Proponents using purchased SRC submit final purchase information to other proponents. |  |
| 9 | Proponents submit their SRC, PVSs, subjective data, subjective test design to ILG and all other proponents. |  |
| 10 | Calibration checked on all video sequences. PVSs needing optional calibration settings identified, and values agreed upon. |  |
| 11 | ILG decides on any PVSs that may need to be discarded. |  |
| 12 | Objective model data run on all subjective datasets. |  |
| 14 | Statistical analysis by proponents and possibly ILG. |  |
| 15 | Draft final report. |  |
| 16 | Approval of final report. |  |

# Objective Quality Models

## Model Type

VQEG HDTV has agreed that Full Reference (FR), Reduced Reference (RR) and No-reference (NR) models may be submitted for evaluation. The side channel allowable for the RR models are:

- 720p: 	(56 kbs, 128 kbs, 256 kbs)

- 1080i:	(56 kbs, 128 kbs, 256 kbs)

Proponents may submit one model of each type (FR, RR, NR) to apply to both image size conditions. Thus, any single proponent may submit up to a total of five different models. Note that where multiple models are submitted, additional model submission fees may apply.

## Full Reference Model Input & Output Data Format

The FR model will be a single program.  The model must take as input an ASCII file listing pairs of video sequence files to be processed.  Each line of this file has the following format:

<source-file>	 <processed-file>

where <source-file> is the name of a source video sequence file and <processed-file> is the name of a processed video sequence file. File names may include a path. Each line may also optionally contain calibration values.  Preferably, calibration values should appear the following order (appearing after <processed-file>):

<Y_gain> <Y_offset> <cb_gain> <cb_offset> <cr_gain> <cr_offset> <h_shift> <v_shift> <delay>

The output file is an ASCII file created by the model program, listing the name of each processed sequence and the resulting Video Quality Rating (VQR) of the model.

<processed-file>  VQR

Where <processed-file> is the name of the processed sequence run through this model, without any path information. VQR is the Video Quality Ratings produced by the objective model.

Each proponent is also allowed to output one or more files containing Model Output Values (MOVs) that the proponents consider to be important.

## Reduced Reference Model Input & Output Data Format

RR models must be submitted as two programs:

- A “source side” program that takes the original video sequence, and

- A “processed side” program that takes the processed video sequence.

Data communicated must be stored to files, which will be used to check data transmission rate.  The source side program must be able to run when the processed video is absent.  The processed side program must be able to run when the source video is absent.  Any type of model that meets these criterion may be submitted.

The input control list and output data files will be as listed for the FR model.

## No Reference Model Input & Output Data Format

The NR model will be given an ASCII file listing only processed video sequence files.  Each line of this file has the following format:

<processed-file>

where <processed-file> is the name of a processed video sequence file. File names may include a path. Each line may also optionally contain calibration values, if the proponent desires.

Output data files will be as listed for the FR model.

NR models will be required to predict the perceptual quality of both the source and processed video files used in subjective quality tests.

## 3.3	Submission of Executable Model

Proponents may submit up to five models: one full reference, one no reference, and one for each of the reduced reference information bit rates given in the test plan (i.e., 56 kbit/sec, 128 kbit/sec, 256 kbit/sec).  Each proponent will submit an executable of the model(s) to the Independent Labs Group (ILG) for validation.  Encrypted source code also may optionally be submitted. If necessary, a proponent may supply a specific computer or machine that implements the model. The ILG will verify that the software produces the same results as the proponent. If discrepancies are found, the independent and proponent laboratories will work together to correct them. If the errors cannot be corrected, then the ILG will review the results and recommend further action.

Proponents may receive other proponents’ models and perform validation, if the model’s owner finds this acceptable.  An ILG lab will be available to validate models for proponents who cannot let out their models to other proponents.

# Subjective Rating Tests

Subjective tests will be performed on two display resolutions:  720p (1280 X 720p resolution) and 1080i (1920 X 1080i resolution).  In both cases, the tests will assess the subjective quality of video material presented in a simulated viewing environment, and will deploy a variety of display technologies.

## Subjective Dataset Submission

Each proponent must submit one subjective dataset.  This dataset must comply with all restrictions in this test plan.  All of the video sequences (source and processed) and all of the subjective data must be distributed to all other proponents and also to ILG performing model validation.

Submitted subjective datasets may use source video that must be purchased (i.e., source video sequences that other proponents must purchase prior to receiving that subjective dataset).  Because the appropriateness of purchased source may depend upon the price of those sequences, the total cost must be openly discussed before a proponent chooses to use purchased source sequences (e.g., VQEG reflector, audio conference); and the seller must be identified.  (Reminder: the scenes to be purchased must be kept secret until model & subjective dataset submission). A majority of proponents must be able to purchase these source video sequence (i.e., for model validation). Proponents who use purchased SRC must either purchase the SRC for the ILG or give the ILG money to purchase that SRC. The list of SRC to be purchased must be given to the ILG, so that the ILG can make sure that multiple proponents do not purchase identical SRC. In the event that purchases source sequences are used, that laboratory must provide (along with the subjective dataset submission) the remaining details needed to purchase these source sequences. If a proponent cannot afford to purchase the source sequences, then another proponent or ILG lab will run their model against the purchased video sequences.

All subjective datasets must be held “secret” prior to model & subjective dataset submission. That is, no proponents may have any knowledge of the scenes or HRCs chosen by another proponent. That is, no other proponent can be told which scenes or HRCs will appear in other proponents’ subjective datasets.

Along with the subjective test, all laboratories will provide a file that defines the HRCs used in this subjective tests.  The file shall explicitly show the parameter values/settings used for every HRC in the test. Manufacturer names should be omitted.

## Number of Datasets to Validate Models

A minimum of four datasets will be used to validate the objective models.  These datasets may come from no fewer than three independent sources.  If less than four subjective datasets are available, then the proponents must pay for ILG laboratories to create the required subjective datasets.

There will be a minimum of three independent sources of subjective datasets (e.g., three proponents, or two proponents + one paid ILG tests); and a minimum of four independent datasets (e.g., at least four tests where each test has its own set of 160-200 PVSs (as determine above) and 24 subjects who did not participate in any of the other three tests).  Therefore, each model will be evaluated based on at least three datasets that were not used to train that model.

## Test Design

The HD Test Plan is designed as a distributed and decentralized effort of the HDTV Group.  Test designs are not expected to be the same across labs, and are subject only to the following constraints:

- Each lab will test the same number of 162 PVSs; this includes the hidden reference.

- The number of SRCs in each test is 9.

- The number of HRCs in each test is 18, including the hidden reference. (17 HRC’s, 1 Reference)

- The test design matrix need not be rectangular (“full factorial”) and will not necessarily be the same across tests.

## Subjective Test Conditions

### Application Across Different Video Formats and Displays

The proposed HDTV test will examine the performance of objective perceptual quality models for different video formats (720p and 1080i). Section 5.2.3 defines format and display types in detail.  Video applications targeted in this test include internet video on demand, HDTV broadcasts, etc.

The instructions given to subjects will request subjects to maintain a specified viewing distance from the display device. The viewing distance has been agreed as 1 minute of arc for each resolution:

- 720p: 	4H.

- 1080i:	3H.

where H = Picture Height (picture is defined as the size of the video window, not the physical display.)

### Viewing Conditions

Each test subject will have his/her own video display.  Subjects will be seated directly in line with the centre of the video display at the specified viewing distance.  The test room will conform to ITU-T Rec. P.910 requirements.

### Display Specification and Set-up

Given that the subjective tests will use different HD display technologies, it is necessary to ensure that each test laboratory selects appropriate display specification and common set-up techniques are employed. Due to the fact that most consumer grade displays employ some kind of display processing that will be difficult to account for in the models, all subjective facilities doing testing for HD TV shall use a full resolution [XXX tbd] display.

## Subjective Test Method:  ACR-HRR

The VQEG HDTV subjective tests will be performed using the ACR-HRR method.

The selected test methodology is the Absolute Category Rating method with Hidden Reference Removal (ACR-HRR).  The ACR method has been used successfully for many years [ITU-T Recommendation P.910, 1999.]  Its advantages are simplicity, that it can be applied to a relatively large number of PVSs in a short time, and that it is relatively easy to implement in computer-controlled experiments.

Hidden Reference Removal has been added to the method more recently to address a disadvantage of ACR for use in studies in which objective models must predict the subjective data:  If the original video material (SRC) is of poor quality, or if the content is simply unappealing to viewers, such a PVS could be rated low by humans and yet not appear to be degraded to an objective video quality model, especially a full-reference model.  In the HRR addition to ACR, the original version of each SRC is presented for rating somewhere in the test, without identifying it as the original.  Viewers rate the original as they rate any other PVS.  The rating score for any PVS is computed as the difference in rating between the processed version and the original of the given SRC.  Effects due to esthetic quality of the scene or to original filming quality are “differenced” out of the final PVS subjective ratings.

In the ACR-HRR test method, each test condition is presented once for subjective assessment. The test presentation order is randomized according to standard procedures (e.g., Latin or Graeco-Latin square or via computer).  Subjective ratings are reported on the five-point scale:

5  Excellent

4 Good

3 Fair

2 Poor

1 Bad.

Figure borrowed from the ITU-T P.910 (1999):

## Length of Sessions

The time of actively viewing videos and voting will be limited to 50 minutes per session.  Total session time, including instructions, warm-up, and payment, will be limited to 1.5 hours.

## Subjects

Each test will require exactly 24 subjects.

The HDTV subjective testing will be conducted using viewing tapes or the equivalent.  Video sequences may be presented from a hard disk through a computer instead of video tapes, provided that (1) playback mechanism is guaranteed to play at frame rate without dropping frames, (2) playback mechanism does not impose more distortion than the proposed video tapes (e.g., compression artifacts), and (3) monitor criteria are respected.

It is preferred that each subject be given a different randomized order of video sequences where possible. Otherwise, the viewers will be assigned to sub-groups, which will see the test sessions in different randomized orders.  At least two different randomized presentations of clips (A & B) will be created for each subjective test.  If multiple sessions are conducted (e.g., A1 and A2), then subjects will view the sessions in different orders (e.g., A1-A2, A2-A1).  Each lab should have approximately equal numbers of subjects at each randomized presentation and each ordering.

Only non-expert viewers will participate. The term non-expert is used in the sense that the viewers’ work does not involve video picture quality and they are not experienced assessors. They must not have participated in a subjective quality test over a period of six months. All viewers will be screened prior to participation for the following:

- normal (20/30) visual acuity with or without corrective glasses (per Snellen test or equivalent).

- normal colour vision (per Ishihara test or equivalent).

- familiarity with the language sufficient to comprehend instruction and to provide valid responses using the semantic judgment terms expressed in that language.

## Instructions for Subjects and Failure to Follow Instructions

For many labs, obtaining a reasonably representative sample of subjects is difficult.  Therefore, obtaining and retaining a valid data set from each subject is important.  The following procedures are highly recommended to ensure valid subjective data:

- Write out a set of instructions that the experimenter will read to each test subject.  The instructions should clearly explain why the test is being run, what the subject will see, and what the subject should do.  Pre-test the instructions with non-experts to make sure they are clear; revise as necessary.

- Explain that it is important for subjects to pay attention to the video on each trial.

- There are no “correct” ratings.  The instructions should not suggest that there is a correct rating or provide any feedback as to the “correctness” of any response.  The instructions should emphasize that the test is being conducted to learn viewers’ judgments of the quality of the samples, and that it is the subject’s opinion that determines the appropriate rating.

- Paying subjects helps keep them motivated.

If it is suspected that a subject is not responding to the video stimuli or is responding in a manner contrary to the instructions, their data may be discarded and a replacement subject can be tested.  The experimenter will report the number of subjects’ datasets discarded and the criteria for doing so.  Example criteria for discarding subjective data sets are:

- The same rating is used for all or most of the PVSs.

- The subject’s ratings correlate poorly with the average ratings from the other subjects (see Annex II).

- Different subjective experiments will be conducted by several test laboratories. Exactly 24 valid viewers per experiment will be used for data analysis. A valid viewer means a viewer whose ratings are accepted after post-experiment results screening. Post-experiment results screening is necessary to discard viewers who are suspected to have voted randomly. The rejection criteria verify the level of consistency of the scores of one viewer according to the mean score of all observers over the entire experiment. The method for post-experiment results screening is described in Annex VI. Only scores from valid viewers will be reported .

The following procedure is suggested to obtain ratings for 24 valid observers:

1.	Conduct the experiment with 24 viewers

2.	Apply post-experiment screening to eventually discard viewers who are suspected to have voted randomly

3.	If n viewers are rejected, run n additional subjects.

4.	Go back to step 2 and step 3 until valid results for 24 viewers are obtained.

## Randomization

For each subjective test, a randomization process will be used to generate orders of presentation (playlists) of video sequences. Playlists can be pre-generated offline (e.g. using separate piece of code or software) or generated by the subjective test software itself at runtime.

Randomization refers to a random permutation of the set of PVSs used in that test.

Note:	The purpose of randomization is to average out order effects, ie, contrast effects and other influences of one specific sample being played following another specific samples.  Thus, shifting does not produce a new random order , e.g.:

Subject1 = [PVS4 PVS2 PVS1 PVS3]

Subject2 = [PVS2 PVS1 PVS3 PVS4]

Subject3 = [PVS1 PVS3 PVS4 PVS2]

If a random number generator is used (as stated in section 4.1.1), it is necessary to use a different starting seed for different tests.

An example script in Matlab that creates playlists (i.e., randomized orders of presentation) is given below:

rand('state',sum(100*clock));  % generates a random starting seed

Npvs=200; % number of PVSs in the test

Nsubj=24; % number of subjects in the test

playlists=zeros(Npvs,Nsubj);

for i=1:Nsubj

playlists(:,i)=randperm(Npvs);

end

## Subjective Data File Format

Subjective data should NOT be submitted in archival form (i.e., every piece of data possible in one file). The working file should be a spreadsheet listing only the following necessary information:

- Experiment ID

- Source ID Number

- HRC ID Number

- Video File

- Each Viewer’s Rating in a separate column (Viewer ID identified in header row)

All other information should be in a separate file that can later be merged for archiving (if desired). This second file should have all the other "nice to know" information indexed to the subjectIDs: date, demographics of subject, eye exam results, etc.  A third file, possibly also indexed to lab or subject, should have ACCURATE information about the design of the HRCs and possible something about the SRCs.

An example table is shown below (where HRC “0” is the original video sequence).

|  |  |  |  | Viewer ID | Viewer ID | Viewer ID | Viewer ID | … | Viewer ID |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Experiment | SRC Num | HRC Num | File | 1 | 2 | 3 | 4 | … | 24 |
| XYZ | 1 | 1 | xyz_src1_hrc1.avi | 5 | 4 | 5 | 5 | … | 4 |
| XYZ | 2 | 1 | xyz_src2_hrc1.avi | 3 | 2 | 4 | 3 | … | 3 |
| XYZ | 1 | 7 | xyz_src1_hrc7.avi | 1 | 1 | 2 | 1 | … | 2 |
| XYZ | 3 | 0 | xyz_src3_hrc0.avi | 5 | 4 | 5 | 5 | … | 5 |

# Source Video Sequences

## Selection of Source Sequences (SRC)

Selection of source sequences will be made by the proponents. Coordination among proponents may be provided by the ILG.  Proponents can not have any knowledge of the source sequences selected for any subjective test other than their own.

## Purchased Source Sequences

See section 4.1 for constraints on the use of purchased source sequences.

## Requirements for Camera, Lens and SRC Coding

The source video can only be used in the testing if an expert in the field considers the quality to be good or excellent on an ACR-scale.  The source video should have no visible coding artifacts. 1080i footage may be de-interlaced and then used as SRC in a 1080p experiment.

The ILG will view the scene pools from all proponents and confirm that all source video sequence have sufficient quality.  The ILG will also ensure that there is a sufficient range of source material and that individual SRCs are not over-used. After the approval of the ILG, all scenes will be considered final.  No scene may be discarded or replaced after this point for any technical reason.

SRC may include 24fps content that has been frame-converted to 25fps or 30fps.

## Content

The source sequences will be representative of a range of content and applications. The list below identifies the types of test material that form the basis for selection of sequences.

1)	movies, movie trailers

2)	sports

3)	music video

4)	advertisement

5)	animation

6)	broadcasting news (business and current events)

7) 	home video

8)	general TV material (e.g., documentary, sitcom, serial television shows)

## Scene Cuts

Scene cuts shall occur at a frequency that is typical for each content category.

## Scene Duration

Final source sequences will 10 seconds.  Source scenes used for HRC creation will typically use extra content at the beginning and end.

## Source Scene Selection Criteria

Source video sequences selected for each test should adhere to the following criteria:

- All source must have the same frame rates (25fps and 30fps).

- Either all source must be interlaced; or all source must be progressive.

- At least one scene must be very difficult to code.

- At least one scene must be very easy to code.

- At least one scene must contain high spatial detail.

- At least one scene must contain high motion and/or rapid scene cuts (e.g., an object or the background moves 50+ pixels).

- If possible, one scene should have multiple objects moving in a random, unpredictable manner.

- At least one scene must be very colorful.

- If possible, one scene should contain some animation or animation overlay (e.g., cartoon, scrolling text).

- If possible, at least one scene should contain low contrast (e.g., soft or blurred edges).

- If possible, at least one scene should contain high contrast (e.g., hard or clearly focused edges, such as the SMPTE birches scene).

- If possible, at least one scene should contain low brightness (e.g., dim lighting, mostly dark).

- If possible, at least one scene should contain high brightness (e.g., predominantly white or nearly white).

# Video Format and Naming Conventions

## Storage of Video Material

Video material will be stored, rather than being presented from a live broadcast.  The most practical storage medium at the time of this Test Plan is a computer hard disk.  Hard disk drives will be used as the main storage medium for distribution of video sequences among labs.  As well, having material stored as files on a hard disk allows for randomization of the PVSs for playback to each subject (or simultaneously-viewing group).

## Video File Format

All SRC and PVSs will be stored in uncompressed AVI files in UYVY color space in 8-bit.

## Naming Conventions

All Source video sequences should be numbered (e.g., SRC 1, SRC 2).  All HRCs should be numbered, and the original video sequence must be number “0” (e.g., SRC 1 / HRC 0 is the original video sequence #1).  All files must be named: <experiment>_src<src_id>_hrc<hrc_id>.v<version #).avi, where <experiment> is a string identifying the experiment; <src_id> is that source sequence’s number, and <hrc_id> is that HRC’s number and <v> is the version number.

For example:

xyz_src01_hrc00.v1.avi

xyz_src01_hrc01.v1.avi

xyz_src01_hrc02.v1.avi

xyz_src02_hrc00.v1.avi

xyz_src02_hrc01.v1.avi

xyz_src02_hrc02.v1.avi

# HRC Constraints and Sequence Processing

## Sequence Processing Overview

The HRCs will be selected separately by the individual proponent or ILG running that test. While audio will not be used in the present tests, the audio tracks on source sequences should be retained wherever possible in both source and processed video clips (SRCs and PVSs) for use in future tests.  In cases where IP is involved in the HRC, transport streams should be saved and Ethereal dumps should be captured and stored whenever possible.

### Format Conversions

A PVS must be the same scale, resolution, and format as the original.  An HRC can include transformations such as 720p to NTSC to 720p as long as one pixel of video is displayed as one pixel native display. No up-sampling or down-sampling of the video image is allowed in the final PVS.

Where a progressive display is used and the test sample requires de-interlacing, then this de-interlacing will be performed offline, and the model will be given the same de-interlaced sample as is shown to the viewer.

### PVS Duration

PVSs to be used in testing will be 10 seconds long.  SRC may be longer and trimmed to length before testing.

## Constraints on Hypothetical Reference Circuits (HRCs)

The subjective tests will be performed to investigate a range of HRC error conditions including both mild and severe errors. These error conditions must include the following:

- Compression artifacts (such as those introduced by varying bit-rate, codec type, frame rate and so on)

- Pre- and post-processing effects

- Transmission errors

HRCs in one experiment may be the same or different from HRCs in other experiments. The HDTV group will determine an equitable way to aggregate models’ performances across different kinds of HRCs.

The overall selection of the HRCs should be done such that most, but not necessarily all, of the codecs, bit rates, encoding modes and impairments set out in the following sections are represented.

### Coding Schemes

Coding schemes that are allowed in the current tests are:

- VC1

- MPEG-2

- H.264 (AVC high profile and main profile).

- H.264 (SVC)

Coding schemes not to be included in the current test are:

- DivX

- MJPEG-2000

- Artificial impairments (e.g. Source video with frame freeze)

.

### Video Bit-Rates:

Bit rates were chosen to accommodate the coding schemes above and to span a wide range of video quality:

- 1080p: 	1–30 Mbps

- 1080i:	1–30 Mbps

### Video Encoding Modes

The encoding modes that will be used may include, but are not limited to:

- Constant-bit-rate encoding (CBR)

- Variable-bit-rate encoding (VBR)

### Frame Freezing and Frame Skipping

A frame freeze is defined as any event where the video pauses for some period of time then restarts. Frame freezes are allowed in the current testing.

Frame skipping is defined as events where some loss of video frames occurs. Frame skipping is allowed in the current testing.

Note that where skipping is included in a test then source material containing still / nearly still sections are recommended to form part of the testing.

The first and the last 1 second may only have +/- quarter second temporal shift and will not contain any anomalous frame repetitions. The maximum of total freeze is 25% of the total length of the sequence.

### Rewinding

Rewinding is not allowed impairment for the HD tests, provided that the time alignment of each frame is within the test plan limitations. Where it is difficult or impossible by a visual inspection to tell if a PVS has rewinding the PVS will be allowed in the test.

### Frame rates

For those codecs that only offer automatically-set frame rate, this rate will be decided by the codec. Some codecs will have options to set the frame rate either automatically or manually. For those codecs that have options for manually setting the frame rate, and should an HRC require a manually set frame rate, the minimum frame rate used will be 24 fps.

Manually set frame rates (new-frame refresh rate) may include:

- 1080p: 	24, 25, 29.97, 30 fps

- 1080i:	24, 25, 29.97, 30 fps

### Transmission Errors

Transmission error conditions will be included in first phase of the project.  The types of errors that may be used include packet errors (both IP and Transport Stream) such as packet loss, packet delay variation, jitter, overflow and underflow, bit errors, and over the air transmission errors. Error concealment and forward error correction should be included in at least some of the HRCs.

## Processing and Editing of Sequences

### Pre-Processing

The HRC processing may include, typically prior to the encoding, one or more of the following:

- Filtering

- De-interlacing

- Colour space conversion (e.g. from 4:2:2 to 4:2:0)

- 3:2 Pull down.

- Down and up sampling is allowed.

- Downscaling to 720p (i.e., paired with post-processing that up-scales back to 1080) is of particular interest.

This processing will be considered part of the HRC. Pre-processing should be realistic and not artificial.

### Post-Processing

Post-processing effects may be included in the preparation of test material, such as:

- Down and up sampling is allowed

- Edge enhancement

- De-blocking

Pre-processing should be realistic and not artificial.

# Calibration

## HRC Calibration Constraints

The choice of HRCs and Processing by the ILG will verify that the following limits are not exceeded between Original Source and Processed sequences:

- maximum allowable deviation in luminance gain is +/- 10%

- maximum allowable deviation in luminance offset  is +/- 20

- maximum allowable deviation in Cb and Cr gain is +/- 20%

- maximum allowable deviation in Cb and Cr offset  is +/- 20

- maximum allowable Horizontal Shift is +/- 1 pixels

- maximum allowable Vertical Shift is +/- 1 lines

- maximum allowable Horizontal Cropping is 30 pixels

- maximum allowable Vertical Cropping is 20 lines

- no Vertical or Horizontal Re-scaling is allowed

- Temporal Alignment between SRC and HRC sequences for the first 1 second and final 1 second should be maintained within +/- 0.25 seconds.  For subjective testing reasons, the temporal registration at the beginning of the sequences should match closely.  See also Section 7 for constraints regarding frame freezes, frame skipping, and rewinding.

- Dropped or Repeated Frames are excluded from above temporal alignment limit

- no visible Chroma Differential Timing is allowed

- no visible Picture Jitter is allowed

Laboratories will verify adherence of all HRCs to these limits by using at least one, but preferably two software packages (NTIA software suggested) in addition to human checking.  See also section 7.2.4 and 7.2.4, which addresses temporal alignment in response to transmission errors.

## HRC Calibration Problems

Since subjective data sets will be finalized prior to submission and remain secret until then, calibration cannot be double checked (i.e., by other proponents) until after model submission.

If a proponent identifies a calibration problem after model and dataset submission, then those calibration values will be addressed by optional allowing models to inputs calibration values.  In this case, all models must use identical calibration values – or the default “no calibration”.

# Objective Quality Model Evaluation Criteria

This section describes the evaluation metrics and procedure used to assess the performances of an objective video quality model as an estimator of video picture quality in a variety of applications.

## Evaluation Criteria

Each model will be evaluated against all datasets.  Primary analysis will consist of each model evaluated on datasets unknown to that proponent (i.e., computed by other proponents or ILG).  The dataset produced by the model’s proponent will be reported but must be clearly marked as such (e.g., “training data”).

## Evaluation Procedure

The performance of an objective quality model to each subjective dataset will be characterized by (1) calculating DMOS values, (2) mapping to the subjective scale, (3) computing the following three evaluation metrics:

- Pearson Correlation Coefficient

- Root Mean Square Error

- Outlier Ratio

along with the 95% confidence intervals of each, and finally (4) testing for statistically significant differences among the performance of various models with the F-test.

These formulae are given in the MultiMedia Test Plan, version 1.21.

Post Subissions Elimination of PVSs

We recognize that there could be potential errors and misunderstandings implementing this HDTV test plan.  No test plan is perfect.  Where something is not written or written ambiguously, this fault must be shared among all participants.  We recognize that proponents who make a good faith effort to have their subjective test conform to all aspects of this test plan may unintentionally have a few PVSs that do not conform (or may not conform, depending upon interpretation).

After model & dataset submission, SRC or HRC or PVS can be discarded if and only if:

- The discard is proposed at least one week prior a face-to-face meeting and there is no objection from any VQEG participant present at the subsequent face-to-face meeting; or

- The discard concerns a SRC not approved by the ILG or no longer available for purchase, and the discard is approved by the ILG; or

- The discard concerns an HRC or PVS which is unambiguously prohibited by Section 7 ‘HRC Creation and Sequence Processing’, and the discard is approved by the ILG; or

- The ILG determine that a submitted dataset is significantly or intentionally non-compliant with the HDTV test plan, in which case the ILG have the option to discard the entire subjective test.

Objective models may encounter a rare PVS that is slightly outside the proponent’s understanding of the test plan constraints.

# Recommendation

The VQEG will recommend methods of objective video quality assessment based on the primary evaluation metrics defined in Section 6. The Study Groups involved (ITU-T SG 12, ITU-T SG 9, and ITU-R SG 6) will make the final decision(s) on ITU Recommendations.

# References

- VQEG Phase I final report.

- VQEG Phase I Objective Test Plan.

- VQEG Phase I Subjective Test Plan.

- VQEG FR-TV Phase II Test Plan.

- Recommendation ITU-R BT.500-11.

- document 10-11Q/TEMP/28-R1.

- RR/NR-TV Test Plan

- VQEG MM Test Plan

“Overall quality assessment when targeting wide-XGA flat panel displays” by SVT Corporate Development Technology, Sweden.

[1] M. Spiegel, “Theory and problems of statistics”, McGraw Hill, 1998.

Annex I
Example Instructions to Viewers

[XXX Subject to Revision Depending on Data-Collection Method Chosen]

“In this test, we ask you to evaluate the overall quality of the video material you see.  We are interested in your opinion of the video quality of each scene.  Please do not base your opinion on the content of the scene or the quality of the acting.  Take into account the different aspects of the video quality and form your opinion based upon your total impression of the video quality.

Possible problems in quality include:

- poor, or inconsistent, reproduction of detail;

- poor reproduction of colours, brightness, or depth;

- poor reproduction of motion;

- imperfections, such as false patterns, or “snow”.

The test consists of a series of judgement trials. During each trial, two versions of a single video sequence, which may or may not differ in picture quality, will be shown in the following way:

“A” is the first version, “B” is the second version. The first presentation of a trial will be announced with the written caption “A”, and the second with “B”.  This pair of presentations will then be repeated, thereby completing a single trial.

In judging the overall quality of the presentations, we ask you to use judgement scales like the samples shown below.

# SAMPLE QUALITY SCALE

As you can see, there are two scales for each trial, one for the “A” presentation and one for the “B” presentation, since both the “A” and “B” presentations are to be judged.

The judgement scales are continuous vertical lines that are divided into five segments.  As a guide, the adjectives “excellent”, “good”, “fair”, “poor”, and “bad” have been aligned with the five segments of the scales.  You are asked to place a single horizontal line at the point on the scale that best corresponds to your judgement of the overall quality of the presentation (as shown in the example).

# You may make your mark at any point on the scale, which most precisely represents your judgement.

In making your judgements, we ask you to use the first pair of presentations in the trial to form an impression of the quality of each presentation, but to refrain from recording your judgements.  You may then use the second pair of presentations to confirm your first impressions and to record your judgements in your Response Booklet.

# We will now show you four demonstration trials.

DEMONSTRATION TRIALS PRESENTED AT THIS POINT

Annex II
Method for Post-Experiment Screening of Subjects

A statistical criterion for rejecting a subject’s data is that it correlates with the average of the other subjects’ data no better than chance.  The linear Pearson correlation coefficient per PVS for one viewer vs. all viewers is defined as:

Where

xi = MOS of all viewers per PVS

yi = 	individual score of one viewer for the corresponding PVS

n = 	number of PVSs

i = PVS index.

Rejection criterion

A subject’s data are declared to be no better than chance if they correlate less than

1.96 *( sigma sub Z) from paragraph 6.4.1 above, where .  For N = 180, sigma sub Z = 0.075, and 1.96 * sigma sub Z = 0.147.  The Fisher Z to R transformation gives the corresponding R = 0.148.  Therefore, to reject a subject’s data on the grounds of randomness,

1.	Calculate R.

2.	Exclude a viewer if R<0.15.

# Comments

Almost all of these definitions relate to frame rate (and the remainder seem to be about transmission errors.  I suggest that the entries be organized by topic rather than alphabetically, so that where possible, we define the basic terms first and those that refer to the basic terms are defined after that.  I find it confusing to navigate the way it is now, as I am always jumping from one definition to another.

Statements about formats to be used in the testing don’t belong in the definition section. This has been moved to the Introduction. .

This percentage needs to be discussed and agreed upon.

To Be Determined

Sub-committee that will own – Chulee.L, Patrick, Marcus and Kjell and Alexander

Obsolete; replace entire annex.

# Text boxes

Editors’ note:  unresolved issues or missing information are indicated by the string <<XXX>>