| INTERNATIONAL TELECOMMUNICATION UNION | STUDY GROUP 12 |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2009-2012 | TD 297rev4 (GEN/12) |
|  | English only Original: English |
| Question(s): | 14/12 | Geneva, 18-27 May 2010 |
| TEMPORARY DOCUMENT |
| Source: | Rapporteurs Q14/12 |
| Title: | Updated Draft Terms of Reference (ToR) for P.NAMS |

In this document, we present the updated Terms of Reference (ToR) for P.NAMS. This document is a modified version of the draft ToR contained in TD146rev5 (GEN/12) from November 2009.

This document incorporates changes discussed during the SG12 Meeting in March 2009 as well as additions proposed during the Q.14/12 Interim Meeting in Stockholm in June 2009. It further contains small modifications discussed at the Interim Meeting in Lulea in March 2010, and the latest addition of examples of a formate for the input side-information provided to the model.

Note that the document describes how error recovery techniques and the jitter-buffer handling will be dealt with in the final P.NAMS standard. Please refer to the P.NAMS model requirements document (TD-332-R1-GEN) for information on how the model evaluation process will be carried out, and which modes of operation will be considered during model selection.

The document is considered as the stable ToR.

ToR

The Terms of Reference for the P.NAMS model is specified in this document. The P.NAMS has two main application areas and four modes of operations, which are outlined in this document.

Scope

The current scope of P.NAMS (Non-intrusive parametric model for the assessment of performance of multimedia streaming) is given below:

This Recommendation describes an objective parametric quality assessment model that predicts the impact of observed IP network impairments on quality experienced by the end-user in multi-media mobile streaming and IPTV applications over transport formats such as: RTP (over UDP), MPEG2-TS (over UDP or RTP/UDP), 3GPP-PSS (over RTP).

This model is restricted to information contained in packet headers, prior knowledge about the media stream and buffering information from the client. Information from decoding the bit-stream or parsing the packet payload is not used.

This model predicts Mean Opinion Scores (MOS) on a 5-point ACR scale (see ITU-T Rec. P.910) for audio and video parts of the stream, as well as a global multi-media MOS score (as defined in ITU-T Rec P.911, for instance).

The primary applications for this model are monitoring of transmission quality for operations and maintenance purposes. The P.NAMS model may be deployed both in end-point locations and at mid-network monitoring points. The location of the model together with the location of the measurement probe determine the mode of operation.

The primary quality prediction made by such a model is not based on the payload of the stream being analysed, but assumes a generic, audiovisual payload.

This Recommendation cannot provide a comprehensive evaluation of transmission quality as perceived by a particular end-user because its scores reflect the impairments on the IP network being measured, that may only be part of the end-to-end connection. Furthermore, the scores predicted by a parametric model (i.e. without access to content) necessarily reflect an average perceptual impairment. However, the model specifically considers aspects of error correction such as Forward Error Correction or packet retransmission, even if the resulting, corrected packet stream is not available as an input.

The effects of audio level, noise, delay, (and corresponding similar video factors) and other impairments related to the payload are not reflected in the scores computed by such a model. Therefore, it is possible to have high scores with this Recommendation, yet have a poor quality of the stream overall.

The audio model is considered as a part of P.NAMS that may be taken up in other standardization activities such as P.NBAMS or a stand-alone audio model. Consequently, care is taken that the application range for the audio model is designed to be slightly larger than necessary for a component of an audiovisual model applied to services as considered for the P.NAMS activity.

General Application areas

The two application areas for P.NAMS are:

- QCIF-QVGA (also known as "low bitrate mode", LBR), mostly for mobile TV and Streaming with the sub application areas:

  - Linear Mobile TV over RTP (includes Mobile TV over a 3G mobile network with MBMS and with unicast, transport over RTP/UDP/IP)

  - Multimedia streaming (includes 3GPP PSS with transport over RTP/UDP/IP)

  - Progressive download (involving e.g. HTTP/TCP/IP, or [RTP/]TCP/IP)

- SD and HD television (also known as  "high bitrate mode", HBR), mostly for IPTV with the sub application areas:

  - Linear broadcast TV (includes transmission over MPEG2-TS/RTP/UDP/IP, MPEG2-TS/UDP/IP and RTP/UDP/IP transport)

  - Video on-demand (includes transmission over MPEG2-TS/RTP/UDP/IP, MPEG2-TS/UDP/IP and RTP/UDP/IP transport)

  - Progressive download (involving e.g. HTTP/TCP/IP, MPEG2-TS/TCP/IP or [RTP/]TCP/IP)

Modes of operations

The four modes of operations are described in Table 1 and Figures 1 a) to e) below.

| Class | Name | Mode abbreviation* | Description |
| --- | --- | --- | --- |
| Mid-point or End-point | Static Operation | NN | The model uses information from the local transport layer, prior knowledge about coding and prior knowledge about the end-point. |
| Mid-Point | Non-embedded Dynamic Operation | BN | The model uses information from the local transport layer, prior knowledge about coding and information about the end-point collected through measurement reporting protocols |
| Mid-Point | Non-embedded Distributed Operation | CN | The model, located inside the network, uses information from the transport layer measured at an end-point and collected through signalling protocols, prior knowledge about coding and information about the end-point collected through signalling protocols |
| End-point | Embedded Operation | CC | The model uses information from the local transport layer, information from the end-point, and prior knowledge about coding |

Table 1: Modes of operations of P.NAMS.

*Mode abbreviation naming scheme:

XY, where

X corresponds to place of measurement (N: Network, C: Client, B: Both network and client)

Y corresponds to place of model (N: Network, C: Client)

Figure 1 a): Static operation mode (NN) inside the network

Figure 1 b): Static operation mode (NN) inside a terminal

Figure 1 c): Non-embedded dynamic operation mode (BN)

Figure 1 d): Non-embedded distributed operation mode (CN)

Figure 1 e): Embedded operation mode (CC)

Building blocks

A possible layout of the P.NAMS model is represented by the building blocks depicted in the Figure 2 below. Figure 3 shows how the case of error resilience methods such as Forward Error Correction (FEC) and Automatic Repeat reQuest (ARQ) is planned to be handled in case of the NN mode; here, due to the measurement in the network, the stream has not been corrected by the resilience methods. The P.NAMS recommendation will contain a specification of how this handling recommended to be done. See Section 5 for more details.

Figure 2: P.NAMS Building blocks; see following sections for more details on the model input provided from the parameter extraction module.

Model Input

The P.NAMS model will receive transport layer information, client information, and prior knowledge about the media stream. The overview information per application area and mode is described in Table 2 below:

|  | Static Operation (NN) | Non-embedded Dynamic Operation (BN) | Non-embedded Distributed Operation (CN) | Embedded Operation (CC) |
| --- | --- | --- | --- | --- |
| Mobile application area - Low bitrate mode | I.1: Prior knowledge about audio and video coding, and end-point as described in section 5.1 I.2: PCAP file [5] without payload I.3: Output P-E (no additional info). | I.1: Prior knowledge about audio and video coding as described in section 5.1 Note: endpoint information provided via signaling and included in I.3 I.2: PCAP file [5] without payload I.3: Output P-E plus additional end-point information. | I.1: Prior knowledge about audio and video coding as described in section 5.1 Note: endpoint information and measurements provided via signaling and included in I.3 I.2: PCAP file [5] provided to specific P-E module situated in end-point. I.3: Output from P-E module in end-point. (see I.2) Parameters as specified for QoE reporting for the 3GPP services PSS and MBMS. See reference [1] and [2] (to be agreed) | I.1: Prior knowledge about audio and video coding; and end-point as described in section 5.1 I.2: PCAP file [5] I.3: Output P-E (no additional info) |
| High bit-rate mode | I.1: Prior knowledge about audio and video coding, and end-point as described in section 5.1 I.2: PCAP file [5] without payload I.3: Output P-E (no additional info). | I.1: Prior knowledge about audio and video coding as described in section 5.1 Note: endpoint information provided via signaling and included in I.3 I.2: PCAP file [5] without payload I.3: Output P-E plus additional end-point information. | I.1: Prior knowledge about audio and video coding as described in section 5.1 Note: endpoint information and measurements provided via signaling and included in I.3 I.2: PCAP file [5] provided to specific P-E module situated in end-point. I.3: Output from P-E module in end-point. (see I.2) Note: Protocol for parameter transmission as specified by other forums, such as Broadband Forum (specification TR-135 reference [3] could be extended to support this) or adaptations of RTCP XR ( IETF, see [4]) | I.1: Prior knowledge about audio and video coding; and end-point as described in section 5.1 I.2: PCAP file [5] I.3: Output P-E (no additional info) |

Table 2a: Overview of input to the P.NAMS application areas and modes of operation

The following Table 2b gives more detailed examples of information that is provided at the input interfaces I.1 (see Figure 2) in terms of prior knowledge.

| Modes | Parameter | Description | Notes |
| --- | --- | --- | --- |
| All | Server information | Streaming server and settings used |  |
| All | Audio encoder | Audio encoder and settings used |  |
| All | Video encoder | Video encoder and settings used | Settings could include: GOP structure... |
| All | Audio decoder | Audio decoder and settings used |  |
| All | Video decoder | Video decoder and settings used |  |
| All | Client | Client identifier |  |
|  | Client buffer size | Size of client buffer | pkts/bytes/ms? |
|  | Client buffer behaviour | Freezing with or without re-buffering |  |
| All | Video resolution | Image size (e.g. QCIF) |  |
| All | Audio bandwidth | The context in which the audio signal should be assessed | NB, WB, SWB, FB |
| All | Audio frame length | Length of audio frames in ms |  |
| All | Payload-unit-start indicator | Information on whether payload-unit-start indicator in TS header means the start of frame or of slice |  |
| All | Random-access indicator | Information on whether random-access indicator in TS header means the start of I-frame or of IDR-frame |  |
| All | Elementary-stream priority indicator | Information on whether elementary-stream-priority indicator in TS header means the start of I-frame or of IDR-frame |  |
| All | Marker bit | Information on whether marker bit in RTP header means the start of frame or of slice |  |

Table 2b: Examples of information available at Input I.1, prior knowledge.

Note that for the modes CC, CN and BN and UDP-based transport, it is assumed that the available information already reflects the impact of the employed Forward Error Correction (FEC), packet re-transmission mechanisms such as Automatic Repeat reQuest (ARQ), and the de-jitter buffer, since the parameter extraction module is located behind these processing steps. In case of the NN mode, the measurement point is located prior to the actual FEC, ARQ and de-jitter buffer mechanisms. Since these mechanisms may have a very strong impact on factors such as the packet loss seen by the decoder, the NN-mode requires an explicit handling of these mechanisms. Two principle approaches are conceivable to capture this case, which are both based on prior knowledge:

- The packet stream S is converted into a stream that reflects an assumed behaviour of FEC, ARQ, and/or jitter de-buffering, reflecting the input format to be provided to the parameter extraction module (PCAP). This step results in a converted stream S’, see Figure 3.

- The input parameters to the model are converted into values that reflect the application of FEC, ARQ and/or de-jitter buffering (module ”loss-related parameter mapping” in Figure 3).

For the basic operation of the model described in this ToR, option b) is chosen.

As an example, the packet loss rate may be converted into the packet loss rate to be expected after FEC, ARQ and/or de-jitter-buffering. The conversion of this or other packet-loss distribution related parameters will be a part of the P.NAMS standard, and is currently being developped in a collaboration with Q.17/12..

In the CC mode, an implementation of the model can be achieved that ensures that the results of the client-behaviour (buffering) and potential error recovery mechanisms (Automatic Repeat reQuest, ARQ; Forward Error Correction, FEC) are available as explicit information to the P.NAMS model. Here, the result of error recovery techniques is explicitly contained in the PCAP-files, which forms the main input information to the P.NAMS model. Information in terms of prior knowledge and side-information on the effect of buffering will be provided to the P.NAMS-model in additional files beside the PCAP-files.

Note that FEC and ARQ are not relevant for mobile Video services, and hence are not considered in the LBR-case.

The TCP-inherent ARQ-like mechanism of retransmission is thought to be conveniently captured at a well chosen measurement point, regardless of the mode of operation. Consequently, in case of TCP-based transport, it is assumed that all retransmission-related information is available to the model, and no explicit handling of ARQ like in the UDP-based transport is required (see above explanations for UDP). This, in turn, requires that for TCP-based transport the parameter extraction module considers all available packets including the retransmitted ones.

5.1 Side information to the PCAP-file

Pre-gathered side information that is supposed to be input to the model is added in a separate text file to be considered as “pre-info text file”. If a buffering event has occurred, with or without skipping, a second text file should be supplied in addition to each pcap-file. This file is referred to as a “buffer text file”.

An example, tab separated txt-document format may look as follows (for a video only file, using mpegTS; for details on the final format please refer to the “P.NAMS Testplan” Document):

--- %%% Pre-info Text File Starts %%% ---

pcapFileName	"filename.pcap"

videoCodec	H264

videoResolution	720P

payloadUnitStartIndicator	START

clientBufferBehaviour	WITHOUTSKIPPING

randomAccessIndicator	IDR

elementaryStreamPriorityIndicator	I

--- %%% File Ends %%% ---

Each line is printed in the style "parameterName\tVALUE\n".

There are more parameters that can be entered for other examples, audio parameters for files that include audio etc. An example for a full list of parameters is included below. Parameters that are not valid for the specific file are not entered in the pre-info text file.

List of parameters (followed by a comment, if any):

modelMode					[CN, CC, NN, BN]

pcapFileName				[pathname.pcap]

transportFormat				[RTP/UDP/IP, TS/TCP/IP etc]

videoCodec					[H264, H263, MPEG4 etc]

videoCodecProfile			[SIMPLE, BASELINE etc]

videoResolution				[QCIF, HVGA, 720P, 576P etc]

videoFrameRate				[24, 25, 30 etc]

audioCodec					[AMRNB, AMRWBP, AAC-HE etc]

audioBandwidth				[NB, WB, SWB, FB]

audioFrameLength			[in ms]

nrAudioFramesPerPacket	[1,2 etc]

clientBufferBehaviour		[WITHSKIPPING, WITHOUTSKIPPING]

randomAccessIndicator	[I, IDR]

elementaryStreamPriority	[I, IDR]

payloadUnitStartIndicator	[START, END]

markerBit					[START, END]

Buffering can be expressed in terms of a "normalized time (TSsec)" in seconds calculated from the TS (instead of using samples/Hz). The first frame in the video is TSsec = 0s.

Buffering information for a media clip that has buffering is planned to be provided as a tab separated text file with one line per buffering event, the buffer text file. The “clientBufferBehaviour” entry in the pre-info text file here indicates whether the buffering events are with or without skipping.

A possible format for the buffer info text file may look like this (for information on the final file formate please refer to the “P.NAMS Testplan” document):

bufferStartTime\tbufferLength\n

0.137	3.200

5.000	0.543

Here, whitespace characters between numbers are referred to by \t and line endings by \n.

Model Output

The P.NAMS model outputs O.1, O.2 and O.3 (see Figure 2) are the estimated multimedia (audiovisual) MOS (O.1), and a separate video (O.2) and audio MOS (O.3). P.NAMS will have four modes, providing a different MOS outputs for the two video resolutions for the two different application areas, see Sections 2 and 3.

Optional parameters for diagnostic purposes can be found in the (non-exhaustive) list below:

- Jitter buffer size

- Bit rate (audio and video)

- Packet-loss ratio (audio and video)

- Packet-discard ratio (audio and video)

- Averaged burst packet loss length (audio and video)

- Burst packet loss variation range

- Mean packet size

- Delay

- Delay variation range

Application Range

In the following, the application ranges for the two application areas are defined in more detail (see Table 3 for the mobile, and Table 4 for the IPTV-case).

The four last columns of Table 3 and 4 give an indication on whether the respective information is considered as available for the respective operation mode. In case that the application information is not or only partly provided, corresponding additional specifications are required. An example for such a case is given in the end of the table for packet loss degradation: Here, in the NN-mode, only the loss- and jitter-information given at the measurement point in the network can be obtained; hence, in case that FEC, or resend-mechanisms are used, or that the joint effect of measured jitter and an assumed jitter buffer behaviour are to be included, corresponding conversions from the measured data to the data relevant at client level are desired (see section 5).

  - Application Range for Mobile Application Area

[Editor’s note : All aspects shown with yellow highlighting will be agreed on during further P.NAMS model development.]

| Application information | Value range, unit | Comments |
| --- | --- | --- |
|  |  | Mode NN | Mode BN | Mode CN | Mode CC |
| Sequence duration (Ts) | SRC lengths 10s: no rebuffering 16s: rebuffering PVS length SRC length + rebuffering length (no rebuffering at end and start) Note: During P.NAMS tests a specific test on rebuffering with different rebuffering durations and different source sequence durations may be carried out (in that case maintaining the same PVS duration for all items) |  |  |  |  |
| Packetization | 3GPP MBMS, PSS or using RTSP directly (all three over RTP/UDP/IP) HTTP/TCP/IP, or [RTP/]TCP/IP |  |  |  |  |
| Video codec | MPEG4 Visual Simple Profile (VSP) H.264 baseline profile |  |  |  |  |
| Video size | QCIF, QVGA, HVGA |  |  |  |  |
| Audio codec | AMR-NB, AMR-WB+, AAC-LC, HE-AAC (v1, v2) tbd. |  |  |  |  |
| Coded video bitrate | QCIF: default 80 kbps, 32 - 256 kbps QVGA: default 250 kbps, 80 - 800 kbps HVGA: 150 - 2000 kbps (provisionally agreed) |  |  |  |  |
| Coded audio bitrate | AMR-NB: 4.75-12.2 kbps AMR-WB+: 6.6-48 kbps AAC-LC: 16-128 kbps HE-AAC (v1, v2) tbd. |  |  |  |  |
| Decoder packet loss concealment | Two types of assumed decoder behaviour: 1) Freezing with skipping, 2) slicing with N slices/frame, PLC to be agreed (e.g. fixed decoder) |  |  |  |  |
| Client jitter buffer behaviour | Rebuffering handling, particular to LBR-case; freezing with and without skipping of length 0 to Y seconds (Y tbd., depends on source sequence length) | Jitter buffer emulation (PCAP-file conversion or parameter conversion, see Figure 2) Specify maximum delay variation Tmax to be handled; tbd with Q.17/12 | Depends on reporting protocol Tbd. | Depends on reporting protocol. Examples are 3GPP PSS or MBMS QoE Reporting, see reference [1] And [2] Tbd. | Measure-ment after de-jitter buffering available |
| Encoder implementation | Default mode for specific/ typical encoder (to be agreed) Tbd. Optional guidance on how to adjust model-parameters to specific encoders will be given in an Appendix or a separate Recommendation (cf. e.g. P.833 for E-model Impairment Factors) |  |  |  |  |
| Decoder implementation | Reference decoder, tbd. Guidance on how to adjust internal model parameters for specific other decoders incl. set-top boxes to be added as Appendix of Recommendation or stand-alone Rec. (see decoder PLC) |  |  |  |  |
| Group of pictures (GoP) | GOP-structure may be estimated from stream. Default mode for typical GoP Structure (tbd.) e.g., M = 1, N = 40 (typically no B frames for mobile case) Length: fixed, variable, adaptive Structure (e.g.: IPPP...PPPI) Optinal solution for adjustment could appear in Appendix of Pecommendation or be handled in separate Recommendation |  |  |  |  |
| Frame rate | To be agreed: 5, 8.33, 12.5, 15, 20, 25, 30 fps |  |  |  |  |
| Information on whether marker bit in RTP header means the end of a frame or of a slice | Boolean |  |  |  |  |
| Type of Audio Content | Range tbd. | Possibly based on packet heuristics | Possibly based on packet heuristics | Possibly based on packet heuristics | Possibly based on packet heuristics |
| Type of Video Content | Range tbd. | Possibly based on packet heuristics | Possibly based on packet heuristics | Possibly based on packet heuristics | Possibly based on packet heuristics |
| Type of Audiovisual Content | Should include audio (spoken voices, background noise, music) Different levels of complexity and motion, for both video and audio Ideally, audio and video material derived from audiovisual material Range tbd. |  |  |  |  |
| Audio channel number | 1 (mono), 2 (stereo) |  |  |  |  |
| # of Audio frames per packet | 1 frame/packet (provisionally agreed) |  |  |  |  |
| Audio-video multiplexed? | Default: No (provisionally agreed) |  |  |  |  |
| Packet loss degradation, video | Uniform loss: 0-10% (provisionally agreed) Burst loss: 0-10%, values to be agreed as well as additional parameters (collaboration with Q.17/12, examples are loss and gap run-lengths, etc., e.g. based on N-state Markov model) | FEC and ARQ assumed to not play a role for LBR. |  | PL properties. Examples is 3GPP PSS, see [1] |  |
| Packet loss degradation, audio | Uniform loss: 0-10% (provisionally agreed) Burst loss: 0-10%, values to be agreed as well as additional parameters (collaboration with Q.17/12, examples are loss and gap run-lengths, etc., e.g. based on N-state Markov model) | FEC and ARQ assumed to not play a role for LBR. |  | PL properties Examples is 3GPP PSS [1]. |  |
| Symmetrical vs asymmetrical handling of audio and video in audiovisual case | Model application: Symmetrical Model development: Some asymmetric cases may be considered |  |  |  |  |

Table 3: Overview of application range of P.NAMS for the mobile application area.

  - Application Range for IPTV Application Area

[Editor’s note : All aspects shown with yellow highlighting will be agreed on during further P.NAMS model development]

| Application information | Value range, unit | Comments |
| --- | --- | --- |
|  |  | Mode NN | Mode BN | Mode CN | Mode CC |
| Sequence duration (Ts) | SRC length: 10s PVS length = SRC length |  |  |  |  |
| Packetization | MPEG2-TS/RTP/UDP/IP RTP/UDP/IP MPEG2-TS/UDP/IP HTTP/TCP/IP, MPEG2-TS/TCP/IP, or [RTP/]TCP/IP (provisionally agreed) |  |  |  |  |
| Video codec | MPEG2, H.264: H.264 baseline profile, H.264 main profile, H.264 high profile |  |  |  |  |
| Video size | SD: PAL, NTSC HD: 720p, 1080p, 1080i |  |  |  |  |
| Audio codec | AAC-LC HE-AAC (V1 and V2) MPEG-1 Layer 2 MPEG-1 Layer 3 (needs further discussion) MPEG-2 audio |  |  |  |  |
| Coded video bitrate | HD MPEG2: default 15 Mbps, 6 - 22 Mbps H.264: default 9 Mbps, 3 - 15 Mbps SD MPEG2: default 4 Mbps, 3 - 15 Mbps H.264: default 2.1 Mbps, 1.5 up to 8 Mbps (provisionally agreed) |  |  |  |  |
| Coded audio bitrate | AAC-LC: 64-256 kbps HE AAC: 32-96 kbps MPEG-1 Layer 2: 64-384 kbps MPEG-1 Layer 3: 64-256 kbps (the above two need further discussion) MPEG-2 audio: 96-192 kbps (provisionally agreed) |  |  |  |  |
| Video decoder packet loss concealment | Types of assumed decoder behaviour: 2 dimensions: Slicing, PLC 1) Freezing with skipping (T(SRC)=T(PVS)), 2) slicing with 1 slices/frame, no PLC. 3) slicing with N slices/frame, PLC to be agreed (e.g. fixed decoder) |  |  |  |  |
| Audio decoder packet loss concealment | Decoder default modes (provisionally agreed) |  |  |  |  |
| Retransmission mechanisms (ARQ); Forward Error Correction (FEC) | Type and range tbd. | PCAP-file conversion or parameter conversion, for the latter see Figure 2: Extra box internal to P.NAMS, will be developed separately to convert packet loss related parameters to the corrected case. Under development with Q.17/12 1) Required: Loss-rate -conversion 2) optional burst-related measure 3) optional: additional parameters | Measure-ment after ARQ, FEC available, depends on description protocols in same way as for parameters when no ARQ is used, see below | Measure-ment after ARQ, FEC available, depends on description protocols in same way as for parameters when no ARQ is used, see below | Measure-ment after ARQ, FEC available |
| Client jitter buffer behaviour | tbd. | Jitter buffer emulation (PCAP-file conversion or parameter conversion, see Figure 2) Tbd with Q.17/12 1) Required: Loss-rate -conversion 2) optional burst-related measure 3) optional: additional parameters | Depends on reporting protocol. Protocol for parameter transmission as specified by other forums, such as Broadband Forum (specification TR-135 reference [3] could be extended to support this) or an adaptation of RTCP XR [4]. tbd | Depends on reporting protocol. Protocol for parameter transmission as specified by other forums, such as Broadband Forum (specification TR-135 reference [3] could be extended to support this) or an adaptation of RTCP XR [4]. tbd | Measure-ment after de-jitter buffering available |
| Type of Audio Content | Range tbd. | Possibly based on packet heuristics | Possibly based on packet heuristics | Possibly based on packet heuristics | Possibly based on packet heuristics |
| Type of Video Content | Range tbd. | Possibly based on packet heuristics | Possibly based on packet heuristics | Possibly based on packet heuristics | Possibly based on packet heuristics |
| Type of Audiovisual Content | Should include audio (spoken voices, background noise, music) Different levels of complexity and motion, for both video and audio Ideally, audio and video material derived from audiovisual material Range tbd. |  |  |  |  |
| Encoder implementation | Default mode for specific/ typical encoder (which encoder used tbd.) Optional guidance on how to adjust model-parameters to specific encoders will be given in an Appendix or a separate Recommendation (cf. e.g. P.833 for E-model Impairment Factors) |  |  |  |  |
| Decoder implementation | Reference decoders, tbd. Aspects NOT covered by decoder packet loss concealment: - postfiltering - de-interlacing Guidance on how to adjust internal model parameters for specific other decoders incl. set-top boxes to be added as Appendix of Recommendation or stand-alone Rec. (see decoder PLC) |  |  |  |  |
| Group of pictures (GoP) | Default modes for typical GoP Structures (provisionally agreed) E.g., M = 3, N = 15 Length: fixed, variable, adaptive Structure (e.g.: IBBPBB...PBBI) Optional solution for adjustment in Appendix. Note: GOP-structure may explicitly be estimated from stream. |  |  |  |  |
| Frame rate | To be agreed: SD: 50i, 25p, 29.97, 59.94 HD: 50p, 50i, 25p, 29.97, 30p, (24p), 59.94 |  |  |  |  |
| Audio channel number | 1 (mono), 2 (stereo) |  |  |  |  |
| # of Audio frames per packet | tbd. |  |  |  |  |
| Audio-video multiplexed? | Depends on transport mechanism |  |  |  |  |
| Encrypted payload | Yes and No Level of encryption: Assumption is that only the payload is encrypted… |  |  |  |  |
| Information on whether payload-unit-start indicator in TS header means the start of frame or of slice | Boolean |  |  |  |  |
| Information on whether marker bit in RTP header means the start of frame or of slice | Boolean |  |  |  |  |
| Information on whether random-access indicator in TS header means the start of I-frame or of IDR-frame | Boolean |  |  |  |  |
| Information on whether elementary-stream-propriety indicator in TS header means the start of I-frame or of IDR-frame | Boolean |  |  |  |  |
| Packet loss degradation, video | Uniform loss: 0-4% (provisionally agreed; model will mainly be used for well-managed or partially managed networks (see G.1050), i.e. in packet loss range 0-2%) Burst loss: 0-2%, values to be agreed as well as additional parameters (collaboration with Q.17/12, examples are loss and gap run-lengths, etc., e.g. based on N-state Markov model) | FEC and ARQ emulated either in terms of PCAP-conversion or in terms of loss parameter conversion (see Fig. 2, 1.C) under development with Q.17/12. Will be tested together with all other modes of operation in subjective tests, but models fed with either converted PCAP-files or parameters. |  | Detailed information available depends on the protocol used for reporting measurement data |  |
| Packet loss degradation, audio | Uniform loss: 0-10% (provisionally agreed; model will mainly be used for well-managed or partially managed networks (see G.1050), i.e. in packet loss range 0-2%) Burst loss: 0-10%, values to be agreed as well as additional parameters (collaboration with Q.17/12, examples are loss and gap run-lengths, etc., e.g. based on N-state Markov model) | FEC and ARQ emulated either in terms of PCAP-conversion or in terms of loss parameter conversion (see Fig. 2, 1.C) under development with Q.17/12 Will be tested together with all other modes of operation in subjective tests, but models fed with either converted PCAP-files or parameters. |  | Detailed information available depends on the protocol used for reporting measurement data |  |
| Packet loss degradation, audiovisual | Uniform loss: 0-5% (provisionally agreed) Burst loss: tbd. | FEC and ARQ emulated either in terms of PCAP-conversion or in terms of loss parameter conversion (see Fig. 2, 1.C) under development with Q.17/12 Will be tested together with all other modes of operation in subjective tests, but models fed with either converted PCAP-files or parameters. |  | Detailed information available depends on the protocol used for reporting measurement data |  |
| Symmetrical vs asymmetrical handling of audio and video in audiovisual case | Model application: Symmetrical Model development: Some asymmetric cases may be considered |  |  |  |  |

Table 4: Overview of application range of P.NAMS for the IPTV application area.

References

[1]	3GPP TS 26.234 “Transparent end-to-end Packet-switched Streaming Service (PSS); Protocols and codecs”

[2]	3GPP TS 26.364 “Multimedia Broadcast/Multicast Service (MBMS); 
Protocols and codecs “

[3]	Broadband Forum Technical Report. TR-135. “Data Model for a TR-069 Enabled STB”. Version: Issue 1. December 2007.

[4]	IETF RFC 3611 “RTP Control Protocol Extended Reports (RTCP XR)”, November 2003.

[5]	Development/LibcapFileFormat, http://wiki.wireshark.org/Development/LibpcapFileFormat.

______________

# Text boxes

Figure 3: Options for handling of FEC/ARQ in P.NAMS, parameter extraction module (P-E). Note that the “Loss-related parameter mapping” module is considered transparent for all non loss-related parameters.