## Slide 1: Comparison of subjective scores between the tests using consumer and professional 4K monitors
Osamu Sugimoto
KDDI R&D Laboratories, Inc.

## Slide 2: Introduction
Professional equipment of 4K video is expensive.
Use of consumer products as we did in HDTV phase1 test should be considered.
This study:
  How subjective test scores correlates when we run subjective tests using the professional and consumer grade monitors?

## Slide 3: 4K monitors
Monitors
  Professional LCD: Astrodesign DM-3410A http://www.astrodesign.co.jp/english/product/dm-3428-dm-3410-a
  Consumer LCD: Toshiba 55X3 (sold as 55ZL2 in European market) http://eu.consumer.toshiba.eu/en/products/tv/55ZL2
 | Consumer | Professional
Model Num. | Toshiba 55X3 | Astrodesign DM3410-A
Panel Size | 55” | 56”
Panel Resolution | 3840x2160 | 3840x2160
Brightness | N/A | 350cd/m2
Contrast Ratio | 1:5000 | 1:950
Notes: Astro: 50-60KUSD
Toshiba: 9-10K

## Slide 4: Subjective test
Test method: DSCQS
Viewing Distance: 3H (H=screen height)
Number of subjects: 24
Test materials
  10 sequences of 10 sec from KDDI’s own 4K footages
  Format: 3840x2160,30fps, progressive
Coding Condition
  H.264(JM15.1): 8,16Mbps (IBBPBBPBBPBBPBB) Rate control Enabled HEVC(HM6.1) : 4,8,16Mbps (IBBBBBBBBBBBBBB) Fixed QP
Professional
Consumer
3H
3H
HDD Recorder
Subjects

## Slide 5: Comparison of DMOS
Chart: DMOS with Professional LCD
| 11.78260869565217 | 1.478260869565217 | -0.869565217391304 | 23.56521739130435 | 1.130434782608696 | 46.82608695652174 | 19.60869565217391 | -1.91304347826087 | 10.34782608695652 | 0.695652173913043 | 2.695652173913043 | 24.69565217391304 | 5.217391304347826 | 4.304347826086956 | -0.304347826086956 | -0.869565217391304 | 1.91304347826087 | 9.73913043478261 | 14.30434782608696 | 4.043478260869565 | 57.52173913043478 | 28.21739130434782 | 14.8695652173913 | 20.30434782608696 | 12.91304347826087 | 5.826086956521739 | 12.60869565217391 | -3.130434782608696 | -6.043478260869565
HEVC PVS | 20.087 | 5.8261 | 0.95652 | 22.5652 | 9.4348 | 50.4783 | 35.087 | 12.3478 | 23.6957 | 7.0435 | 2 | 36.6957 | 18.3043 | 3.1739 | 3.6087 | 0.95652 | 2.5217 | 10.6957 | 2.6087 | 2.9565 | 59.7391 | 28.3478 | 10.4783 | 22.3913 | 12.5652 | 4.7391 | 8.9565 | 5.2609 | 5.087
H.264 PVS | 21.2609 | 4.7391 | 28.0435 | 23.1304 | 57.5217 | 27.2609 | 42 | 6.1304 | 29.2609 | 16 | 17.4783 | 2.1739 | 14.1739 | 5.6087 | 38.1304 | 11.7826 | 27.5217 | 10.2174 | 6.5217 | -1.1304
 | 20.087 | 5.8261 | 0.95652 | 22.5652 | 9.4348 | 50.4783 | 35.087 | 12.3478 | 23.6957 | 7.0435 | 2 | 36.6957 | 18.3043 | 3.1739 | 3.6087 | 0.95652 | 2.5217 | 10.6957 | 2.6087 | 2.9565 | 59.7391 | 28.3478 | 10.4783 | 22.3913 | 12.5652 | 4.7391 | 8.9565 | 5.2609 | 5.087 | 21.2609 | 4.7391 | 28.0435 | 23.1304 | 57.5217 | 27.2609 | 42 | 6.1304 | 29.2609 | 16 | 17.4783 | 2.1739 | 14.1739 | 5.6087 | 38.1304 | 11.7826 | 27.5217 | 10.2174 | 6.5217 | -1.1304
Correlation Coef=0.911

## Slide 6: Conclusion
Two subjective test results using consumer/professional 4K monitors are compared.
We may use consumer 4K monitors for VQEG test since it has high correlation with professional ones (R=0.91), but further study seems to be required.