| INTERNATIONAL TELECOMMUNICATION UNION | STUDY GROUP 9 |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2009-2012 | TD 340 Rev.1 (GEN/9) |
|  | English only Original: English |
| Question(s): | 12/9 | Geneva 3-11 December, 2013 |
| TD |
| Source: | Editors |
| Title: | Output – Draft New Recommendation- P.3D-fatigue “Information and guidelines for assessing and minimizing visual discomfort and visual fatigue from 3D video ” |

Note: This document represents the output from Q12/9 session during SG 9 meeting, 3-11 December 2013. It provide revisions based on the previous TD 846 (GEN/9). Note that the series was changed  from J.3D-fatigue to P.3D-fatigue.

----------------<Recommendation No.>

Draft New Recommendation P.3D-fatigue: Information and guidelines for assessing and minimizing visual discomfort and visual fatigue from 3D video

AAP Summary

<to be added before consent>

Summary

[Editor’s note: update this summary to better match the edited document. The last bit (viewing environment & viewing time) in particular seem inappropriate. (Margaret)]

This Recommendation addresses issues related to assessing and minimizing visual discomfort and visual fatigue from 3D video. Issues addressed include 3D video characteristics that cause visual discomfort, symptoms of visual fatigue, viewing environment considerations, and viewing time considerations.

Keywords

This clause is intentionally left blank.

Introduction

3DTV systems are based on binocular disparity. Compared to the real world scenario, the reproduction of depth in 3DTV systems is limited to by the camera position, number of cameras, source content, and the technical limitations of the display technique. These include to resolution, frame rate, and view separation conditions. Current display technologies may also induce a conflict between accommodation (eyes focusing on the screen) and the convergence (eyes converging to a point in front of or behind the screen). These limitations can cause visual discomfort and visual fatigue.

# 1	Scope

This Recommendation includes information and guidelines for assessing and avoiding visual discomfort and visual fatigue from 3D video. It describes potential causes of visual discomfort and symptoms of 3D visual fatigue, including problems caused by watching stereoscopic and autostereoscopic television. This information is primarily intended to be used for the design and conduct of subjective assessment of the video or audiovisual quality of 3D video. It is appropriate for all 3D viewing experiences.

1.1	 Limitations

This Recommendation includes guidance on recognizing visual fatigue symptoms and identifying 3D programming clip characteristics that may cause visual fatigue.

This Recommendation excludes objective assessment methods of 3D visual fatigue, because these are not computational algorithms but rather correspond to a medical diagnostic process performed by medical doctors.

# 2	References

None.

# 3	Definitions

## 3.2	Terms defined elsewhere

None.

## 3.2	Terms defined in this Recommendation

This Recommendation defines the following terms:

3.2.1	Accomodation-vergence conflict: Accomodation (eyes focussing on an object) and convergence (eyes pointing toward the object) are normally linked. Accomodation-vergence conflict is a conflict between accommodation (eyes focusing on the screen) and the convergence (eyes converging to a point in front of or behind the screen). Current 3D display technologies may induce accommodation-vergence conflict.

3.2.2	Binocular disparity: The difference between corresponding points seen by the left and right eyes. This can be the strongest depth cue for close objects.

3.2.3	Binocular depth cues: Binocular depth cues stem from binocular disparity and the state of the oculomotor system.

3.2.4	Cardboard effect: The cardboard effect occurs when the imaging and display conditions reduces the reproduction magnification ratio of depth directions and distorts the perception of objects with visually imperceptible thickness. The 3-D positions of stereoscopic objects are perceived stereoscopically but they appear unnaturally thin.

3.2.5	Depth cues: Visual indicators of the relative distances between the observer and viewed objects. There are binocular and monocular depth cues.

3.2.6	Depth distortion: Depth distortion is the discrepancy between the displayed depth reconstruction and real world. The cardboard effect is one example of a depth distortion.

3.2.7	Depth motion: Objects moving in depth (e.g., toward the viewer) .

3.2.8	Depth resolution: spatial resolution in depth direction. Coarse resolution in depth direction may reduce picture quality in 3D television.

3.2.9	Frame effect: 3D pictures appear highly unnatural when objects positioned in front of the screen approach the screen frame. This unnatural effect is called “the frame effect”. The effect is generally reduced with a larger screen, because observers are less conscious of the existence of the frame when the screen is larger.

3.2.10	Medical signs:	 Medical signs are physiological reactions that are measured and interpreted within a controlled procedure.

3.2.11	Medical symptoms: Medical symptoms are expressed by the observer and constitute an indication of his or her perceived mental or physical state.

3.2.12	Planar motion: Motion with constant depth (i.e., within a plane perpendicular to the observer).

3.2.13	Puppet theater effect: This is an example of size distortion. The reproduction magnification ratio of an object at the shooting distance (the perceived size) varies with the imaging and display conditions. The resulting distortion in size may make an object be perceived as unnaturally small.

3.2.14	Size distortion: Distortions in the 3D geometry may occur due to inconsistencies between the capturing situation (notably the camera settings) and the reproduction (notably the display settings). The puppet theater effect is an example.

3.2.15	Monocular depth cues: Monocular depth cues can be perceived from a single eye’s view. They include occlusion (objects hidden behind other objects), relative sizes of known objects, vanishing point perception, blur from the focus, motion parallax, light, shade, texture gradient, aerial perspective, height in the visual field, kinetic depth, and others.

3.2.16	Visual discomfort: Visual discomfort is a negative sensation that is subjective reported. Visual discomfort may be triggered by the perception of 3D presentations. When present, visual discomfort is usually a transient state that disappears quickly after the person stops watching the problematic stimuli. The amount and duration of visual discomfort is highly individual. Visual discomfort may have other causes, such as visual flicker.

3.2.17	Visual fatigue: Visual fatigue is generally caused by the repetition of excessive visual effort and can build up as these efforts are repeated. It disappears after sufficient rest. Visual fatigue is a medical state that may be diagnosed by the presence of objective indications (medical signs) and subjective indications (medical symptoms). Visual fatigue can only be diagnosed by a medical doctor.

3.2.18	Window violation:	Window violation occurs when an object that is in front of the display overlaps the border of the screen. The 3D screen is often be perceived as a window, and in the real world objects can only be cropped when they lie behind the window. However, objects with crossed disparity are also cropped. When this occurs, the part of the object within the screen appears to be in front of the screen, while the cropping conflicts with this perception, by implying that the object should be at the depth of the screen or behind the screen.

# 4	Abbreviations and acronyms

This Recommendation uses the following abbreviations and acronyms:

ABV	Abnormal Binocular Vision

# 5	Conventions

“3D” in this Recommendation refers to a technology that projects dedicated views for each eye. The ultimate goal is these views depict the same situation as would be seen in reality (e.g., horizontally shifted). The technology as a whole can include more than two views, as per a multi-view autostereoscopic display. This can be noted as S3D for stereoscopic TV, or 3DMV for multiview.

# 6	Technological Issues for 3D Displaying

This clause describes background information required to understand technological issues for displaying 3D content, including constraints of camera capture, transmission, display, and the human visual system.

6.1	Accomodation-vergence conflict

Accomodation (eyes focussing on an object) and convergence (eyes pointing toward the object) are normally linked. Current 3D display technologies cause a conflict because accommodation and convergence do not follow the usual pattern. With 3D displays, the eyes focus on the screen but the eyes converge to a point in front of or behind the screen. This is the accommodation-vergence conflict.

The accommodation-vergence conflict has a static component (as described above) and also has a temporal component due to a link within the vision system. The accommodation control system and vergence ocular motor system are linked. Changes in accommodation automatically induce changes in vergence, and vice versa. This is the temporal component of the accommodation-vergence conflict. This is in conflict with current 3D display technology, because the accommodation always stays on the screen while the vergence changes according to the virtual object’s position (binocular disparity).

More research is needed, because [b-Shiomi] indicates that there is no accommodation-vergence conflict.

6.2	3D geometric distortions

[Editor’s note: insert text that describes this situation (Pierre)]

[b-Woods]

6.3	Comfortable viewing zone

[Editor’s note: the following clause needs to be written. (Jing)]

How to compute Depth of Field (DoF) is an area for further study. Subjective tests show the “comfort zone” is delimited by the Depth of Field (DoF) of the human eye. For typical 3DTV viewing conditions, DoF=±0.2 diopters is used as a common threshold. To reduce bias due to the presence or feeling of visual discomfort on 3D source test material, it would be interesting to calculate the depth range of each scene in diopter unit to know whether the scene is in accordance with the comfort zone requirement. The depth range around the screen plane can be calculated in diopter unit knowing the maximum crossed and uncrossed horizontal disparities and the viewing conditions.

# 7	Binocular Disparity Relationship in Capturing, Storing and Rendering

This clause explains the link between the camera positions while capturing, the resulting disparity in the captured content, and the perceived angular disparity at the viewer.

7.1	Conversion equations

The following equations are taken from [b-Chen].

Viewing distance:

d: Viewing distance

px: pixel width

Maximum uncrossed disparities: (eyes should not diverge)

e: inter-pupillary distance

Foreground distance of comfortable viewing zone

Zf: largest distance between the farthest object in front of the display and the display

Zb: largest distance between the farthest object in the background of the scene and the screen

Depth rendering abilities in pixel:

Df: maximum crossed disparity in pixel

Db: maximum uncrossed disparity in pixel

7.2	Conversion of pixel disparities to retinal disparities

[Editor’s note: insert text that describes these equations (Pierre)]

The following equations are taken from [b-Cormack].

r: retinal disparity

In the special case of the midsaggital plane:

7.3	Typical constraints for displays

[Editor’s note: insert text that describes these tables (Pierre)]

|  | SD |
| --- | --- |
| Resolution | 720x576 | 720x480 |
| Display diagonal (inch) | 24 | 32 | 24 | 32 |
| Display height (m) | 0.366 | 0.488 | 0.366 | 0.488 |
| Pixel width (mm) | 0.635 | 0.847 | 0.762 | 1.016 |
| Viewing distance (m) | 2.183 | 2.911 | 2.620 | 3.493 |
| Viewing distance (times H) | 5.968 | 5.968 | 7.162 | 7.162 |
| Maximum uncross disparity (pixel) | 102 | 77 | 85 | 64 |
| Foreground dist. confortable viewing zone (m) | 0.663 | 1.071 | 0.901 | 1.436 |
| Background dist. confortable viewing zone (m) | 1.692 | 4.055 | 2.883 | 8.094 |
| Number of pixel in the conforatble zone (foreground) | 44.7 | 44.7 | 44.7 | 44.7 |
| Number of pixel in the conforatble zone (Background) | 44.7 | 44.7 | 44.7 | 44.7 |

|  | HD |
| --- | --- |
| Resolution | 1920x1080 | 1920x540 |
| Display diagonal (inch) | 40 | 46 | 55 | 40 | 46 | 55 |
| Display height (m) | 0.498 | 0.573 | 0.685 | 0.275 | 0.316 | 0.378 |
| Pixel width (mm) | 0.461 | 0.530 | 0.634 | 0.509 | 0.586 | 0.700 |
| Viewing distance (m) | 1.586 | 1.823 | 2.180 | 1.751 | 2.014 | 2.408 |
| Viewing distance (times H) | 3.183 | 3.183 | 3.183 | 6.366 | 6.366 | 6.366 |
| Maximum uncross disparity (pixel) | 141 | 123 | 102 | 128 | 111 | 93 |
| Foreground dist. confortable viewing zone (m) | 0.382 | 0.487 | 0.662 | 0.454 | 0.578 | 0.783 |
| Background dist. confortable viewing zone (m) | 0.736 | 1.047 | 1.685 | 0.944 | 1.358 | 2.237 |
| Number of pixel in the conforatble zone (foreground) | 44.7 | 44.7 | 44.7 | 44.7 | 44.7 | 44.7 |
| Number of pixel in the conforatble zone (Background) | 44.7 | 44.7 | 44.7 | 44.7 | 44.7 | 44.7 |

|  | UHD |
| --- | --- |
| Resolution | 3840x2160 |
| Display diagonal (inch) | 40 | 46 | 55 |
| Display height (m) | 0.498 | 0.573 | 0.685 |
| Pixel width (mm) | 0.231 | 0.265 | 0.317 |
| Viewing distance (m) | 0.793 | 0.912 | 1.090 |
| Viewing distance (times H) | 1.592 | 1.592 | 1.592 |
| Maximum uncross disparity (pixel) | 282 | 245 | 205 |
| Foreground dist. confortable viewing zone (m) | 0.108 | 0.141 | 0.195 |
| Background dist. confortable viewing zone (m) | 0.149 | 0.203 | 0.304 |
| Number of pixel in the conforatble zone (foreground) | 44.7 | 44.7 | 44.7 |
| Number of pixel in the conforatble zone (Background) | 44.7 | 44.7 | 44.7 |

# 8	3D Video Content Guidelines

8.1	Introduction

The goal of 3D video is to enhance the perception of reality by altering depth cues, in particular by introducing binocular depth cues.

The overall sensation of reality a viewer sees depends technical factors that impact perceptual dimensions. The technical factors include resolution and color-fidelity. The perceptual dimensions include sharpness and depth cues.

This affects the potential for the sensation of reality, but the actual sensation of reality achieved depends also on the combination of the technical factors and the scene content itself. For example, if all of the objects in a wide angle shot are far away from the viewpoint, then the scene will generally not benefit from binocular depth cues, because those are not used by the viewer in this situation.

8.2	Disparity constraints

[Editor’s note: this section needs to be improved, notably with diagram showing relationship between content disparity and display disparity. (Jing, Pierre & Marcus)]

Excessive disparity/parallax causes visual discomfort possibly, because it worsens the conflict between accommodation and vergence. Therefore, it has been suggested that to minimize the accommodation-vergence conflict, the disparities in the stereoscopic image should be small enough so that the perceived depths of objects fall within a “comfort zone”.

The stereoscopic test content should be normally comfortable to watch. The visual comfort of stereoscopic images depends critically upon the disparity contained in the image. The visual comfort of stereoscopic images depends also upon the subject’s inter-pupilary distance and the viewing distance.

The following safety guidelines are recommended for filming, production, and selection of stereoscopic 3D video content.

- Fast spatial and temporal changes of disparity in stereoscopic 3D content should be avoided. The fast change of binocular disparity may induce visual discomfort accompanied by symptoms such as focusing difficulty and eye strain.

- To prevent visual discomfort, excessive disparity of stereoscopic 3D content should be avoided. Excessive binocular disparity may induce visual discomfort accompanied by symptoms such as focusing difficulty and eye strain.

- Image content with rotating or lateral shaking may induce the sensation of self-motion (visually induced self-motion sensation).

- 8.3	View asymetries

- [Editor’s note: this section needs information about calibration errors between views. (Marcus & Jing) Reference table 1 of 3D-sam. This table lists the visibility thresholds. Research is required to determine discomfort thresholds, but the technical factors are identical.]

- Viewers may not feel comfortable viewing left and right images that have size, verticality, inclination, and brightness differences. Cross-talk between the left and right images may also have an impact on viewing comfort.

These safety guidelines may be ignored for brief periods of time, for creative purposes.

Thresholds for disparity should be expressed in angular degrees of the viewing angle.

[Editor’s note: read the following paragraph. See what if anything should be moved to clause 6.1 on accommodation-vergence; delete the rest. (Marcus)]

All 3DTV systems displayed on a screen in a single plane (such as a television screen) have limitations for a number of reasons. One of them is the potential conflict between convergence (the object that they eyes point themselves towards) and accommodation (the point on which the lens of the eye focuses) which the two signals gives rise to. The human eye focuses on an object according to the distance to that object. At the same time, we also control the convergence point (gaze point) on the object. Therefore, there is no inconsistency between accommodation and convergence in our everyday life. However when viewing 3D images, the focus point (accommodation) must always be fixed on the screen, independent of the convergence point which is derived from the disparity of the signals. Otherwise, the observer cannot focus clearly. Thus, an inconsistency between accommodation and convergence is introduced in 3D systems Optimizing 3D systems is the process of minimizing the effects of the limitations.

Visual fatigue caused by viewing stereoscopic motion images is a particular safety concern. Viewers’ repeated adaptation to the discrepancy between eye convergence and accommodation causes a decline of their visual functions and results in visual fatigue.

8.4	Scene cuts

[Editor’s note: read for needed changes. (Jing & Marcus)]

Attention should be paid to the distribution of parallaxes in the stereoscopic images. From the correlations between psychological factors and the parallax distribution, we can grasp the essential characteristics of stereoscopic images, e.g., the sense of presence they convey and their ease of viewing. The parallax distribution of stereoscopic images is discontinuous during scene-change frames, where the scene depth and perceived convergence distance change. We need to evaluate how these changes affect the visual discomfort experienced during viewing of stereoscopic images.

8.5	Excessive disparity/parallax

[Editor’s note: the following base text needs to be re-written. (Marcus)]

Excessive disparity/parallax causes visual discomfort. Possible causes include the accommodation-vergence conflict and fusion limit.

Therefore, it has been suggested that to minimize the accommodation-vergence conflict, the disparities in the stereoscopic image should be small enough so that the perceived depths of objects fall within a “comfort zone”.

9	3D Viewer Guidelines

9.1	The Influence of Stereopsis and Abnormal Binocular Vision (ABV)

Subjects with abnormal binocular vision such as strabismus, amblyopia, and anisometropia have decreased 3D perception (e.g., more difficulty perceiving 3D).

Among people with ABV, subjects that have a normal degree of stereopsis are more sucsceptible to 3D fatigue than subjects that have poor stereopsis. This includes 3D fatigue symptoms such as dizziness, headaches, eye fatigue, and pain. A normal degree of stereopsis is for example good stereopsis as measured with a Titmus stereofly test.

If a person cannot perceive 3D, or feels severe 3D fatigue while watching 3D content, he or she should consult ophthalmologic specialists for evaluation of abnormal binocular vision. However, badly produced 3D content will cause 3D fatigue in everyone.

Visual functions vary greatly from person to person, so it is essential to understand that there are individual differences before subjective assessment begins. For instance, there are limits to the binocular parallax of left and right images which a person can fuse into one image; when the parallax exceeds these limits, a double image is perceived. In this situation, depth perception collapses and viewing becomes extremely uncomfortable. For this reason, it is necessary to know the range of binocular parallax over which two images can be fused into one. However, individual differences are vast and will necessitate a study of the stereopsis function of many people.

9.2	Warnings for Subjects

Viewers of 3DTV should be made aware of the following warnings:

- Avoid viewing 3D TV if body functions start to deteriorate or if excessive stress is perceived.

- Stop viewing 3D TV if double vision is experienced.

- Image content with rotating or lateral shaking may induce the sensation of self-motion (visually induced self-motion sensation). Stop watching 3D TV temporarily if you feel uncomfortable with this sensation.

- Individuals with a shorter interpupilary distance may feel more visual discomfort with 3D TV than others (e.g., children).

- Individuals who experience motion sickness in automobiles or amusement park rides may experience more visual discomfort during 3D TV viewing.

9.3	Symptoms of 3D visual fatigue

[Editor’s note: this text needs to be examined for changes. (Jing & Marcus)]

[Editor’s note: this text moved here from later in the document. Only changes are marked, not the move.]

The following symptoms may indicate 3D visual fatigue. More information can be found in [b-Kuze].

- Difficulty in tracking the motion on TV

- Eye strain: blurred vision, bleary, dry eyed, gritty, eye ache, sting, eyes heavy, hazy, warm eyes, flickering and watery eyes.

- Focusing difficulty: double vision, near vision difficulty, far vision difficulty, and trouble fusing stereoscopic images.

- General fatigue symptoms: feeling heavy in the head, difficulty in concentration, dizziness, stiff shoulder and stiff neck.

- Headache: pain in the temple and pain in the middle of the forehead.

- Nausea: vomiting and vertigo.

- Transient visual dimness after watching TV

If a person feels any of these symptoms, it may be an indication of visual fatigue. He or she should stop 3D TV viewing until the side effect disappears.

If a person repeatedly experiences 3D fatigue symptoms, he or she should consult ophthalmologic specialists for evaluation of abnormal binocular vision. The 3D TV hardware operation should also be examined for problems.

10	3D Viewing Environment and Playback Guidelines

[Editor’s note: Carefully review this section (e.g., the relationship between accommodation, screen size, etc.; constraints), (Marcus, Pierre)]

Illumination, sound, viewing height, and TV brightness and focus should be adjusted to comfortable levels when watching 3D TV.

If an image appears as a double image or if it is hard to perceive a 3D image, stop using the system and check for errors in the display settings. If you still experience stereopsis problems with no apparent hardware problems, then you should temporarily stop viewing 3D TV.

Some viewers might not notice whether left and right images are reversed. The reversed vision of left and right images can cause visual fatigue and discomfort. Reversed left and right images can be caused by many problems (e.g., editing errors, hardware problems, camera setup, viewing angle).

10.1 Relationship Between Viewer and 3D Monitor

The viewer should be seated as advised by the 3D television manual, at a comfortable distance from the monitor. For television monitors, a minimum of 3H (three times picture height) is advised. For computer monitors, a minimum of 1.5H is advised.

Optimal 3D viewing means the viewer should be seated upright, in front of the screen (i.e., minimal head tilt). The viewing direction should be normal (e.g., head facing perpendicular) to the screen.  The horizontal viewing angle from the screen should be minimum (e.g., face the screen directly instead of at an angle).

Figure 1. Diagram demonstrates viewing direction and viewing angle. It is generally said that the minimum value for depth of field of the human eye is ±0.3 D, where diopter (D) is the reciprocal value of distance (m). This means that we can perceive the image without defocusing when the object is located within ±0.3 D. When viewing 3D television, the accommodation point is fixed on the screen, and therefore 3D pictures should preferably be displayed within this range. Since ordinary television programs include images at infinite distance, the desirable range of depth to be displayed with 3D systems is considered to be within 0 to 0.6 D. Therefore, 0.3 D, i.e. 3.3 m, is considered to be the optimum viewing distance.

Camera parameters (camera separation, camera convergence angle, focal length of lens), resolution of the system and the frame effect should be taken into account in determining viewing conditions (screen size). In the case of HDTV when watching at the standard viewing distance of 3 H (H denotes picture height), the viewing distance of 3.3 m corresponds to a 90-inch screen. In the case of standard definition television (SDTV) when watching at the standard viewing distance of 6 H, this distance corresponds to a 36 inch screen. A subjective assessment of the relationship between screen size and depth perception was carried out with 3D HDTV system, and the results showed that the most natural depth perception was obtained with a screen size of 120 inches, which corresponds to viewing distance of 2.2 H.

The effective viewing angle should allow 20% angular rotation of head movement in the horizontal plane.

10.2 Viewing Time and Visual Fatigue

Acceptable viewing time for 3D content varies depending upon the content. A short time resting is recommended for every 1 or 2 hours, or when the eyes feel tired.

11	Assessment methods for symptoms of visual fatigue

11.1 Questionnaire to assess symptoms of visual fatigue

[Editor’s note: insert questionnaire, biographical reference, etc. (Kjell)]

This questionnaire is taken from [b-Kennedy].

For an example of this technique, see [b- Brunnström].

11.2 Pair comparison (PC) subjective test to visual discomfort

[Editor’s note: describe method, insert biographical reference to Jing’s paper, etc. (Jing)]

Appendix I

Open Questions

(This appendix does not form an integral part of this Recommendation)

More research is needed on the accommodation-vergence conflict. [b-Shiomi] indicates that there is no accommodation-vergence conflict.

Bibliography

[b- Brunnström]	Brunnström, K., Wang, K., and Andrén, B., "Simulator sickness analysis of 3D video viewing on passive 3DTV", Stereoscopic Displays and Applications XXIV, Vol: 8648, A. J. Woods, N. S. Holliman, and G. E. Favolora Eds., paper 1 (2013)

[b-Chen]	Chen, W.; Fournier, J.; Barkowsky, M. & Callet, P. L. (2010), “New Requirements of Subjective video quality assessment methodologies for 3DTV,” Video Processing and Quality Metrics 2010 (VPQM), Scottsdale, USA.

[b-Cormack]	Robert Cormack, “The computation of retinal disparity,” Perception and Psychophysics, vol. 37, no. 2, pp. 176–178, 1985

[b-Kennedy]	Kennedy, R. S., Lane, N. E., Berbaum, K. S., and Lilienthal, M. G., "Simulator Sickness Questionnaire: An Enhanced Method of Quantifying Simulator Sickness", The International Journal of Aviation Psychology 3 (3), 203-220 (1993)

[b-Shiomi]	Shiomi, T., Hori, H., Uemoto, K., Miyao, M., Takada, H., Hasegawa, S., Omori, M., Watanabe, T., and Ishio, H., "Comparison of Simultaneous Measurement of Lens Accommodation and Convergence in Natural Vision and 3D Vision", SID Symposium Digest of Technical Papers, Vol: 43, 1178-1181 (2012)

[b-Kuze]	Kuze, J., & Ukai, K. (2008). “Subjective evaluation of visual fatigue caused by motion images,” Displays, 29(2), 159–166.

[b-Woods]	Andrew Woods, Tom Docherty, and Rolf Koch, “Image distortions in stereoscopic video systems,” Proceedings of the SPIE, Stereoscopic Displays and Applications IV, 1993, vol. 1915, pp. 36–48.

______________________

# Comments

“Assessment methods” is not appropriate, given the contents of this document. The modified title better matches the current contents of this draft Rec.

Review scope

May need to broaden scope

- Reverse typical situation, because consumer situation is more difficult than studio

Note that the deleted limitations are all mentioned in this document.

Move this sentence to the appropriate section later in the paper.

Note: this text was moved from later in the document. Only edits are marked as changes (not the move).

# Text boxes

Television

Viewer

α

α marks the viewing angle

The viewer has the preferred viewing direction and viewing angle: head facing perpendicular to the screen, and zero degree viewing angle.

Viewer

Television